## Slide 1: GRWG VIS/NIR Sub-Group Briefing Report
2016 GSICS Joint Meeting on Research and Data Working Groups
Tsukuba, Japan
29 February to 4 March 2016
GSICS VIS/NIR Sub-Group Members presented by David Doelling

## Slide 2: VIS/NIR Reference Instrument
We are in the process of selecting a reference instrument
    Radiometric noise or flat fielding, scan angle dependency, calibration stability, polarization knowledge, spectral resolution or SRF knowledge
  Jack Xiong and Aisheng Wu to review the MODIS and VIIRS calibration accuracies to select reference instrument on Thursday
  Aqua-MODIS band 1 Collection 6
  NPP-VIIRS I1 or M5, IDPS or LandPEATE
  We began using MODIS, since it was established in retrieval community as being well calibrated and VIIRS was just launched
  The momentum is with VIIRS, since its calibration has been verified, has many channels very similar to the GEO 3rd generation, and has a longer projected life span than MODIS
Future will need to transfer the calibration between reference successive MODIS and VIIRS instruments
  Each MODIS and VIIRS channel is independently calibrated
  Need to establish traceable chain of calibration transfers between successive reference instruments ultimately tied to CLARREO or TRUTHS

## Slide 3: Spectral Band Adjustment Factors (SBAF)
There are 3 possible VIS/NIR hyperspectral datasets that can be used for SBAF
  SCIAMACHY 30x240 km FOV, mostly complete visible spectra (except > 1.6µm), high resolution spectra
  GOME-2 40x80 km FOV, limited visible spectra, high resolution spectra
  SCIAMACHY 30m FOV, complete spectral range, low spectral resolution
NASA-Langley SBAF web site established
  The SBAF uncertainty can now be reduced by stratifying by angle, PW and other factors
Future SBAF
  Obtain more hyper-spectral datasets and further collocations of atmospheric, cloud, aerosol conditions

## Slide 4: VIS/NIR Combining Methods
The VIS/NIR product to contain the individual calibration approach coefficients
Combine the multiple calibration approaches to provide users calibration coefficients with the least uncertainty
Combining methods proposed
  Bertrand, evaluate consistency calibration results among methods and optimize weighting for final coefficients with respect to the uncertainty of the absolute calibration transfer of the reference instrument, and the noise of the method with respect to the degradation
  Fangfang, iterative recursive filtering technique, this takes the more stable part of all methods to estimate the final instrument degradation
This year goal to define combining of methods for the DCC and lunar calibration methods among GPRCs
  In the future more calibration methods will be developed and will be added to the VIS/NIR product

## Slide 5: Lunar Calibration Status Sebastien and Tom
GIRO algorithm
  Initiated at the GSICS lunar calibration workshop at EUMETSAT, Dec 1-4 , 2014
  Have a follow on GSICS lunar workshop before May 2016
  GIRO is the GSICS implementation of the USGS ROLO model provides uniform implementation across GEO calibration centers
GLOD dataset
  GLOD is the GISCS Lunar Observation dataset designed to improve the ROLO model
  EUMETSAT, CNES, NOAA, JMA, KMA, NASA have provided many lunar images
  Recently ISRO, JMA and KMA presented updated results using GIRO.
  Very large amount of Himawari-8 acquisition

## Slide 6: Lunar Calibration Next Steps
Uncertainty Estimation
  Accurate estimation of the over-sampling factor
  Benchmarks to access improvements of GIRO
Accounting for spectral differences between instruments
  using hyper-spectral instruments with Moon observations (GOME-2, Hyperion, SCIAMACHY
Establishing an absolute scale for lunar calibration
  using Aqua MODIS / NPP VIIRS in order to scale the ROLO model calibration when comparing with other methods
  Work on ROLO model version 2

## Slide 7: DCC calibration Status
Started in 2014
  NASA Langley provided all GPRCs verification data to validate the proper implementation according to ATBD submitted in 2011
The DCC method has been implemented by all GPRCs by 2015 and will report on their status and issues of the implementation
The DCC methodology provides excellent estimate of the relative degradation of the monitored instrument, however the GEO domain specific DCC methodology noise can be reduced by adjusting DCC methodology components as needed
1) DCC BRDF
  KMA has evaluated BJ Sohn model
  CNES has defined the more Lambertian part of the BRDF
2) DCC deseasonalization
  NOAA, EUMETSAT, CMA have developed methods
3) DCC statistic (mean, mode, median) and identification ( to provide sufficient sampling)

## Slide 8: DCC calibration to Demonstration Product is this years goal
DCC ATBD submitted by EUMETSAT
Began product acceptance procedure
This years goal is to write a combined GPRC GSICS DCC calibration method paper
  Paper needs to estimate the uncertainty of the DCC calibration method with regards to determine the stability of the monitored instrument and the absolute calibration transfer of the reference instrument

## Slide 9: GSICS products and plotting
VIS/NIR Product file format is nearly finalized
  File naming convention following WMO format
  File parameters and coefficients structures finalized, to include variables that describe the calibration method adjustments for each GEO in order to reproduce the calibration coefficients faithfully
  One VIS/NIR calibration file containing all calibration from multiple methods and channels
  Frequency Update being resolved
    Dependent on calibration method sampling: DCC can be updated daily and Lunar monthly
    Dependent on the magnitude of the monitored instrument on orbit degradation
Bias monitoring plotting being developed similar to the IR bias monitoring
  JMA has presented protoype
  Do we plot the relative degradation, the correction?

## Slide 10: Other VIS/NIR activities
Recommend a solar spectra for the GSICS community in collaboration with CEOS IVOS
  Nigel Fox would like to engage the GSICS community with this effort
  The solar spectra could depend on the wavelength and application
  GSICS has provided a common reference web site to obtain the operational VIS/NIR spectral response function and instrument event logging
Apply VIS/NIR calibration strategies to other wavelengths
  DCC for wavelength <1 µm, test for >1 µm
  Lunar, reexamine lunar spectra from lunar database
  Inter-band calibration methodologies may play a role in the future to validate or provide calibration coefficients derived for one band applied to another for consistent retrieval results, which use multiple channels, such as ocean color and aerosols

## Slide 11: Develop new VIS/NIR calibration approaches
Having multiple calibration methods, which produce consistent calibration coefficients, validates all techniques
  An individual method maybe more suitalbe for the user application
  Methodology success is dependent on the monitored and reference instrument
Need to prepare for new 3rd generation GEO calibration methodologies
  GRPCs priorities are for current instrumentation
  Have onboard calibration, which as not the case with 2nd generation, and have very similar channel bandwidths as the reference instrument, making other methodologies more reliable than earth invariant targets
Will discuss the development of other calibration VIS/NIR methods, which can be applied consistently across sensors
  Methodologies that take advantage of the 3rd generation GEOs
  Is there a need to calibrate other instrument records other than GEOs?

## Slide 12: Backup Slides

## Slide 13: VIS/NIR absolute calibration reference
Currently no visible instrument can be used as an absolute calibration reference
  MODIS absolute calibration uncertainty is 1.6% during ground characterization
Hyper-spectral instrument is preferred to reduce SBAF errors
  No hyper-spectral instrument over the entire visible band
CLARREO or TRUTHS will give eventually provide an on-orbit SI traceable reference
Until then the VIS/NIR calibration reference must consist of overlapping sensor sensor records to transfer the calibration SI traceable reference back in time
  In order to reduce the uncertainty between overlapping sensor, the sensor characteristics should be very similar
  The 4 JPSS and NPP VIIRS instruments will provide overlapping coverage between 2012 and 2038 and are nearly exact replicas
In the future invariant targets such as the moon can provide an SI traceable reference
  This provides a direct calibration transfer without a reference instrument

## Slide 14: VIS/NIR calibration strategy
Calibrate sensors traceable to the reference instrument calibration
Use multiple calibration approaches to inter-calibrate the monitored and reference sensor
  GSICS approaches being developed: DCC, lunar
  This year to start developing new calibration approach: rayliegh scattering, desert, ray-matching
Combine the multiple calibration approaches to provide users calibration coefficients with the least uncertainty
  Method weighting is dependent on wavelength, and monitoring, absolute calibration uncertainty
  This year to start developing combining method technique
  All calibration approach calibration coefficients will be available on the product file, so that user may select approach optimized for the retrieval