## Slide 1: JMA Agency Report
Arata Okuyama, Masaya Takahashi,
Hidehiko Murata
Meteorological Satellite Center,
Japan Meteorological Agency

## Slide 2: Contents
Update of JMA GSICS members
Summary of JMA related action status
  GEOLEOIR GSICS product template was updated. [GDWG]
  Templates of landing page submitted to GDWG. [GDWG]
  NetCDF template for SRF data and list of existing SRF data sets [had been submitted]. [GDWG]
  The uncertainty analysis to support progress to Pre-Operational mode is ongoing. [GRWG]
  Calibration event database design is ongoing. [GRWG]
Himawari8/AHI data quality
2015 achievements / 2016 work plan
AHI GEO-LEO-IR to Pre-operational phase
...

## Slide 3
Member | GRWG | GDWG | GEO-LEO-IR | DCC | Moon | Vicarious method (RTM) | Ray matching | GEO-GEO
Masaya Takahashi (Mr.) | Y | Y | Y | Y | Y |  | Y | 
Arata Okuyama (Mr.) | Y |  |  | (Y) | (Y) | Y |  | 
Hidehiko Murata (Mr.) | Y |  |  |  |  |  |  | Y
JMA GSICS members
EP
Kotaro Bessho
GRWG
Arata Okuyama
Masaya Takahashi
Hidehiko Murata
GDWG
Masaya Takahashi
Point of operational contact: Arata
Co-chair Feb 2015~

## Slide 4
Action Ref | Description | Assigned to | Due Date | State
GRWG_14.8 | CMA and JMA to present their analysis on GEO-GEO IR products at the next meeting. | CMA/JMA | 1-May-15 | Reported in New Delhi (2015)
GRWG_14.23 | All GPRCs to provide satellite instrument specific links to calibration events to WMO-OSCAR. | Main.ALL, Main.GPRC | 1-May-15 | Reported in New Delhi (2015)
 | - Work in progress. Almost all agencies now nominated someone for the calibration tasks team, these nominees are providing Rob with the links. |  |  | 
GRWG_14.24 | All GPRC to seek consensus on common naming conventions for calibration events at the level of Main-Categories/Sub-Categories/Event Types. | Main.ALL, Main.GPRC | 1-May-15 | Open
 | - Only progress on this is that we have now a calibrations task team. Within the GDWG Rob would like to discuss the way forward on this, i.e., in cooperation work on a white paper defining common naming conventions |  |  | 
GRWG_14.25 | EUMETSAT/NOAA/NASA/JMA to define a calibration events database design, and if needed, discuss this in a future webex meeting. | Main.EUMETSAT, Main.NOAA, Main.NASA, Main.JMA | 1-May-15 | Open
 | - To be discussed at the 2015 GDWG meeting. This was our plan, but may be too ambitious. At least now. First issue is to agree on nomenclature, and report this is a white paper. Second issue is to adopt the common nomenclature within existing calibration events data bases. Third issue could be to work towards a common database design, and a centralized database, however, Rob foresees that this will take long and that it requires extra resources. |  |  | 
GRWG_14.27 | All GPRCs to review their GSICS websites to take into account of the new developments in GSICS as these websites will be reviewed in the next joint meeting. | Main.ALL, Main.GPRC | 1-May-15 | Open can be closed??
GRWG_14.29 | Masaya Takahashi to check for a document regarding minimum content for GPRC GSICS webpage. If this document does not exist, then he shall author one and upload it to the Wiki. | Masaya Takahashi | 1-May-15 | Reported in New Delhi (2015)
GRWG_14.35 | EUMETSAT/NOAA/NASA/JMA to perform analysis to evaluate the optimal temporal resolution for a DCC product. GPRCs are invited to report at the next web-meeting on the DCC method. | Main.EUMETSAT, Main.NOAA, Main.NASA, Main.JMA | 1-May-15 | DCC approach was discussed in Webex meeting in 4 Feb. 2016
GRWG_15.47 | JMA to investigate and provide a report on the uncertainty analysis to support progress to Pre-Operational mode. | MasayaTakahashi | 29-Feb-16 | Open
Status of actions assigned to JMA (GRWG)
Can be closed item

## Slide 5
Action Ref | Description | Assigned to | Due Date | State
GLCWS_14.5 | All participants to provide lunar irradiances from the missing instruments to the common lunar calibration data set. | AllGroups? | 1-Dec-15 | Moon data of MT2 and H8 was provided.
GLCWS_14.7 | GSICS Data Working Group to identify a suitable mechanism for sharing the lunar calibration dataset. | MasayaTakahashi | 1-Dec-15 | Discussed in New Delhi (2015)
GLCWS_14.10 | The GSICS Data Working Group is asked to develop a procedure for verifying users’ implementation of GIRO. | MasayaTakahashi | 1-Dec-15 | Discussed in New Delhi (2015)
Status of actions assigned to JMA (Lunar calibration WS )
GLCWS_14.5 : Lunar data already provided need to be revised. Updated version will be provided.
Can be closed item

## Slide 6
Status of actions assigned to JMA (GDWG)
Action Ref | Description | Assigned to | Due Date | State
GDWG_14.2 | GDWG to investigate methods to structure the order the global attributes within the netCDF file - e.g. between attributes related to the method and the application. | Main.Masaya | 1-May-15 | Discussed in Webex 5 June 2014
GDWG_14.3 | GDWG to investigate how to include algorithm type in filename. | Main.Masaya | 1-May-15 | Will be discussed in GDWG
GDWG_14.10 | All GPRCs to provide satellite instrument specific links to calibration events to WMO-OSCAR. (cf. GRWG_14.23) | Main.All | 1-May-15 | Reported in New Delhi (2015)
GDWG_14.11 | All GPRC to seek consensus on common naming conventions for calibration events at the level of Main-Categories/Sub-Categories/Event Types. (cf. GRWG_14.24) | Main.All | 1-May-15 | Open
GDWG_14.12 | EUMETSAT/NOAA/NASA/JMA to define a calibration events database design, and if needed, discuss this in a future web meeting. (cf. GRWG_14.25) | Main/EUM/NOAA /NASA/JMA | 1-May-15 | Open
Can be closed item

## Slide 7
Status of actions assigned to JMA (GDWG)
Action Ref | Description | Assigned to | Due Date | State
GDWG_2015.4c1 | The GRWG need to examine the aspects to be revalidated and confirm they have no major impact. (ref: changing the existing GEOLEOIR variables to combined versions).- | Main/EUM.JMA | 31-May-15 | Discussed by email
GDWG_2015.4c2 | Update the GEOLEOIR GSICS product template on the Wiki. | Main.JMA | 31-Jul-15 | Discussed in [gsics-dev]
GDWG_2015.4c3 | Update the Wiki to include the accurate timing information as an optional comment attribute of the validity period in their products. | Main.JMA | 31-Jul-15 | Open
GDWG_2015.4c4 | JMA to provide list of new GEOLEOIR global attributes to GDWG members and member should provide input within 1 week on the proposed updates | Main.JMA | 31-May-15 | Discussed in [gsics-dev]
GDWG_2015.4d | Identify if using the enhanced data model has impact to the usage of the new products. | Main/EUM.JMA | 31-Jul-15 | Will be discussed in GDWG
GDWG_2015.4l2 | EUMETSAT and JMA to provide templates of landing page to GDWG (or GSICS wiki). | Main/EUM.JMA | 30-Apr-15 | Closed
GDWG_2015.6a1 | JMA GRWG to provide the list of existing SRF data sets to be stored. GPRC responsible for these data sets shall provide them to GDWG co-chair as soon as possible. | Main.JMA | 31-Jul-15 | Will be closed soon
GDWG_2015.6a2 | JMA to provide the netCDF template to GDWG co-chair for these SRF files. | Main.JMA | 30-Apr-15 | Closed
GDWG_2015.6a5 | The GEOLEOVISNIR or LEOLEOVISNIR shall include an optional global attribute referencing the location of the associated SRF netCDF file. | Main/EUM.JMA | 1-Mar-16 | Will be discussed in GDWG
GDWG_2015.6b1 | GDWG co-chair to support GRWG to implement the recommendations for sharing work in a Data Managed way. | Main/EUM.JMA | 30-Apr-15 | Closed
GDWG_2015.6b3 | CMA, IMD, JMA and KMA to collaborate in the implementation of the netCDF GSICS product checker. | Main/CM/IMD/JMA.KMA | 31-Dec-15 | Open
GDWG_2015.6f | WMO and GPRCs to provide the GCC with examples of document management procedures including templates to support the creation of GSICS branding documentation templates. | Main.All | 31-Dec-15 | Open
GDWG_2015.9b2 | GDWG will come with a proposal on how to number the actions. The action tracking tool should include the actions coming from the web meetings. | Main/EUM.JMA | 31-May-15 | Open
GDWG_2015.9b3 | Alternatives to the current action tracking tool should be discussed at further stage (web meeting). | Main/EUM.JMA | 31-May-15 | Open

## Slide 8
Navigation error of Himawari Standard Data (L1B equivalent) is less than around 0.3 pixel (1 pixel = 2 km). It is estimated by landmark analysis.
AHI data quality (INR)
1 Jan., 2016 01:00 (UTC)
2 Jan., 2016
00:00 (UTC)
East-West direction [pix] North-South direction [pix] Magnitude [pix] Number of landmark points
1 pix
(~2km)
Referenced landmark
Direction and magnitude of error
Residual navigation error
10.4um band (2 km), every 10 minutes
1200

## Slide 9
Band [μm] | Average
B07 (3.9) | 0.096
B08 (6.2) | 0.132
B09 (6.9) | 0.216
B10 (7.3) | 0.229
B11 (8.6) | 0.280
B12 (9.6) | 0.178
B14 (11.2) | 0.116
B15 (12.4) | 0.111
B16 (13.3) | 0.015
Band [μm] | Average in the daytime
B01 (0.47) | 0.127
B02 (0.51) | 0.157
B03 (0.64) | 0.189
B04 (0.86) | 0.150
B05 (1.6) | 0.462
B06 (2.3) | 0.138
B01(0.47)
B02(0.51)
B03(0.64)
B07(3.9)
B08(6.2)
B15(12.4)
Band to band registration error is less than 0.1 – 0.2 pixels (1 pixel = 2 km).
The error is:
  estimated by correlation analysis between Band 13 (10.4 um) and each band.
  large in midnight in VIS-3.9um bands.
  stable in IR bands.
The registration process will be updated soon.
1 pixel = 2km (All band)
Averaged error magnitude from 2-4 January, 2016
AHI data quality (Band to band registration)

## Slide 10
Band 1 (0.47μm) Band 2 (0.51μm) Band 3 (0.64μm)
Band 4 (0.86μm) Band 5 (1.6μm) Band 6 (2.3μm)
Time series of DCC from ray-matched data, Ray-matching and RT simulation results
There is no significant bias in Band 1-4 (0.47-0.86 um)
+/- 5% bias in Band 5 and 6 (1.6 and 2.3 um).
AHI data quality (VIS-NIR calibration)
will be reported in [4m]

## Slide 11: Vicarious calibration for AHI
Clear sky ocean
  Ocean color needs to be considered in shorter wavelength band ( < 0.6um)
  Possibly also polarization
  It is dark for NIR bands
Land surface
  It can provide low uncertainty.
  Precise ground surface reflectivity is necessary, because AHI’s band width is narrower than the one of MTSAT-2.
  VIIRS BRDF product is awaited, because its bands are close to AHI’s.
Liquid water cloud
  Looks good.
DCC
  Kernel file is under development in JMA/MRI.
observation
observation
simulation
MODIS ocean color (NASA) is applied.
observation
observation
simulation
Land
Water cloud
MODIS
AHI
Grass
Slope 0.98
Slope 1.06
simulation
B06 (2.3um)
B06 (2.3um)
B01 (0.47um)
B01 (0.47um)
Clear sky ocean
Clear sky ocean

## Slide 12
The Tb bias is less than 0.2 K in all band at standard radiances.
Band 7
Band 8
Band 9
Band 10
Band 11
Band 12
Band 13
Band 14
Band 15
Band 16
AHI data quality (IR calibration)
will be reported in [3k]

## Slide 13: AHI data quality (Diurnal variation in IR)
There is no significant diurnal variation seen in MTSAT-2
  The biases at the standard radiance are shown.
  Data period is December 2015.
  Reference sensors are:
Metop-A/IASI
Metop-B/IASI
Aqua/AIRS
S-NPP/CrIS
MTSAT-2/Imager
Himawari-8/AHI
will be reported in [3k]

## Slide 14
AHI calibration and navigation monitoring is available on JMA/MSC Web page.
http://www.jma-net.go.jp/msc/en/index.html
Monitoring web page

## Slide 15: Improvements of the Ground Segment
Swath boundary
Band 4 (low-radiance emphasized Image) @ clear sky sea surface
Himawari Standard Data will be update from 05:00UTC, 9 March 2016 05:00UTC
Implementation of coherent noise reduction processing
  Band 7 (3.9 um): already applied
  Band 1, 2, 4, 5, 6, 10, 11, 12, 13, 14 and 15: will be applied
Improvement of band-to-band co-registration algorithm for IR bands
Implementation of granular noise reduction in resampling processing and Bug fix
Before
After
Coherent noises
Notes: HSD is L1B equivalent data.

## Slide 16: Application of GEO-GEO AHI-AHI comparison as a monitoring support tool
To support operational quality check
  e.g. After operational configuration change
  e.g. Stray-light in eclipse season midnight
For quick and qualitative check
  No collocation, no RT computation
  GSICS approach is necessary for quantitative analysis.
Sometime false alarm appears.
  Threshold tuning is based on trial and error.
  For internal use.

## Slide 17
2015 achievement
  Feasibility study for DCC inter-calibration for all VIS/NIR bands
  AHI lunar calibration using GIRO (ongoing)
  AHI-CrIS inter-calibration
  (AHI calibration monitoring environment)
2016 work plan
  Submission of AHI GEO-LEO-IR product to Pre-operation phase
  Prime Correction
  Extend inter-comparison of MTSAT-2 VIS approaches (Lunar, DCC, RTM) to entire MTSAT-2 operation period
  Collaboration with GDWG members (e.g. generating GSICS netCDF checker, use of gitHub for sharing codes)
  SCOPE-CM calibration-related activities
  Re-processing of surface albedo retrieval (LAGS)
  Inter-calibration of GMS WV/IR channels using HIRS (IOGEO)
2015 achievements / 2016 work plan