## Slide 1: USGS Report to GSICS March 01, 2016
Tom Stone, USGS Flagstaff, (on-site)
Greg Stensaas and Ron Morfitt, USGS EROS, (telecon)

## Slide 2: Overview
Landsat Mission Status
  Observatory statuses
  Instrument performance and anomalies
  Lunar calibration
Additional Activities Relating to Cal/Val
  Non-Landsat imagery assessments
  Land Product Characterization System (LPCS)
  Requirements Capabilities and Analysis for Earth Observations (RCA-EO)
  National Earth Observation Assessment (EOA)
Future Collaborative Efforts

## Slide 3: Landsat 7 Spacecraft Status
Attitude Control System
X-band System
S-band System
Performance nominal
Enhanced Thematic Mapper +
Batteries
Performance nominal
Solid State Recorder
Reaction Control System
1/07/04 Fuel line #4 thermostat #1a failure
2/24/05 Fuel line #4 thermostat failure; Primary
heater circuit disabled
4/25/13 Fuel line #2 thermostat failure; Redundant
heater circuit disabled
Solar Array
5/14/2002 Circuit #14 Failure
5/16/2005 Circuit # 6 Failure
8/13/2008 Circuit #14 partial recovery
14 circuits remain operating
no impact to ops
11/15/1999 SSR PWA #23 Loss
02/11/2001 SSR PWA #12 Loss
12/07/2005 SSR PWA #02 Loss
08/02/2006 SSR PWA #13 Loss
03/28/2008 SSR PWA #22 Loss
09/03/2008 SSR PWA #23 Recovered
10/12/2013 SSR PWA #11 Loss
Each PWA is 4% loss of launch capacity
Boards are likely recoverable
Performance nominal
•05/05/2004 Gyro 3 Shut Off
•1-gyro control system in development
≈ 16 years of on-orbit operations
•5/31/2003 SLC Failure
•4/01/2007 Bumper mode
Remote Tlm Cmd (RTC) Box
•09/27/2014 RTC A Failover
Power Subsystem
Power Control Unit
10/18/2014 BVR failover

## Slide 4: Landsat 8 Spacecraft Status
Operational Land Imager
Thermal Infrared Sensor
10/1/2014 - Side-A SSM Encoder
Propulsion Subsystem
Thermal Control System
Electrical Power System
Attitude Control System
RF Communications
Command & Data Handling System
X-band System
S-band System
Batteries
Solid State Recorder
Solar array
≈ 3 years of on-orbit operations

## Slide 5: Active Landsat International Ground Stations
10 Active L7 Stations 17 Active L8 Stations
L7 pLGN

## Slide 6: Landsat-7 Radiometric Performance
Lifetime TOA reflectance based on PICS stable with seasonal variations
Coherent noise component continues to increase
Continuing quarterly ETM+ absolute gain updates
Planning to propagate L8 OLI reflectance based calibration to L1-7

## Slide 7: Landsat-8 Radiometric Performance
SNR continues to exceed requirements
OLI radiometric stability, worst case band, about 1% over 2 years; most bands ~0.3%
Continuing quarterly relative gain updates

## Slide 8: L8 TIRS Out-of-field Stray Light

## Slide 9: TIRS Stray Light Correction Results (Preliminary)
Original
GOES Correction
TIRS Correction
Model of stray light determined by optical model
  Effectively a point spread function for each detector
  Verified by comparing PSF to special lunar scans
Method 1:
  Convolves PSF with GOES imagery to estimate stray light per pixel in TIRS image
  Subtract stray light estimate from TIRS image
Method 2:
  Convolves PSF with TIRS imagery, scene before and after
  Where no TIRS imagery, use nearest TIRS pixels
  Subtract stray light estimate from TIRS image

## Slide 10: TIRS Scene Select Mirror Anomaly
SSM encoder current began increasing last Summer/Fall
Reached yellow limit December 19, 2014
  Encoder powered down
  Product generation system couldn’t handle no encoder
  TIRS imagery zeroed through early March
    Software updated April 23, 2015
TIRS electronics switched to side-B March 4, 2015
  Radiometric and Geometric quality attained once more
Typical OLI-TIRS alignment
OLI-TIRS alignment without encoder

## Slide 11: L8 OLI Lunar Calibration
Lunar trending follows other cal methods
Absolute offsets are relatively large — cause is being studied
lunar
Notes: Landsat 8 is the first Landsat to look at the Moon

## Slide 12: USGS Imagery Assessments 2013-2015
Assessments:
  ResourceSat-2 AWiFS-2, VNREDSat-1, KOMPSAT-3, WorldDEM™, PROBA-V, Planet Labs (Doves-3 & 4, Flock-1a, Flock 1-c), SkyBox-1 & 2, SPOT-7
Future assessments:
  More Planet Labs satellites, CBERS-4, KompSat-3A, DMC-3 constellation
  Higher-Level Product Quality Monitoring
Snapshot of results:
  Spatial resolution is not just GSD
    More Pixels do not always mean More Resolution
  Aperture makes all the difference!
    Small aperture systems: more noise, resolution issues
  Compression Artifacts – varying degrees
    More and more systems using compression
    Minor impact to detection, more impact to science
  Pictures vs. Measurements
  Follow-on satellites, or pairs, are very similar
    AWiFS-1/AWiFS-2, Pleiades-1a/-1b, SPOT-6 & 7, etc.
Planet Labs Image over NYC 07 Sep 2014

## Slide 14: Requirements Capabilities and Analysis for Earth Observations (RCA-EO)
Strong partnership between USGS and NOAA for infrastructure development, data sharing, and assessment of civil Earth Observation user requirements and capabilities
Supporting and benefitting from the OSTP National Earth Observation Assessments (EOA)
Collaborating with DOI and other civil agencies in assessing their needs
http://remotesensing.usgs.gov/rca-eo/
  Purpose:
  Support program planning and budget justifications – informed by user needs
  Improve the impact of USGS science and operational products and services
  Quantitative analyses to guide decisions for research investments and technology innovations
  Identify new Earth Observation solutions or capability gaps to better meet user needs

## Slide 15: RCA-EO Components
15
Value
Tree
Capabilities
Requirements
Analysis
RCA-EO Components
User Requirements
        Database of system-independent user needs
Observing Systems Capabilities
        Database of current and future Earth observing systems
Value Tree Information (VTI)
        Organizational program Earth observing input and capabilities mapped to the organization’s goals and objectives
Earth Observation Requirements Evaluation System (EORES) and Analysis
RCA-EO is driving toward a user needs driven business management process to address mission priorities, and incorporate evolving Earth observing technology
EORES
Using EOA VTI to elicit User Requirements
        Across all Civil Federal Agencies

## Slide 16: National Earth Observation Assessment
National Earth Observation Assessment (EOA 2012)
  http://www.whitehouse.gov/sites/default/files/microsites/ostp/NSTC/national_plan_for_civil_earth_observations_-_july_2014.pdf
  Conducted to inform the National Plan for Civil Earth Observations
  Identified a portfolio of observing systems relied upon by the Federal agencies
  Provided a cross-cutting and integrated look at observing capabilities (satellite and non-satellite systems)
  Quantified the impact of those observing systems in delivering societal benefit
Second National Earth Observation Assessment (EOA 2016) underway
  Refined process to capture details related to impacts and allow analysis of value information
  Tri-annual National Federal Government assessment
Both use an organizing framework for the assessment of 13 Societal Benefit Areas (SBAs) plus Reference Measurements
    Reference Measurements include geodesy, bathymetry, topography, geolocation, etc.
    Agriculture & Forestry, Biodiversity, Climate, Disasters, Ecosystems (Terrestrial & Freshwater), Energy & Mineral Resources, Human Health, Ocean & Coastal Resources & Ecosystems, Space Weather, Transportation, Water Resources, Weather
  SBA Teams each produced an assessment for their SBA

## Slide 17: Landsat – EOA 2012 Results
Assessment of 362 US Earth Obs. Systems (EOS) (space, air, land, and sea platforms) contributions to 13 Societal Benefit Areas (SBAs)
Landsat was 3rd out of total, and Landsat 2nd “most critical SBA impact” of 132 satellite systems (GPS=1)
10 of 13 (77%) SBAs use Landsat data
Landsat has a Significant Impact on 6 SBAs;
  Ranked #1 for contributions in Biodiversity, Ecosystems, and Energy
  Ranked #2 for contributions in Agriculture/Forestry, Climate, Human Health, and Water
31 of 52 (60%) Sub-SBA Areas utilize Landsat
  Landsat had a Significant Impact on 15 Sub-SBAs and a Moderate Impact on 6 Sub-SBAs
Societal Benefit Areas (inner ring)
Sub-Societal Benefit Areas (outer ring)
LANDSAT

## Slide 18: Additional Activities
Joint Agency Commercial Imagery Evaluation (JACIE) Workshop collocated with ASPRS; 40-plus JACIE papers
  April 12-14, 2016, Ft Worth, TX, http://conferences.asprs.org/Fort-Worth-2016/blog
  http://calval.cr.usgs.gov/satellite-sensor-characterization/rst-presentations-publications/
Extensive support to the RCA-EO Project
  Building “Capabilities” database
  Developing analysis methods and processes
ESA Sentinel-2a
  Archive Level 1c products available via USGS Earth Explorer; http://earthexplorer.usgs.gov/
ISRO ResourceSat-2
  Starting agreement to archive ResourceSat-2 products over the U.S.
Land Change Monitoring, Assessments and Projections (LCMAP)
  Architecture being built and tested, and Analysis Ready Data definition being published, and LCMAP Algorithms being developed
Preparing for Landsat-9 launch (Dec 2020) with NASA GSFC
Landsat 10 planning beginning
  Studies: Sensor type, resolution, platform type or types, swath width, coverage, ….,
Notes:   - Planet Labs has improved optics and detectors since our earlier investigations
  - CBERS-4 is of very high interest
  - DMC-3 is to launch with in the coming weeks (we think) and has 75cm pan band, 3m VNIR. Interestingly, 100% of imaging capacity leased by Beijing company

## Slide 19: Near-term GSICS Activities
Recommended solar spectrum for calibration purposes
  Total and spectral solar irradiance — referenced to which instrument(s) and measurement(s) ?
  Spectral resolution — accommodation of hyperspectral sensors
  Coordination with CEOS-WGCV
Lunar inter-calibration
  Evaluating uncertainties in the ROLO lunar irradiance model (to be discussed in GRWG VIS/NIR Lunar session, talk 4d)
  Coordination with CLARREO (Tom is on the Science Definition Team)

## Slide 20: Future Collaboration
Jointly support CEOS efforts
  Interoperability
  QA4EO
  Calibration test sites and processes
Continue to work cross-calibration and validation
  RadCalNet
  PICS
  Lunar
  LPCS
  Potential Joint Agency efforts
Become more involved in GRWG efforts, as needed
Cross calibration/comparison discussions welcomed
Notes: LPCS: Land Product Characterization System

## Slide 21
Thank You!
あ
り
が
と
う
Notes: LPCS: Land Product Characterization System