## Slide 1: Primary GSICS or Key Comparison References?
Tim Hewison
EUMETSAT

## Slide 2: Overview & Purpose of the Presentation
Overview
Primary GSICS or Key Comparison References?
Purpose of the Presentation
Explain Concept of Key Comparison Reference Values
Consider how to apply KCRVs to merge multiple inter-calibration references

## Slide 3: New Prime GSICS Corrections
Chart: Availability of References
Mon | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Ref1 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Ref2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Ref3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Modified References
Mon | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Ref1 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Ref2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Ref3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Define one Primary GSICS Reference
  For each spectral band/application
  By consensus agreement within GSICS
Use others as Transfer References
Blend corrections from all references
  After modifying Corrections to Primary GSICS Reference
Ensures long-term continuity
  Without calibration jumps
Ensures Traceability
  back to single Primary Reference
Simplifies users’ implementation
Could also blend multiple methods?
Chart: Simple Weighting of Each Reference
%Ref1 | 103 | 103 | 103 | 103 | 103 | 103 | 103 | 53 | 53 | 53 | 36.3333 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
%Ref2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 52 | 52 | 52 | 35.3333 | 52 | 52 | 52 | 52 | 52 | 0 | 0 | 0
%Ref3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 34.3333 | 51 | 51 | 51 | 51 | 51 | 101 | 101 | 101

## Slide 4: Correcting the Corrections and Blending References
Applied
by User
Reference-1 (Primary)
Monitored Instrument
GSICS Correction, g1 Mon1
Reference-2
(Secondary)
GSICS Correction, g2 Mon2
MonRef1
Delta
Correction, g1/2
21
Derived by GSICS
Modified
Correction, g2,1/2
Mon 21
Prime GSICS Correction, g0 Mon1
-
g̅
+

## Slide 5: Users’ Application of Prime GSICS Correction
Monitored Instrument
Prime GSICS Correction, g0 Mon1
MonRef1

## Slide 6: Scope of Prime Corrections
In the future the concept could be extended to obtain SI traceability if such a reference instrument becomes available - either using the double difference of GSICS Corrections, or by applying the SRFs to direct differences of hyperspectral instruments obtained by SNOs.
It was pointed out that after the overlap period, the traceability chain is strictly broken. This means we need to characterise the uncertainty growth - particularly in the case where there is a significant trend in the references' double differences.
The necessary stationarity tests should be applied to time series of double differences of GSICS Corrections using AIRS and IASI. [Masaya Takahashi (JMA) plans to investigate this.] They could also be applied to time series of IASI-A/B double differences after applying synthetic jumps.
We also discussed applying the concept to blend results from different inter-calibration methods (e.g. for GEO-LEO VIS products). It was noted that in general the uncertainty of the blended product could be larger than that of the best method, if the methods are applicable to different scenes, as this could cause them to underestimate the uncertainty when applying their results to more general scenes.
Rob Roebeling delivered Viju John's presentation on the impact for Archive Re-Calibration products. This analysis will need to account for diurnal variations in the geostationary imagers' calibration. It was greatly appreciated that NOAA (Manik Bali) plans to investigate this for both GOES and Meteosat imagers.
Masaya Takahashi (JMA) proposed changes to the content of the netCDF files and GSICS servers to accommodate the changes proposed above. Masaya's recommended solutions were approved in principle, but the details will be discussed further by email.

## Slide 7: Key Comparison Reference Values
Now we have multiple possible reference instruments
  AIRS, IASI-A, IASI-B, CrIS, ...
  MODIS-A, MODIS-T, VIIRS, ...
Consider alternative approach – Key Comparison Reference Values
  Weighted average of all available references
  Need realistic uncertainties for each reference
  May need to define a minimum uncertainty to prevent one becoming dominant
  KCRV has finite uncertainty,
    but included in that of each Reference’s “degree of equivalence”
  Used in Metrology
For more details, see KCRV Introductory Presentation by Emma Woolliams (NPL)

## Slide 8: Concerns about KCRVs
How to define?
  For hyperspectral references – independently for each channel/band
  Over dynamic range – typical values? In radiance bins?
  Using 3-dimensional weighting (“Key Comparison Reference Curves”)
  - according to uncertainties as function of (wavelength, radiance, time, ...) ?
How often to re-define KCRV?
  Daily? Monthly? Yearly?
  As soon as new reference becomes available?
  After some monitoring period to ensure uncertainties realistic?
  As soon as a reference becomes unavailable?
Concerns:
  KRCV changes when references join/leave the ensemble
  Will introduce discontinuities in FCDRs derived from them
How to Proceed?
  NPL have some funding to investigate
  Who is interested in joining?