## Slide 1: GEO-LEO IR regression method and variables
For more convenient GSICS Correction variables
Regression methods
Reduced Major Axis regression

## Slide 2: Unit of the GSICS Correction
Current contents
  Offset and slope to convert GEO radiance to LEO radiance in [mW m-2 sr-1(cm-1)-1].
  Tb bias at std. scene
  Conversion coefficients and equations between Tb and radiance
  Optional variables in MTSAT-2:
    Offset and slope to convert GEO DN to LEO radiance in [mW m-2 sr-1(cm-1)-1]
    LUT from GEO DN to LEO Tb [K]
Situation in AHI
  Himawari Standard Data (HSD, L1B equivalent) is based on radiance in [W m-2 sr-1 um-1 ].
  JMA/MSC web page provides conversion coefficients between rad[WN] and Tb[K].
  LUT approach (JMA optional B) is not reasonable for AHI any more.
    3.9 um band has 14 bits.
  HSD has “Inter-calibration information block” to contain the information (C).
GEO DN
GEO Tb [K]
GEO rad. [WN]
LEO rad. [WN]
LEO Tb [K]
LEO rad. [WL]
GSICS Correction
GEO rad. [WL]
A)
For “WL” users to obtain LEO radiance
C)
B)
HSD data format
C)

## Slide 3: For more convenient coefficients...
GEO DN
GEO Tb [K]
GEO rad. [WN]
LEO rad. [WN]
LEO Tb [K]
LEO rad. [WL]
Current GSICS Correction
GEO rad. [WL]
Many users will adopt the same unit as L1B data of each monitored imager.
For more convenient coefficients, why don’t we contain conversion coefficients from DN to corrected radiance, (A) or (C), depending on the unit of monitored sensor L1B data?
IASI, AIRS, Cris Meteosat?
[mW m-2 sr-1(cm-1)-1]
Himawari, GOES-R?,
MODIS, VIIRS
[mW m-2 sr-1um-1]
A)
C)

## Slide 4: How can we take regression?
Bias in “cold end”
  Uncertainty of brightness temperature (Tb) bias tends is larger in lower Tb range, especially in SWIR.
  Some meteorologists are interested in cold region.
  It is caused by non-linearity between radiance and Tb and is significant in shorter wavelength.
Is such the large bias true?
Planck’s law says...
 | 3.9 um | 6.2 um | 10.4 um
300 K | 0.6021 | 5.682 | 9.823
200 K | 0.00128 | 0.1187 | 0.9703
[W･m-2･sr-1･(μm)-1]
Tb bias is -5 K at 220 K, -15 K at 210K. The corrected radiance become minus in Tb < 207 K.
Energy is 1/470

## Slide 5: How can we take regression?
To take a regression in Tb space?
  It can bring reasonable-like averaged bias in lower Tb range, but ...
  GEO Tb and LEO Tb are not always linear, because radiance and Tb is not linear.
To separate Tb bins and take a regression in each bin?
  How to separate?
To set a valid Tb range?
  How to estimate the validity?
Band 7 (3.9 um)
Radiance vs Radiance
Tb vs Tb
Radiance vs Radiance
Tb vs Tb
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
Band 8 (6.2 um)
invalid
January 2016
January 2016

## Slide 6: Three Regression Methods
Least squares regression is appropriate when there is uncertainty only regarding the y-variable. If both variables are subject to sampling and measurement error, major axis or reduced major axis regression is recommended. In the first two cases, the sum of the squared distances indicated by the green lines is minimized. In the final case, it is the areas of the triangles bounded by the horizontal and vertical green lines that are summed and minimized.
http://bill.srnr.arizona.edu/classes/182/Giraffe/Regression.htm
Least Square
Major Axis
Reduced Major Axis

## Slide 7: Which Regression?
Least squares (LS)
  No error in X is assumed
  Y = aX + b is not equivalent to X = a’Y + b’
Major Axis regression (MA)
  Unit of X and Y should be the same
  Y = aX + b is equivalent to X = a’Y + b’
Reduced Major Axis reg. (RMA)
  X and Y are correlated
  Y = aX + b is equivalent to X = a’Y + b’
  Easy to calculate
The top left figure is from http://aoki2.si.gunma-u.ac.jp/R/scatter.html (in Japanese)
Radiance vs Radiance
AHI (3.9um, Tb < 230K) and IASI/A
LEO
GEO - LEO
N = 578
January 2016

## Slide 8: MTSAT-1R 6.8 um vs. AIRS/IASI
LS regression
RMA regression
Analyzed TB difference at 250 K
Analyzed TB difference at 220 K

## Slide 9: Discussion
Unit of the GSICS Correction
  Why don’t we contain conversion coefficients from DN to radiance?
Tb bias in lower Tb region
  Regression in Tb space:
    GEO and LEO Tb is not always linear, especially for SWIR.
    Regression in multiple Tb bins, or set a valid range?
RMA regression:
  RMA (or MA) regression is suitable since both GEO and LEO contain error
    LS regression assumes X-axis value contains no error.
  However, LS regression is acceptable if the error of GEO/LEO data is small and they are well correlated
    Difference between LS and RMA is very small in monthly statistics between MTSAT-1R and AIRS/IASI
  RMA (or MA) should be used in case of limited number of data compared
    Daily statistics
    Bias analysis by dividing some bins (Tb, time, location,...)