## Slide 1: Hyperspectral Infrared Sounder Traceability and Uncertainty
Likun Wang1* and Tim Hewison2
1. CICS/ESSIC/UMD
2. EUMETSAT
*Email: wlikun@umd.edu
Contributions from CNES, UW, UMBC, NOAA/STAR, JPL/AIRS team, EUMETSAT …
2016 GSICS Annual Meeting, Tsukuba, Japan

## Slide 2: Outline
Hyperspectral IR Instruments
Calibration uncertainties and traceability
  Using CrIS as an example
Inter-Comparison results
Discussion

## Slide 3: Spectral Coverage of AIRS, IASI, and CrIS
AIRS (2378 channels)
Aqua (2002-now)
IASI (8461 channels)
MetOp-A(2006-now)
MetOp-B (2013-now)
CrIS Normal Resolution
(1305 channels)
NPP (2011-now)
CrIS Full Resolution
(2211 channels)
NPP (2014-now)
Proposed for Future
CrIS on JPSS/2

## Slide 4: AIRS: Grating Spectrometer
From Christ Barnet
AIRS detector Array
Launched on 2002 on NASA Aqua

## Slide 5: IASI and CrIS: Interferometer
CrIS optical system
IR spectrum
Interferogram
Fourier
Transform
From Yong Han, NOAA/STAR

## Slide 6: Radiances consistency of CrIS, IASI, and AIRS Inter-calibration for other instrument
GEOS Decontamination
  Each Agency routinely uses AIRS/IASI to assess calibration accuracy of its own geostationary instruments
Spectral and radiometric consistency among CrIS, AIRS and IASI is significant for GSICS community.
GSICS Framework: Independent Calibration Assessment

## Slide 7: Hyperspectral Sounder Calibration
Radiometric calibration
  Calibration accuracy
  Noise
Spectral calibration
  How does frequency shift?
Geometric calibration
  Geolocation accuracy
Must be well documented and monitored during the mission
Radiometric
Spectral
Spatial

## Slide 8: NPP CrIS Sensor Data Record Calibration Uncertainty Specifications
Band | Spectral range (cm-1) | N. of chan. | Resolution (cm-1) | FORs per Scan | FOVs per FOR | NEdN @287K BB mW/m2/sr/ cm-1 | Radiometric Uncertainty @287K BB (%) | Spectral (chan center) uncertainty ppm | Geolocation uncertainty km
LW | 650-1095 | 713 | 0.625 | 30 | 9 | 0.14 | 0.45 | 10 | 1.5
MW | 1210-1750 | 433 | 1.25 | 30 | 9 | 0.06 | 0.58 | 10 | 1.5
SW | 2155-2550 | 159 | 2.5 | 30 | 9 | 0.007 | 0.77 | 10 | 1.5
SDR Calibration Uncertainty
Radiometric uncertainty specification converted to that expressed in brightness temperature
NEdT, 0K
From Vladimir Zavyalov of SDL

## Slide 9: Radiometric calibration Uncertainties
From Dave Tobin at Univ. of Wisconsin

## Slide 10: On-orbit Radiometric Uncertainty (RU) for a typical clear sky scene
From Dave Tobin at Univ. of Wisconsin

## Slide 11: Spectral Calibration
LWIR
Cross-correlation method under Clear Sky between Observation and RTM calculation
Inter FOV: ~ 1 ppm
Spectral calibration with respect to CRTM is less than 4 ppm for LWIR, MWIR, and SWIR
CrIS respect to CRTM
IASI respect to 4A/OP
From Yong Chen of UMD
From Elsa Jacquette of CNES
Inter FOV: ~2.5 ppm.
Overall region ~2ppm but some regions have larger undercities

## Slide 12: Part II Inter-comparison Results
SNO direct comparison
  CNES , UW, NOAA/STAR, JPL, UMBC
Double Differences: relative to common reference
  RTM Simulations
  Other instruments
Aircraft Instruments

## Slide 13: Simultaneous Nadir Overpass (SNO) Between CrIS and IASI
IASI
CrIS
Time Difference: <= 120 Sec
FOV distance difference: <=(12+14)/4.0 km = 6.5 km
Angle Difference: ABS(cos(a1)/cos(a2)-1) <= 0.01
From Changyong Cao
SNO Spectra during full resolution test
On August 27 2013
CrIS: Afternoon orbit
IASI : Morning orbit

## Slide 14: CrIS vs. IASI-A SNO Results NOAA/STAR
South Pole (2475)
North Pole (2168)
Bias: CrIS-IASI
STDEV: CrIS-IASI
Bias: CrIS-IASI
STDEV: CrIS-IASI

## Slide 15: CrIS vs. IASI-A results from UW
From Dave Tobin at Univ. of Wisconsin

## Slide 16: IASI vs. CrIS from CNES

## Slide 17: Scene-Dependent Bias CrIS-IASI/A
CO2 sounding channel
CO2 sounding channel
Atmospheric window channel
Atmospheric window channels
Atmospheric window channels
water vapor absorption channels

## Slide 18: Simultaneous Nadir Overpass (SNO) Between CrIS and AIRS
AIRS
AIRS
CrIS
CrIS
SNOs at Polar regions
SNOs at the
Tropics
CrIS and AIRS: afternoon orbit
From Changyong Cao
From Changyong Cao

## Slide 19: CrIS vs. AIRS from STAR
SNO spectra at North Pole
SNO spectra at South Pole
SNO spectra at the Tropics
CrIS-AIRS
CrIS-AIRS
CrIS-AIRS
SNO spectra in Global
CrIS-AIRS

## Slide 20: Scene-Dependent Bias
CO2 sounding channels
Atmospheric window channels
shortwave channels
water vapor absorption channels
North Pole
South Pole
Tropics

## Slide 21: AIRS vs. CrIS from UW
From Dave Tobin at Univ. of Wisconsin

## Slide 22: IASI vs. AIRS From CNES

## Slide 23
Double Difference between CrIS and IASI2CrIS
From Yong Chen of UMD

## Slide 24: Inter-comparison with SHIS from UW
From Joe Taylor of UW

## Slide 25: Conclusion
CrIS, AIRS, and IASI radiometric and spectral calibration uncertainties should be monitored and reported to GSICS.
CrIS vs. IASI-A/IASI-B
  IASI spectra can be converted into CrIS spectral grid and the comparison can be done along CrIS spectral grid.
  CrIS and IASI well agree each other at LWIR and MWIR bands with 0.1-0.2K differences, but MWIR band is more consistent. CrIS is warmer than IASI at LWIR band.
  No apparent or strong scene dependent bias.
  At SWIR band, a sharp increases can be clearly seen at spectral transition region.
  The results from different groups generally agree.
IASI/CrIS vs. AIRS
  IASI/CrIS and AIRS are hard to compare at the finest spectral grid. Different groups choose the different spectral regions using box-car average methods. The results are hard to compare to each other,
  IASI/CrIS and AIRS agree each other at LWIR and MWIR bands with the differences of 0.1-0.2 K .
Given the fact that the radiometric differences do exist between hyperspectral instruments, the inter-calibration community should be cautious to use only one hyperspectral sounder as a prime reference. A best practice should compare the broad- or narrow-band instruments against all four hyperspectral sounders to avoid biasing the results.

## Slide 26: Radiances consistency of CrIS, IASI, and AIRS (2) Climate Data Records
AIRS – Simulations (Reanalysis)
Hyperspectral radiance measurements can serve as a benchmark for model assessment, but the consistency is the key.

## Slide 27: SNOs Latitude Distribution Time Series
The SNOs between SNPP and Aqua occurred every days.
The SNOs between MetOp and SNPP occurred every 50 days.
Fortunately, once an SNO event occurs, their orbits will continuously cross each
other every orbit.

## Slide 28: Resample IASI to CrIS
Fourier Transform
Inverse Fourier Transform
1) De-Apodization of IASI spectra
2) Truncation of IASI spectra
3) Apodization using CrIS Hamming Apodization function
CrIS – IASI
Re-sampling error very small

## Slide 29: Match CrIS with AIRS: Focus on 25 spectral regions
CrIS-AIRS match error is less than 0.06K with consideration of
AIRS degraded channels.
Ideal case

## Slide 30: Match CrIS with AIRS: Focus on 25 spectral regions
CrIS-AIRS match error is less than 0.06K with consideration of
AIRS degraded channels.
In reality

## Slide 31: CrIS vs. IASI/MetOp-B
South Pole (2284)
North Pole (2020)
Bias: CrIS-IASI
STDEV: CrIS-IASI
Bias: CrIS-IASI
STDEV: CrIS-IASI
applied retrospectively