## Slide 1
Inter-Comparison of VIIRS and Aqua MODIS TEB Using Hyperspectral IR Souder Measurements as Transfer Reference
Yonghong Lia, Aisheng Wua, Xiaoxiong Xiongb
aSigma Space Corporation, 4801 Forbes Blvd, Lanham, MD 20706, USA
bSciences and Exploration Directorate, NASA/GSFC, Greenbelt, MD 20707, USA
2016 GSICS GRWG/GDWG Annual Meeting, Tsukuba, Japan, Feb 27 - Mar 4.

## Slide 2
Introduction
Methodology
  SNO from hyperspectral measurements (IASI, AIRS and CrIS) as transfer reference
  Results
    Spectral and spatial integration
    Spectral band adjustment factor
    NPP VIIRS and Aqua inter-comparison
Summary
Outlines

## Slide 3
MODIS RSR vs CrIS and AIRS spectral range

## Slide 4
Simulated MODIS and VIIRS radiance from hyperspectral data
Spectral and spatial integration
[λ1,λ2]: range of Relative Spectral Response (RSR) wavelength
Aggregate MODIS pixels within each IASI IFOV
  MODIS 1-km pixels are collocated with an AIRS/CrIS 14-km IFOV
  Typically >100 MODIS pixels are collocated within one hyperspectral IFOV
  Only IFOVs with >70 MODIS pixels are considered in SNO data collection
MODIS Pixel
AIRS/CrIs Pixel

## Slide 5
VIIRS and MODIS Spectral band adjustment factor (SBAF)
SBAF=
AIRS
CrIS

## Slide 6
ΔBT = BT(VIIRS) –(MODIS)
VIIRS and MODIS TEB inter-comparison
Before RSR
correction
After RSR
correction
AIRS
CrIS

## Slide 7
BT (K) | M13-B22 | M13-B23 | M15-B31 | M16-B32
230 | 0.16 0.11 | 0.04 0.10 | -0.01 0.01 | 0.04 0.09
250 | 0.06 0.08 | 0.04 0.05 | -0.04 0.00 | 0.02 0.07
270 | 0.10 0.15 | 0.16 0.15 | -0.05 -0.06 | -0.03 0.04
290 | 0.07 0.16 | 0.12 0.15 | -0.04 -0.06 | -0.10 0.00
AIRS CrIS
Relative calibration differences (K) between VIIRS and MODIS TEB

## Slide 8
Results
Average Differences between MODIS and IASI Measurements

## Slide 9
Summary
There is excellent agreement (well within 0.20K) between NPP VIIRS and Aqua MODIS for the spectrally matched TEB.
Real-time hyperspectral IR measurements (IASI, AIRS and CrIS) can facilitate high quality sensor-to-sensor calibration and inter-comparison.