## Slide 1: Application of GIRO to NIR bands
Meteorological Satellite Center,
Japan Meteorological Agency

## Slide 2: Lunar calibration for AHI
AHI observes the moon on routine basis. 60-70 lunar images can be obtained in a day on average.
More than 5000 images were archived in a half year.
AHI has 3 NIR bands. We are interested in a performance of GIRO for the NIR bands.
 | Wavelength [um]
Band 1 | 0.47
Band 2 | 0.51
Band 3 | 0.64
Band 4 | 0.86
Band 5 | 1.6
Band 6 | 2.3
AHI VNIR bands

## Slide 3
Region 4, 5: mainly used for landmark observation, but region 5 is also used for lunar observation
Full Disk Observation
every 10 min.
Region 1
2000 x 1000km
(NE Japan)
Every 2.5 min.
Region 2
2000 x 1000km
(SW Japan)
Every 2.5 min.
Region 3
1000 x 1000 km
(Target Area)
Every 2.5 min.
Region 4
1000 x 500 km
(Landmark Area)
Every 30 sec.
Region 5
1000 x 500 km
(Landmark Area)
Every 30 sec.
Preliminary fixed area
Flexible observation area
AHI FoR
Earth edge
Lunar observations
Band5 (1.6μm)
Full Disk / Regional Observation in 10 minutes Repeat Cycle

## Slide 4: AHI Lunar Observation
Performed using Region 5 (1000x500km for the earth scene) flexible observation
Just one scan to observe the Moon
1 observation / 30 seconds
-> lots of observation
Earth disk
MTSAT-2/Imager
(Jul.2010 – Dec.2013)
98 Obs. / 3.5 years
Lunar phase angle [deg]
Full moon
-180 -120 -60 0 60 120 180
Earth disk
AHI FoR
Himawari-8/AHI
(30 Mar. – 12 Sep. 2015)
4956 Obs. / 5.5 months

## Slide 5: AHI Lunar Observation for GIRO
2979 useful lunar observations for the GIRO within the applicable phase angle:
2 deg <= |phase angle| <= 92 deg
47 days data
-> 60-70 lunar observation / day on average
Time series of AHI lunar phase angle [deg]
B01 (0.47μm)
B02 (0.51μm)
B03 (0.64μm)
B04 (0.86μm)
B05 (1.6μm)
B06 (2.3μm)
2015-08-01T03:03:26Z (phase angle: 10.5deg)
[deg]

## Slide 6: AHI Lunar Calibration – Preliminary Results
MSG1/SEVIRI NIR1.6 result
by B. Viticchie at the Lunar calibration Workshop in Dec. 2014
Himawari-8/AHI Band05 (1.6μm)
8 June to 3 September 2015
ΔIrr (%)
Phase angle (deg)
Phase angle dependence
Similar results with other instruments (e.g. MSG/SEVIRI NIR1.6)
Need to be investigated further
Difference of lunar irradiance between the observation and GIRO [%]
25 May to 8 June 2015
Operated under different calibration coefficients

## Slide 7: Phase angle vs ΔIrr
~ 3%
~ 4%
~ 4%
~ 3%
~ 10%
~ 15%
Phase angle dependency depends on band.
It looks significant in longer wavelength.
The variation might be caused by coherent noise on images.
Need to be investigated further

## Slide 8
AHI Lunar Calibration Preliminary Results – Case Study
AHI FoR
Earth edge
Lunar observations
29 August 2015
Phase angle: from -11.5 to -9.0 [deg]
100 observation / ~90 minutes
Difference of lunar irradiance between the observation and GIRO [%]
Averaged deep space counts
Number of the Moon pixels
ΔIrr (%)
~0.6%
Deep space count depends on a distance from the Earth.
~0.3 count

## Slide 9: Summary and Future Plan
Lunar observation by AHI
  AHI observed more than 5000 images in a half year.
  The AHI’s frequent observation function helps to investigate characteristics of GIRO output.
Findings
  AHI NIR bands, 1.6 um and 2.3 um, shows the angular dependency similar to MSG1/SEVIRI 1.6 um.
  Deep space count in AHI potentially depends on distance from the earth.
Future plan
  Processing AHI lunar data after September
  Improvement of deep space data handling
  Inter-comparison of results with the ones by other calibration approaches such as DCC and SD observation.
  Further investigation, especially the case such as 29 August