## Slide 1: NOAA’s Progress toward DCC Demo Product
GSICS Annual Meeting in Tsukuba, Japan, 2016

## Slide 2
GOES Imager 4KM data
Subset GOES data
Potential DCC identification
Lat = [-25., 25.]
Lon = [nadir_lon – 30, nadir_lon + 30.]
Time duration = [1:30pm LST – 2.0, 1:30pm LST + 2.0]
SZN < 50
VZN < 50
Tb4 < 215K
STDV(Tb4) < 10K
STDV(Refl) < 5%
Data Analysis
Time titude
Longitude
Solar zenith angle
Solar azimuth angle
Satellite viewing zenith angle
Satellite viewing azimuth angle
Raw count for the solar reflected channel(s)
Radiance for the IR channels
Standard deviation of the reflectance (3x3 pixels window)
Standard deviation of the Tb (3x3 pixels window)
Archived variables in the intermediate products
Implemented since Dec. 2012
Paused since July 2015 due to the server breakdown
Plan to revive them with the help of NOAA GDWG
Procedures to Select Potential DCC

## Slide 3
Potential DCC Data
Lat = [-20., 20.]
Lon = [nadir_lon – 20, nadir_lon + 20.]
Time duration = [12:00pm LST, 3:00pm LST ]
SZN < 40o
VZN < 40o
Tb4 < 205K, after GSICS correction
STDV(Tb Ch10.7um) < 1K
STDV(Refl, Ch0.65um) < 3%
Archived intermediate products
DCC Thresholds
DCC pixel selection following the criteria by Doelling et al. (2011), the outline ATBD for the NASA DCC method:
https://gsics.nesdis.noaa.gov/pub/Development/AtbdCentral/GSICS_ATBD_DCC_NASA_2011_09.pdf
Data Analyses

## Slide 4
Data Analysis
Monthly DCC pixel
Reference Reflectance
Hu’s BRDF model
ADM Correction
Representative DCC Reflectance
DCC# > 2000?
NO
Next Month
YES
Spectral Conversion
Mean/Median/Mode
SCIAMACHY-based SBAF
De-seasonalization
Trending
Gain
Not available yet

## Slide 5: Issue to be solved before submitting the demo product
Sever is down since July 2015
Need to work with NOAA GDWG to revive the GOES-13/15 Imager DCC pixel selections