## Slide 1: VIS/NIR reference instrument requirements
Doelling
Feb 22, 2016

## Slide 2: VIS/NIR absolute calibration reference
Currently no visible instrument can be used as an absolute calibration reference
  MODIS absolute calibration uncertainty is 1.6% during ground characterization
CLARREO or TRUTHS will give eventually provide an on-orbit SI traceable reference
Until then the VIS/NIR calibration reference must consist of overlapping sensor sensor records to transfer the calibration SI traceable reference back in time
In the future invariant targets such as the moon can provide an SI traceable reference
  This provides a direct calibration transfer without a reference instrument

## Slide 3: VIS/NIR overlapping reference instruments
In order to reduce the uncertainty between overlapping sensor, the sensor characteristics should be very similar
  The 4 JPSS and NPP VIIRS instruments will provide overlapping coverage between 2012 and 2038
  Since all 5 VIIRS instruments will be nearly exact replicas, VIIRS inter-calibration will not need SBAF, and the same calibration methodologies can be used throughout, thus reducing the inter-calibration uncertainty
For both VIIRS and MODIS each channel is independently calibrated, thus requiring each channel used as a reference to be stable over time and inter-calibrated over time
  Possible to do inter-channel calibration using lunar and earth targets to determine the relative calibration bias between channels.

## Slide 4: Possible VIS/NIR overlapping Reference Instruments
NOAA/Metop AVHRR instruments
  1980 to 2024, similar channels within the 3 builds
  Limited visible channels, degrading NOAA orbits, no onboard calibration, AVHRR/3 dual gain
Terra/Aqua MODIS instrument
  2000 to 2021, 1 morning and 1 afternoon satellite, onboard SD calibration
NPP/JPSS VIIRS instrument
  2012 to 2038, afternoon orbit, 5 satellites, onboard SD calibration
GOES 3rd generation imagers
  2016 to 2035, ~10 GEO satellites onboard SD calibration in 4 locations GOES-West, GOES-East, Himawari, COMS, GEO inter-calibration possible
MTG 3rd FTI generation imagers
  2019 to 2039, 4 GEO satellites, onboard SD calibration in 1 location.
Metop SG 3MI and Sentinel 5 instruments
  2021 to 2042, both imager and hyper-spectral instruments, morning orbit, 3 satellites, onboard SD calibration

## Slide 5: Reference Instrument Minimum Requirements
Once a sequence of overlapping sensor is selected as the reference record, the other reference records will be used to validate the calibration transfer.
The reference instrument must have an active instrument calibration team funded by the project over the lifetime of the satellite
  Must have onboard calibration that is well characterized, preferably with SD and lunar monitoring
  The pre-launch and on orbit calibration must be well documented in journals
  The data must be publicly available and easy to order and download and be released in near real-time
  The instrument must have many users to verify the calibration and discover any calibration anomalies

## Slide 6: Requirements with respect to tracing the reference calibration
Instrument calibration uncertainty
  Radiometric noise, scan angle dependency, calibration stability, polarization knowledge, spectral resolution or SRF knowledge
Hyper-spectral instrument is preferred to reduce SBAF errors
  If the broadband instrument is very stable and the SBAF uncertainty is less than the uncertainty of the Hyperspectral sensor calibration, then the braodband instrument is preferred.
Dynamic range considered when transferring the reference calibration from one sensor to another.
  Prefer to have at least some inter-calibration locations other than at the poles. All JPSS to be in the same orbit makes this possible

## Slide 7: Requirements with respect to Target sensor
These requirements change with target sensor and inter-calibration methodology
Lunar observations
Geographic coverage
Dynamic range, saturation
Spectral range
Scanning capabilities, pointing, or VZA limitations
Orbit limitations, sun-synch orbit, precessing orbit, diurnal coverage
# of collocations
Geolocation and co-registration accuracy

## Slide 8: Suggested VIS/NIR Instrument References
The reference sensor weighting scheme is then the overall uncertainty to transfer the SI traceable calibration reference to the target reference
Pre 2012 Aqua-MODIS
Post 2012 use VIIRS, VIIRS onboard calibration superior and better characterized than MODIS
Evaluate the 3rd generation GEO and Metop-SG calibration stability and reconsider VIS/NIR reference instrument
Also worth to have several reference records established
  To monitor the primary reference
  In case of instrument failure and lack of overlap