## Slide 1: Revising the ROLO Lunar Model — A Status Update
Thomas C. Stone
U.S. Geological Survey, Flagstaff, AZ USA
GSICS webmeeting
30 August 2016

## Slide 2
To produce a new lunar irradiance model using data existing today requires the following steps, in sequence:
Reprocessing the ROLO lunar image dataset (model basis data)
  ROLO is still the most extensive collection of lunar measurements
  involves revising the telescope data reduction routines for image processing to irradiance measurements
    routines for evaluating background and edge spread effects
    data quality checks: comparison against the current lunar model
Reformulating the lunar disk reflectance model
  e.g. implement band-dependent libration terms
Fitting the irradiance dataset — obtaining model coefficients
  develop and implement fit constraints derived from external data, e.g. PLEIADES, SNPP-VIIRS
  iterate with (2) above
Testing the new model
  reprocess existing lunar measurement datasets and compare results
    do we still see a phase angle dependence for e.g. MSG series?

## Slide 3
Next efforts at USGS:
revising the ROLO data reduction system
  i.e. Step 1 of the sequence
assessing uncertainties in the existing ROLO model
  essential for ground-based aerosol measurements at night using moonphotometers
  geometric specification — irradiance changes with phase and libration
  spectral specification of the lunar reflectance (and solar irradiance)
Future efforts: redeveloping the lunar calibration reference
requires new, high-accuracy basis dataset(s)
  NIST ground-based lunar irradiance measurement project
    Stephen Maxwell has taken over from Claire Cramer
  NASA-Langley cubesat mission — ARCSTONE
    prototype instrument designed and built by Resonon, tested at NIST
    instrument EDU is under development
    proposal submitted to NASA Instrument Incubator Program → TRL 5