## Slide 1: GRWG VIS/NIR Sub-Group Briefing Report
GSICS VIS/NIR Sub-Group Members presented by David Doelling
2016 GSICS Joint Meeting on Research and Data Working Groups
Madison, WI, USA, March 20-24, 2017

## Slide 2: What motivates my burning questions
The CERES project temporally interpolates clouds and fluxes in between CERES measurements to compute daily and monthly TOA fluxes for climate studies
  Use geostationary hourly clouds and derived broadband fluxes that are carefully normalized to the CERES observed fluxes
CERES seeks as many geostationary imagers across the equator as possible
  Meteosat-8 over the Indian Ocean domain will greatly improve diurnal fluxes in the region
I also hope for end of life LEO imagers to maneuver into a precessionary orbit in order to sample more diurnal local hours to validate the GEO derived broadband fluxes and clouds
  Terra in 2021 may do one last orbit maneuver to maintain the 10:30 local time orbit for a few years and then precess until it de-orbits

## Slide 3: GSICS and CEOS IVOS recommended solar spectra
Recommend a solar spectra for the GSICS community in collaboration with CEOS IVOS
  Engaged Nigel Fox and IVOS community with this effort
  Had GSICS sponsored web meetings in December 2016 and February 2017
  IVOS held a solar spectra discussion as part of their annual meeting in Arizona last week
  Short term approach to construct a solar spectra based on the best solar spectra datasets, which have been scaled to a common TSI reference in the more temporal stable part of the spectra. (Thuillier and COSI datasets)
  Long term approach to account for the variability in the UV radiation, the solar sunspot cycle, and higher spectral resolution using both observed and modeled datasets

## Slide 4: VIS/NIR Reference Instrument
We are in the process of migrating to NPP-VIIRS as the reference instrument
    NPP-VIIRS is the best characterized, stable, and freely available VIS/NIR sensor
    No major RVS or degradations have been identified
  VIIRS has very similar channels as the current and future 3rd generation GEOs.
    Suggest NPP-VIIRS I1 band rather than M5 band, since the spectral response function is nearly identical with Aqua-MODIS Band 1
    The NPP-VIIRS LandPEATE version 001 I1 band has been radiometrically scaled to the calibration of Aqua-MODIS B1
Future will need to transfer the calibration between reference successive MODIS and VIIRS instruments
  Each MODIS and VIIRS channel is independently calibrated
  Need to establish traceable chain of calibration transfers between successive reference instruments ultimately tied to CLARREO or TRUTHS

## Slide 5: Spectral Band Adjustment Factors (SBAF)
There are 3 VIS/NIR hyperspectral datasets that can be used for SBAF
  SCIAMACHY 30x240 km FOV, mostly complete visible spectra (except > 1.6µm), high resolution spectra
  GOME-2 40x80 km FOV, limited visible spectra, high resolution spectra
  Hyperion 30m FOV, complete spectral range, low spectral resolution, limited sampling
NASA-Langley SBAF proposal was accepted for funding
  To incorporate SCIAMACHY, GOME-2, Hyperion, IASI and AIRS
  The SBAF uncertainty can now be reduced by stratifying by angle, PW, many more surface types
Future SBAF
  Obtain more hyper-spectral datasets and further collocations of atmospheric, cloud, aerosol, and surface type conditions

## Slide 6: VIS/NIR Combining Methods
The VIS/NIR product to contain the individual calibration approach coefficients
Combine the multiple calibration approaches to provide users calibration coefficients with the least uncertainty
Combining methods proposed
  Bertrand, evaluate consistency calibration results among methods and optimize weighting for final coefficients with respect to the uncertainty of the absolute calibration transfer of the reference instrument, and the noise of the method with respect to the degradation
  Fangfang, iterative recursive filtering technique, this takes the more stable part of all methods to estimate the final instrument degradation
This year goal to define combining of methods for the DCC and lunar calibration methods among GPRCs
  In the future more calibration methods will be developed and will be added to the VIS/NIR product

## Slide 7: Lunar Calibration Status Sebastien and Tom
- New version of the GIRO implemented Q4 2016 ==> no issue anymore with licenses
- Preparation of the License Agreement for distributing the GIRO and the GLOD. First two agreements sent out in February 2017 to USGS and JMA! Once signed by all parties, the license will be provided to the Lunar Calibration Community members. This open the distribution of the GIRO and GLOD.
- Several requests for access received in 2016: ESA (working on Moon measurements with CIMEL photometers) and private companies! Only ESA was granted access.
- Preparation of the Second Joint GSICS/IVOS Lunar Calibration workshop, hosted by CMA in China: two web meetings (see Lunar Calibration area on the GSICS wiki for the topics)
- Study funded by EUMETSAT on the validation of SBAFs using hyperspectral measurements allowed in depth analysis of SCIAMACHY lunar observations ==> follow-on studies are already planned, with potential improvement of the ROLO/GIRO.

## Slide 8: Lunar Calibration for next year Sebastien and Tom
- Continue with the preparation of the Lunar Calibration Workshop
- Development of a benchmark for the GIRO
- Inter-calibration using the Moon: EUMETSAT developed a prototype based on the approach presented in Tsukuba. JMA has also implemented it.
- Move from MODIS to VIIRS for lunar inter-calibration (and DCC)

## Slide 9: DCC calibration Status
The DCC method has been implemented by most GPRCs in 2015
  Continue to work with KMA and IMD
Continued to improve the DCC invariant target method, by evaluating the DCC BRDF, deseasonalization methods, DCC PDF statistic, BT threshold, the inter-annual variability of the DCC reflectance

## Slide 10: DCC calibration to Demonstration Product is this years goal
Work with GPRCs to achieve demonstration product
Began product acceptance procedure
Write a combined GPRC GSICS DCC calibration method/implementation paper
Begin to implement the DCC invariant target calibration to other VIS, NIR and SWIR bands

## Slide 11: GSICS products and plotting
VIS/NIR Product file format is nearly finalized
  File naming convention following WMO format
  File parameters and coefficients structures finalized, to include variables that describe the calibration method adjustments for each GEO in order to reproduce the calibration coefficients faithfully
  One VIS/NIR calibration file containing all calibration from multiple methods and channels
  Frequency Update being resolved
    Dependent on calibration method sampling: DCC can be updated daily and Lunar monthly
    Dependent on the magnitude of the monitored instrument on orbit degradation
Bias monitoring plotting being developed similar to the IR bias monitoring
  JMA has presented protoype
  Do we plot the relative degradation, the correction?

## Slide 12: Develop new VIS/NIR calibration approaches
Having multiple calibration methods, which produce consistent calibration coefficients, validates all techniques
  An individual method maybe more suitalbe for the user application
  Methodology success is dependent on the monitored and reference instrument
Need to prepare for new 3rd generation GEO calibration methodologies
  GRPCs priorities are for current instrumentation
  Have onboard calibration, which as not the case with 2nd generation, and have very similar channel bandwidths as the reference instrument, making other methodologies more reliable than earth invariant targets
Will discuss the development of other calibration VIS/NIR methods, which can be applied consistently across sensors
  Methodologies that take advantage of the 3rd generation GEOs
  Is there a need to calibrate other instrument records other than GEOs?