## Slide 1: Use of NWP+RTM as inter-calibration tool
Tim Hewison
EUMETSAT

## Slide 2: Direct Comparison of Collocated Radiances
Relative differences
Limited coverage
Trends
Ob1-Ob2
Radiances
Notes: These direct comparisons have formed the bulk of the GSICS activities to date, and, therefore form the focus of this presentation.
However, these represent only 1 of the 3 basic methodologies we use to address the requirements of GSICS.

## Slide 3
Double differencing
Cancels model bias
Regional averages
Extended ranges
Trends/Sensitivities
Atmospheric Variables, p (z), T (z), q (z), l (z)
z
Temp / Dew Pt
RTM
NWP Model
Ob1-Model
Radiances
Ob1-Ob2
Ob-Model stats for ranges of:
  Lat/Lon, angles, dates, radiances
Ob2-Model
Indirect Comparison via NWP model
Notes: Another method we are investigating in parallel with direct comparisons, is indirect comparisons, against a third party.

## Slide 4: How to inter-cal with RTMs?
Numerical Weather Prediction (NWP) centres routinely
  Process observations from multiple satellite instruments
  Run RTM for each observation (or a subset)
  Monitor relative differences to quality control satellite observations
  Apply empirical bias correction to ensure consistency
  Currently only for Microwave + IR channels
Calculate Double Differences
  Assumption – NWP+RTM model biases cancel out
  Limiting range of conditions to minimise variability of these biases
Also possible with other inputs – e.g. GRUAN profiles
  Higher quality control
  Higher absolute accuracy possible
  Far fewer samples

## Slide 5: Why inter-cal with RTMs?
Direct comparisons are not always possible
  Incompatible orbits
  Not simultaneous
To increase the sample size
  NWP+RTM models can generate millions of „collocations“ per day
To increase diversity of comparison – allows investigation of
  Diurnal variations
  Scan-angle dependence, etc
Work with NWP + RTM communities to understand model biases

## Slide 6: Previous GSICS work on NWP+RTM inter-cal
Had proposed a dedicated sub-group on the topic
  Dropped in favour of following it up in sub-groups
  Probably only IR and MW sub-groups at the moment
  Microwave is certainly more developed than the IR in this regard
EUMETSAT commissioned external studies:
  Can be used for tracking relative changes between instruments
  But no absolute agreement with direct inter-calibration methods

## Slide 7: Coordinating NWP+RTM method within GSICS
GSICS is about inter-calibration
  We should not get “bogged down” in RTM details
  RTMs are a tool to allow comparison of different sensors, based on double-differences.
  Key for GSICS to understand models’ relative biases and how to constrain them
  Coordinate with NWP + RTM experts to understand relative biases
Commonalities that would benefit from coordination
  Follow up in Microwave Sub-Group session – Item 6g
  Web meeting for IR Sub-Group? Guest chair?

## Slide 8: Thank you for your attention
Your thoughts?