## Slide 1: Developing GSICS products for IR channels of GEO imagers Tim Hewison
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2
GPRC | Monitored Instrument | Reference Instrument | GSICS NRT Correction | GSICS Re-Analysis Correction | GSICS Bias Monitoring
EUMETSAT | Meteosat-8-11/SEVIRI Meteosat-7/MVIRI | Metop-A/IASI | Operational Demo | Operational Demo | Plots RAC
JMA | MTSAT-2 Imager | IASI (+ AIRS) | Demo | Demo | Plots RAC
NOAA | GOES-13 & -15 Imager GOES-11 & -12 Imager | IASI (+ AIRS) | Pre-op | Pre-op Demo | Prototype
 | GOES Sounder | IASI (+ AIRS) | Development | Development | In development
CMA | FY2C – E | IASI (+ AIRS) | Development | Development | Prototype
KMA | COMS-1 | IASI | Prototype | Prototype | 
ISRO | INSAT-3D | IASI | Prototype | Prototype | 
GSICS GEO-LEO IR Product Status 2017-02
Full GSICS Product Catalog available at http://www.star.nesdis.noaa.gov/smcd/GCC/ProductCatalog.php

## Slide 3: GEO-LEO IR Issues - Prime
Combining and Transitioning Reference Sensors
  Prime GSICS Correction concept
  Based on series of double-differences
  Also good for monitoring reference sensors‘ relative calibration
  Need to include double-differences in the netCDF files!
  Need to enhance plotting tool to visualise double differences!

## Slide 4: GEO-LEO IR Issues – Incidence Angle
Meteosat-8 moved to 41.5°E
  During summer 2016
Kept fixed 21:30Z IASI overpass
  Used for 0°E SEVIRI images
  In prototype processor
  Until 2016-09-11
Fewer collocations
  More variable results
Increased incidence angle
  Changed sounding channels´ bias
  Further investigation of sensitivity?
Decontamination in Jan 2017

## Slide 5: Meteosat-7
Meteosat-7 End of Life
Long-term drift in IR channel bias
  -1.75K in 2008-06
  -3.5K in 2017-02
Prime suspect: ice contamination
  Build-up of ice layer on optics
  Absorption band ~12µm
  Modifies SRF
  Apparent bias in IR
Decontamination 2016-03
  1st since move to IODC
Sudden change in bias
  Need to reprocess!

## Slide 6: GEO-LEO IR Issues – Diurnal/Seasonal
Account for diurnal variations in GEO imagers‘ calibration
  Important issue for 3-axis stabilised platforms
  Thermal + Straylight factors
  Especially in eclipse season?
  Inadequate Midnight Black Body Correction
  Combine results from multiple reference sensors (on platforms with different equator crossing times)
  Assign different uncertainties to different times of day/season?
Are seasonal variations sufficiently accounted for in current products?
Recommendation: KMA to assess uncertainties in double differences between COMS-1/MI and IASI-A and -B (e.g. as standard error)

## Slide 7: GEO-LEO IR Issues – Cold End
Current ATBD uses linear weighted regression of collocated radiances
  Concentrate on warm end (more clear sky pixels near equator)
  Reliability of results at cold end needs further validation
  Conversion to brightness temperature amplifies errors
  Could use alternative algorithm
  E.g. Convert collocated radiance to Tb, bin, then do regression?
GIR.2016.3o.1
Arata to check how the cold end corrections are behaving using AIRS.
GIR.2016.3o.2
Arata to use the various regression methods for both radiance and brightness temperatures and process the corrections as derived from AIRS and report back.
How to follow up these activities?

## Slide 8: GEO-LEO IR Issues – New GEO imagers
New GEO imagers have new channels
Spectral coverage of reference instruments?
  Extension of gap-filling method?
Development of GSICS products?

## Slide 9: GEO Imagers Spectral Coverage
 | Meteosat/FCI |  |  | GOES-R/ABI |  |  | Himawari-8/AHI |  |  | FY-4A/AGRI |  |  | KOMPSAT-2A/AMI |  |  | INSAT-3DR/Imager |  | 
 | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax | lmin | lnom | lmax
SWIR | 3.60 | 3.80 | 4.00 | 3.80 | 3.90 | 4.00 | 3.74 | 3.85 | 3.96 | 3.50 | 3.75 | 4.00 | 3.60 | 3.85 | 4.10 | 3.80 | 3.90 | 4.00
MWIR | 5.80 | 6.30 | 6.80 | 5.70 | 6.15 | 6.60 | 6.07 | 6.25 | 6.44 | 5.80 | 6.25 | 6.70 | 5.72 | 6.24 | 6.76 |  |  | 
 | 7.10 | 7.35 | 7.60 | 6.80 | 7.00 | 7.20 | 6.89 | 6.95 | 7.01 | 6.90 | 7.10 | 7.30 | 6.70 | 6.95 | 7.20 | 6.50 | 6.80 | 7.10
 |  |  |  | 7.30 | 7.40 | 7.50 | 7.27 | 7.35 | 7.44 |  |  |  | 7.01 | 7.35 | 7.70 |  |  | 
LWIR | 8.50 | 8.70 | 8.90 | 8.30 | 8.50 | 8.70 | 8.44 | 8.60 | 8.76 | 8.00 | 8.50 | 9.00 | 8.35 | 8.60 | 8.85 |  |  | 
 | 9.51 | 9.66 | 9.81 | 9.60 | 9.70 | 9.80 | 9.54 | 9.63 | 9.72 |  |  |  | 9.39 | 9.63 | 9.87 |  |  | 
 | 10.15 | 10.50 | 10.85 | 10.05 | 10.30 | 10.55 | 10.30 | 10.45 | 10.60 | 10.30 | 10.70 | 11.10 | 9.99 | 10.43 | 10.87 | 10.30 | 10.80 | 11.30
 | 12.55 | 12.30 | 12.55 | 10.80 | 11.20 | 11.60 | 11.10 | 11.20 | 11.30 | 11.50 | 11.00 | 12.50 | 10.70 | 11.20 | 11.70 | 11.50 | 12.00 | 12.50
 | 13.00 | 13.30 | 13.60 | 11.80 | 12.30 | 12.80 | 12.20 | 12.35 | 12.50 | 13.20 | 13.50 | 13.80 | 11.69 | 12.30 | 12.92 |  |  | 
 |  |  |  | 13.00 | 13.30 | 13.60 | 13.20 | 13.30 | 13.40 |  |  |  | 12.93 | 13.30 | 13.68 |  |  | 

## Slide 10: Actions on IR Sub-Group
Action Id | Item | Effort Level | Urgency | Summary | Lead | What to Do | Expected Completion | Actual Completion | Deliverable Usage | Status
GIR.2016.3n.1 | Handling Diurnal Cycle in GEO-LEO IR |  |  | Fred to report at next meeting on cooperation with KMA on black body calibration correction. | NOAA(Fred) | Analysis | 2017-annual meeting |  |  | Pending
GIR.2016.3o.1 | v2 of GEO-LEO IR - alternative ATBDs(cold end corrections effect) |  |  | Arata to check how the cold end corrections are behaving using AIRS. | JMA(Arata) | Analysis | 2017-annual meeting |  |  | Pending
GIR.2016.3o.2 | v2 of GEO-LEO IR - alternative ATBDs (regression model and correction) |  |  | Arata to use the various regression methods for both radiance and brightness temperatures and process the corrections as derived from AIRS and report back. | JMA(Arata) | Analysis | 2017-annual meeting |  |  | Pending
Show entries
Search:

## Slide 11: IR Sub-Group Activities
GEO-LEO IR
  GEO-ring test data to support SCOPE-CM IOGEO
  Promotion of products through GPPA
  Handling GEO diurnal calibration variations
  New inter-calibration algorithms
Wed pm | GRWG: IR Sub-Group | 
 | Chair: Tim Hewison | 
13:00 | Tim Hewison | Developing GSICS products for GEO imagers
 | Fred Wu | – including diurnal cycles
 | Dohyeong Kim | – accounting for seasonal variations
 | All (incl Na Xu) | – Review Plans for GEO-LEO IR products
 | All | – new algorithms

## Slide 12
Thank You for your contributions!