## Slide 1: Update on Lunar Calibration Development
Thomas C. Stone
U.S. Geological Survey, Flagstaff, AZ USA
GSICS Joint Working Groups Meeting
Madison, Wisconsin
23 March 2017

## Slide 2: Outline
Overview of lunar calibration
Requirements for absolute lunar calibration
  the need: capabilities enabled by an absolute lunar reference
  considerations for achieving high accuracy
Recent efforts
  new measurements
  assimilating current observational datasets
Way forward

## Slide 3: Background — Overview of Lunar Calibration
At reflected solar wavelengths, the Moon can be regarded as a solar diffuser, which has exceptionally stable reflectance.
To use the Moon as a calibration reference requires an analytic model
  to predict the lunar brightness for any Moon observations made an instrument (i.e. the Sun-Moon-Observer geometry)
  the model comprises the lunar calibration reference
To build a lunar photometric model requires a large set of characterization measurements of the Moon, spanning several years
  to capture the periodic brightness variations sufficiently for modeling
  the range of available Moon views is constrained by orbital mechanics
Development of the lunar calibration system at USGS found the most useful radiometric quantity is the spatially integrated lunar irradiance.

## Slide 4: Lunar Model Development at USGS — ROLO
A dedicated ground-based telescope facility — the Robotic Lunar Observatory (ROLO):
Lunar disk reflectance model
• empirically derived formulation
• a function of only the geometric variables of phase and the lunar librations:
• located at Flagstaff, AZ 2143 m altitude
• acquired >110 000 Moon images in
32 multispectral bands
• in operation more than 8 years

## Slide 5: Lunar Irradiance Model — Operation
The fundamental model outputs (Ak) at 32 ROLO bands are fitted with a lunar reflectance spectrum, which is convolved with the instrument band spectral response functions and the solar spectrum to give the lunar irradiance (EM):
The model computations (Afit) and ΩM are for standard Sun–Moon and Moon–Observer distances of 1 AU and 384400 km
Apply distance corrections:
The final output E′M is the lunar irradiance present at the instrument location at the time of the observation, in each sensor spectral band.

## Slide 6: Requirements for Absolute Lunar Calibration
Although the ROLO/GIRO model is the most precise and reliable lunar radiometric reference available, it typically is not used for absolute calibration. Why not?
uncertainty in the model absolute scale is ~5-10%
  originates with the ROLO telescope dataset
  the main source of error is the atmospheric correction
    derived nightly from star observations, but airmass range is limited to ≤2
    applies also to Vega, which is the calibration reference for ROLO
The current absolute accuracy limitation is solely with the lunar model.
  the Moon potentially can provide an absolute calibration reference with total uncertainty under 1% (k=2)
  To achieve a high-accuracy, SI-traceable absolute lunar calibration reference requires acquisition of a new measurement database.

## Slide 7: Requirements for Absolute Lunar Calibration
Described in a CGMS Working Paper (2016)
prepared by USGS on behalf of GSICS, in response to CGMS action A43.01
provided:
  requirements for ground-based measurements
    to sample phase and libration parameters sufficiently for modeling
  requirements for above-atmosphere measurements
    to anchor the absolute scale
  formulation of the model-based lunar reference
  impacts on space-based sensor calibration
  recommendations to the CGMS
http://cgms.eumetsat.int/views/agendas.xhtml → CGMS-44 → WG II → WG II/8 → CGMS-44-GSICS-WP-01

## Slide 8: Capabilities Enabled by a High-Accuracy Lunar Reference
calibration to the same reference standard for all sensors that have viewed the Moon
  removes cross-sensor biases; facilitates inter-operability of datasets
back-calibration of data archives that contain lunar images
  Moon observations acquired in the past are valid forever. An updated lunar model can be applied to irradiance measurements for any time.
  example: geostationary meteorological imagers
    the Moon is captured in the off-Earth regions of a rectangular FOR
    potential consistent EO records extending back decades in time
ability to bridge a gap in continuous Earth observation records
  with views of the invariant Moon by instruments operating before and after the gap, the sensors can be inter-calibrated
  the accuracy of the bridge calibration depends on the accuracy of the lunar reference
transfer of pre-launch calibration to on-orbit operations

## Slide 9: Considerations for a High-Accuracy Lunar Reference
Requirements for new measurements of the Moon to use as a basis dataset for a revised lunar reference model:
Primary consideration: absolute accuracy ≤1% with SI traceability
  the potential achievable accuracy is limited only by capabilities for making calibrated measurements in the field
  some absolute measurements above the atmosphere are required
Radiometric and geometric specification of the lunar irradiance
  requires a multi-year measurement campaign, to sufficiently sample the parameter space of phase angles and lunar librations
  the availability of different Moon views is governed by celestial mechanics
Spectral specification
  the lunar reflectance spectrum is dependent on phase and on terrain type
  requires spectrally resolved measurements
      SCIAMACHY lunar observation data may be immediately useful

## Slide 10: Considerations for a High-Accuracy Lunar Reference
Polarization specification
  moonlight is polarized up to ~13%, varying widely with phase angle
      also dependent on wavelength and lunar terrain type (thus librations)
  accounting for polarization effects is essential for achieving high accuracy
      an inherent property of the Moon, thus must be part of the reference
      effects are instrument-dependent — tied to the sensor’s sensitivity
  a polarization model is needed, separate from the radiometric one
      requires collecting disk polarization measurements (basis dataset)

## Slide 11: Recent Efforts — New Lunar Measurements
NIST ground-based Lunar Spectral Irradiance (LUSI) project
  non-imaging optical system, COTS spectrometer: 390−1040 nm
  on-site calibration reference: 30 cm integrating sphere “artificial Moon”
  Mt. Hopkins, AZ: two nights in Nov. 2012 with good viewing conditions
      atmospheric correction by Langley analysis of the lunar data
      combined total uncertainty under 1% (k=1) from 400 nm to 1000 nm
  current status: NIST staff is budgeted for setup at Mauna Loa, Hawaii (3397 m alt); airborne project is funded by NASA (ER-2, 20 km alt)
C. Cramer — NIST

## Slide 12: Recent Efforts — New Lunar Measurements
China Meteorological Administration (CMA) ground-based campaign
  multiple lunar imaging and spectral instruments, 350−2500 nm
  ancillary atmospheric measurements: lidar, aerosol photometer, sounder
  3 months of dedicated acquisitions from Lijiang, Yunnan (3193 m alt)
      December 2015 to March 2016
  report from CMA: presentation 8g
China Meteorological Administration

## Slide 13: Recent Efforts — New Lunar Measurements
ARCSTONE: lunar reflectance measurements from a 6U cubesat
  project led by NASA Langley Research Center, PI: C. Lukashin
  2 non-imaging spectrometers: VNIR 350−950 nm, SWIR 900−2300 nm
  lunar disk reflectance measurements by alternating observations of the Sun and the Moon, with absolute accuracy ≤0.5% (k=1)
      using the same optics for both measurements, accommodating the ~105 intensity difference with spatial dispersion and integration times
  current status : breadboard spectrometers built, tested at NIST; March 2017 — EDU instrument development funding approved by NASA ESTO
Blue Canyon Technologies

## Slide 14: Recent Efforts — Measurements from Spacecraft
GSICS Lunar Observation Database (GLOD)
  established as part of the GIRO, with users’ agreement to contribute data
  potential to set the lunar irradiance scale with well-calibrated instruments in orbit, e.g. Aqua-MODIS, NPP-VIIRS, Landsat-8 OLI, PLEIADES
  instruments’ lunar measurements must first be validated
  example: PLEIADES (CNES)
      several intensive data collects, some with Moon views every orbit
S. Lachérade — CNES

## Slide 15: Recent Efforts — Nighttime Aerosol Photometry
aerosol Sunphotometers adapted to measure moonlight
  various instruments deployed around the world, several active research groups: AEMET (Spain), AERONET (USA), DWD (Germany), ISAC (Italy), NILU (Norway), PMOD (Switzerland), and recently ESA
  with reliable calibration of the photometers, this represents a potential extensive set of lunar irradiance measurements
    ground-based measurement, thus requires atmospheric correction
Cimel Sun/Moon photometer at ROLO site in Flagstaff (AERONET)

## Slide 16: Recent Efforts — Nighttime Aerosol Photometry
atmospheric transmission (optical depth) follows extinction law :
linear form for Langley analysis, to get cal coefficient κ and optical depth τ
  requires the exoatmospheric lunar irradiance, i.e. the ROLO reference
    varies with time ‒ phase angle and distance change with Earth rotation
  errors in V and I0 are indistinguishable in the ratio
    nighttime aerosol analysis reveals uncertainties in both quantities

## Slide 17: Way Forward
The goal is a reformulated lunar reference (model) with high accuracy and SI traceability (≤1.0% (k=2) is feasible).
near term — reprocessing the ROLO dataset
  to address observed residual geometry dependencies in the lunar model
  work in progress; subject to funding and staffing constraints
assimilating existing and current/ongoing Moon observations
  requires validating the instruments’ lunar irradiance measurements
  utilize the GLOD holdings, operational views of the Moon
collecting a new lunar measurement database
  requirements outlined in CGMS Working Paper: CGMS-44 GSICS-WP-01
    includes an above-atmosphere component
  to achieve the full potential for accuracy, must consider polarization aspects
increasing the cognizance of stakeholders to the value of a high-accuracy reference for reflective solar bands
  e.g. motivate a change in traditional thinking for algorithm development

## Slide 18
Thank You!