## Slide 1: Sensitivity of BRDF model in RTM DCC calculation
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Contents
DCC(RTM) reflectance sensitivity test
  With different BRDF (Baum and MIE)
  With different SRF (COMS and AHI)

## Slide 3: DCC(RTM) Calculation
  With different BRDF (Baum and MIE)
Observation
Model
RTM(SBDART)
Ocean BRDF
Tropical profile
Sohn, B-J., Seung-Hee Ham, Ping Yang, 2009: Possibility of the Visible-Channel Calibration Using Deep Convective Clouds Overshooting the TTL. J. Appl. Meteor. Climatol., 48, 2271~2283.
Thresholds of DCCs
(1) Cold cloud condition to select clouds overshooting tropopause layer
- TB10.8 ≤ 190K where TB10.8: Brightness Temp. at 10.8-µm band
(2) Homogeneity checks
- STD(TB10.8) ≤ 1K
- STD(R0.6)/Mean(R0.6) ≤ 0.03 where R0.6: Visible reflectance
RTM Inputs
Surface – Ocean BRDF
Atmosphere – Tropical profile
Cloud properties
- COT = 200, particle size (re) = 20 μm
Baum scattering model
MODIS Products
MODIS data
MOD021KM
COMS 0.675-μm Reflectance
COMS 10.8-μm Brightness Temperature
Simulation accuracy (COT = 200, Re = 20 μm) < 5% uncertainty
*applying MODIS visible sensor(Sohn et al, 2009)

## Slide 4: Sensitivity of reflectivity(BRF)
Albedo and BRF increase rapidly with the increase of COT ~30
The further increase in COT, BUT the slope decreases.
Sohn, B-J., Seung-Hee Ham, Ping Yang, 2009: Possibility of the Visible Channel Calibration Using Deep Convective Clouds Overshooting the TTL.
J. Appl. Meteor. Climatol., 48, 2271-2283.

## Slide 5: Sensitivity of reflectivity in COT
BRF increase with the increase of VZA
The maximum difference of BRFs up to 0.05 (COT from 100 to 200)
BRF : Bidirectional Reflectance Function
(Sohn et al., 2009)
Notes: 반사도는 VZA가 증가함에 따라 감소함.
COT 100에서 VZA의 변화(0~60도)에 따라 BRF는 0.82~1까지 변화함.

## Slide 6: Sensitivity Test()
RTM 민감도 테스트 결과 그림 3, 4
Forward scattering tend to be increased while backward scattering is decreased with respect to particle size.
Fixed cloud parameters(COT=200, =20)
(Sohn et al., 2009)

## Slide 7: Baum BRDF vs MIE BRDF
Baum BRDF
MIE BRDF

## Slide 8: BRDF comparison (Baum vs MIE)
Baum BRDF
COT(200), Re(20), SZA(30)
MIE BRDF
COT(200), Re(20), SZA(30)
Mean = 0.967
Mean = 0.931
Comparison reflectance of between Baum and Mie BRDF
COT=200, =20=30deg

## Slide 9: Radiance comparison (Baum vs MIE)
2016.08
Baum BRDF
MIE BRDF

## Slide 10: Reflectance comparison (Baum vs MIE)
2016.08
Baum BRDF
MIE BRDF

## Slide 11: BRDF comp (Baum vs MIE)
DCC calibration results
COMS_cal. vs COMS_Obs. |  | BAUM | MIE | n
Radiance | STDV | 12.522 | 15.739 | 5351
 | Mean_bias | 54.323 | 49.855 | 
Reflectance | STDV | 0.026 | 0.033 | 
 | Mean_bias | 0.152 | 0.141 | 
2016.08
 |  | BAUM | MIE | Difference
Reflectance | Mean_Cal. | 0.987 | 0.975 | 0.012
 | Mean_Obs. | 0.834 | 0.834 | 0

## Slide 12: BRDF sensitivity (Three SRFs)
SRF : Spectral Response Function
Type | Wavelength
Fixed SRF = 1 | 0.5 – 0.85
COMS SRF | 0.5 – 0.85
AHI SRF | 0.582 – 0.694
3 types of RTM SRF with BRDF model (Baum)

## Slide 13: BRDF comparison (COMS vs AHI SRF)
COMS BRDF
COT(200), Re(20), SZA(30)
AHI BRDF
COT(200), Re(20), SZA(30)
Mean = 0.967
Mean = 0.955

## Slide 14: Radiance (AHI vs COMS SRF)
Comparison radiance of between AHI SRF and COMS SRF.
Fixed COT=200, =20.
SZA
SZA

## Slide 15: Reflectance (AHI vs COMS SRF)
Comparison reflectance of between AHI SRF and COMS SRF
Fixed COT=200, =20.
SZA
SZA

## Slide 16: COMS VIS Degradation Trend
Daily mean
Monthly mean
COMS VIS degradation trend during April 1, 2011 to December 31, 2016

## Slide 17
Thank you