## Slide 1: Update on the NASA Langley Satellite Calibration SBAF Tools
Benjamin Scarino1, David R. Doelling2, Arun Gopalan1, Thad Chee1, Rajendra Bhatt1, and Conor Haney1
1SSAI, One Enterprise Pkwy Ste 200, Hampton, VA 23666 USA
2NASA Langley Research Center, 21 Langley Blvd MS 420, Hampton, VA 23681-2199 USA
                2017 GRWG/GDWG Annual Meeting
                20 - 24 March 2017 Madison, WI
                GRWG: VIS/NIR Sub-group
                Thursday, March 23rd, 14:40

## Slide 2: Outline
Purpose
Spectral Band Adjustment Factor (SBAF) [brief] review
Calibration webpage
  Highlighting the Solar Constant Comparison Tool
Tool updates
  IASI
  SCIAMACHY and introducing GOME-2
    Consistency
    Showcasing SRF and Spectra Tool
  Revisiting Hyperion
Summary and conclusions

## Slide 3: Purpose
Provided tools for use by inter-calibration developers
  GSICS deliverable
  Open sharing to benefit calibration community
Support proposed effort to provide open access SBAFs for consistent inter-satellite calibration and retrievals
Need users | Will take suggestions and adapt Spectral domains Tool features New sub-setting options Different buttons Plotting controls Uncertainty Range
Need input from instrument teams New/updated/recommended SRFs New calibration Version updates E.g., next SCIAMACHY release this year | 

## Slide 4: SBAF Review
(a) The Wherli 1985 solar irradiance spectra. (b) The SCIAMACHY reflectance spectra over DCC, clear-sky ocean, and vegetation overlaid with GOES-12 Ch1 (G12) and MODIS Band 1
Derivation of reference- and target-sensor pseudo radiance (Lp)

## Slide 5: SBAF Review
3rd-order relationship of WV channels resoled by 3rd-order SBAF application
400 – 2500 nm
240 – 1750 nm
3600 – 15500 nm
240 – 790 nm
SBAF reduces relative gain difference of multiple independent calibration methods
SBAF applicable for 0.24-2.50 μm via SCIAMACHY, Hyperion, and GOME-2
  GOME-2 affords smaller footprint from narrower spectral range
IASI covers 3.60-15.5 μm
Will also support AIRS starting this year

## Slide 6: NASA Langley Satellite Calibration Webpage
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER
https://satcorps.larc.nasa.gov

## Slide 7: Solar Constant Tool
Select any instrument visible-band SRF for convolution
Select up to 4 solar spectra from 6 options
Plot provides image of SRF relative response and solar irradiance relative to wavelength
Table reveals the SRF convolution of flux, irradiance, and radiance for the chosen solar spectra(s)

## Slide 8: NASA Langley Satellite Calibration Webpage
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER
https://satcorps.larc.nasa.gov

## Slide 9: IASI-based IR SBAF Tool Update
Available spectral domains and selection features as shown
Current user request for land/water mask
Recently implemented user requests for 11-μm BT subsetting, and wavelength cutoff for spectral convolution

## Slide 10: IASI-based IR SBAF Tool Update
Users conducting Overshooting Convective Top studies found it helpful to construct piece-wise SBAFs using limited ranges of 11-μm BT
Works for any channel SBAF, not just 11-μm

## Slide 11: IASI-based IR SBAF Tool Update
A user suspected SBAF uncertainty was caused by CO2 absorption band just beyond 4.0 μm
Intend to enable means simple spectral absorption band analysis

## Slide 12: SCIAMACHY-based Visible SBAF Tool Update
Available spectral domains and selection features as shown
A current request for enhanced interfacing capabilities, i.e., run-time/real-time automation, script-driven production
  Security considerations
Land-use community user recently requested clear-sky IGBP-specific subsetting
  Probably better served by GOME-2
User-controlled outlier filtering

## Slide 13: GOME-2-based Visible SBAF Tool Introduction [In Development]
Currently based on 1 month of data (July 2008)
Will support full record as year continues
Live for 18 IGBP Land Classification types (clear sky)
  Better sampled than can be accomplished with SCIAMACHY footprints

## Slide 14: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
8 years of SCIAMACHY vs. 1 month of GOME-2, and the ability to sample a properly-represented Wetlands scene ID

## Slide 15: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
GOME-2-based SBAFs over Barren land (IGBP=16) suggest a 0.2% spectral disparity between the above SRFs
SCIAMACHY-based SBAFs suggest no spectral correction necessary

## Slide 16: Spectral Response Function Comparison Tool
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER
A fair SBAF comparison should have have adequate sampling from each instrument, with comparable viewing/solar geometry
Preferable to use a PICS
Otherwise can get significant SBAF difference for a more disparate SRF pairing

## Slide 17: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
A fair SBAF comparison should have have adequate sampling from each instrument, with comparable viewing/solar geometry
Preferable to use a PICS
Otherwise can get significant SBAF difference for a more disparate SRF pairing

## Slide 18: Spectral Response Function Comparison Tool
For example, VIIRS I1 vs. M5 Band
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER

## Slide 19: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
SBAFs inconsistent for disparate bands
Some difference could be owed to seasonal/regional/anisotropic effects

## Slide 20: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
Best effort can be made to pick similar view/illumination angle allowances, season, and domain
Won’t account for specific SZA difference
Note: Will not be an adequate imitation of a simultaneous, co-located comparison

## Slide 21: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
Likely that agreement is highly dependent on scene homogeneity
SCIAMACHY may miss small clouds
GOME-2 perhaps more accurately distinguishing spectra of bare rock vs. soil vs. sand, whereas SCIAMACHY may represent more of an average

## Slide 22: SCIAMACHY and GOME-2 Clear-sky IGBP Scene Spectra
Other scene types suggest better consistency for same disparate SRFs
Again, conclusions about consistency are best afforded from formal PICS study
Bottom line: Attempt to best match scene conditions of one’s calibration approach

## Slide 23: SCIAMACHY Spectra Plotting Tool
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER
Mean radiance/reflectance spectra and standard deviation available for all SCIAMACHY Earth targets.

## Slide 24: Hyperion-based Visible SBAF Tool Update
Map displays entire record of Hyperion ground measurements

## Slide 25: Hyperion-based Visible SBAF Tool Update
Map displays entire record of Hyperion ground measurements
Grey → black = low → high density
Irregular distribution due to nature of tasked retrieval

## Slide 26: Hyperion-based Visible SBAF Tool Update
Map displays entire record of Hyperion ground measurements
Grey → black = low → high density
Irregular distribution due to nature of tasked retrieval
Enter coordinates for area of interest, or simply ‘shift+click+drag’

## Slide 27: Hyperion-based Visible SBAF Tool Update
Map displays entire record of Hyperion ground measurements
Grey → black = low → high density
Irregular distribution due to nature of tasked retrieval
Enter coordinates for area of interest, or simply ‘shift+click+drag’

## Slide 28: Summary and Conclusions
Providing support for calibration community and developers with open access SBAFs for consistent inter-satellite calibration and retrievals
  Want to work with instrument teams to showcase highest-quality data and latest SRFs
  Feedback, suggestions, and requests
Will integrate full record of GOME-2, introduce AIRS
Update on the NASA Langley Satellite Calibration SBAF Tools
Benjamin Scarino
benjamin.r.scarino@nasa.gov