## Slide 1
Action: Determine Feasibility of Extracting Inter-Calibration Algorithm and Coefficients
GSICS MW Subgroup/Topical Area: LUT/Correction Tables
Notes: Mitch provided long time support for project from the program side, such as leveraging funding.
And Fuzhong also provides program support and coordinate the CRTM team to work with our product development team. You may notice that most of my SDS science team members are from his Branch.
I also want to thank Changyong for his long time support from scince side. I can always count on his support when I need a discussion on science. even when I need support from his team members.

## Slide 2
MSU/AMSU-A
Digital Counts (C)
Radiance (R)
(Cc , 2.73K)
(Cw, Rw)
(Ce, RL)
(Ce, Re)
RL is the linear calibration term
Nonlinear Calibration: one set of calibration coefficients for all scan positions
S
Slope
mZ
{
Z is the quadratic nonlinear term
Baseline Calibration Algorithms
Notes: It is a design goal to make the calibration as linear as possible. If the calibration is linear, then the two calibration points will uniquely determine a linear calibration equation, where the earth scene radiance can be obtained as linear interpolation from the two calibration points. This is shown by the straight line in this plot. However, in reality, the MSU instrument contains a week quadratic nonlinear term, and the final equation looks like this. The nonlinearity is measured by this nonlinear coefficient MU.

## Slide 3
k j
SNO Algorithm to Determine Inter-Calibration Coefficients
Radiance Error Model for SNO Matchup K and J :
Calibration Equation for each pixel of the SNO Matchup K and J :
Subtracting the above equations gives the Error Model for
the satellite SNO pair K and J
Minimizing the errors in the SNO matchups results
in optimized inter-calibration coefficients
Reference satellites are NOAA -10 for MSU and NOAA-15 for
most AMSU-A channels
Notes: To obtain the coefficients, we establish a radiance error model for the SNO matchup, say satellite k and j. The calibration equation for each satellite is like this, when you subtract them from each other, you obtain the error model like this. Here the Z terms and delta Rl are measured variables, the E are error residual term related to the spatial and time differences in the SNO matchup datasets. Using some statistical chracteristics, this E term can be ignored here. Then we can use regressions to obtain the calibration coefficients. When we do regression, we need to consider the colinearity between the nonlinear terms for the SNO matchups. As a mater of fact, we find there is a high degree of colinearity between satellite pairs for the Z terms. This plot gives you an example for NOAA 11 and 10, here the correlation of the Z terms reach as high as 0.95. So the colinearity equation is part of the regression model, which serves to reduce the independent variables in the regression.

## Slide 4: Calibration Coefficients from SNO Approach
Calibration coefficients are a set of fixed parameters obtained from SNOs (Zou et al. 2006, 2009, Zou and Wang 2011)
: constant offset
k : rate of changes in the offset
: constant non-linear coefficient
l: the rate of changes of the
non-linear coefficient
Inter-calibration coefficients for all other MSU/AMSU temperature sounding channels can be found at
https://www.star.nesdis.noaa.gov/smcd/emb/mscat/algorithm.php
https://www1.ncdc.noaa.gov/pub/data/sds/cdr/CDRs/AMSU%20Brightness%20Temperatures/AlgorithmDescription_01B-18_18a.pdf
Inter-calibration coefficients description
Example of Inter-calibration coefficients
Notes: Mitch provided long time support for project from the program side, such as leveraging funding.
And Fuzhong also provides program support and coordinate the CRTM team to work with our product development team. You may notice that most of my SDS science team members are from his Branch.

## Slide 5
CM SAF // SSM/I, SSMIS
Prerequisites for inter-calibration
Inter-calibration coefficients depend on Antenna Pattern Correction (TATB)
  APC procedures and coefficients must be provided together with inter-calibration algorithm and coefficients
SSMIS F16 and F17 affected by an emissive reflector
  emissivity and algorithm or offsets must also be provided
SSM/I and SSMIS are affected by sunlight and moonlight intrusions
  these offsets should also be provided (as lookup table)
How can this extra information be provided for a GSICS product?
  Additional data layer(s) or algorithms plus coefficients?
Inter-calibration offsets without these corrections are not useful and applying them by the users will be more complicated than just using the FCDR as it is.
Notes: It is a design goal to make the calibration as linear as possible. If the calibration is linear, then the two calibration points will uniquely determine a linear calibration equation, where the earth scene radiance can be obtained as linear interpolation from the two calibration points. This is shown by the straight line in this plot. However, in reality, the MSU instrument contains a week quadratic nonlinear term, and the final equation looks like this. The nonlinearity is measured by this nonlinear coefficient MU.

## Slide 6
CM SAF // SSM/I, SSMIS
Inter-calibration model
Reference instrument SSM/I onboard DMSP-F11
Using the Earth as vicarious inter-calibration target for scene-dependent inter-calibration
Ocean as cold end target
Land as warm end target, but restricted to depolarised scenes as double differences to remove diurnal cycle variations
Limited simultaneous overpasses  use monthly gridded TBs to derive inter-calibration coefficients
Inter-calibration Model includes non-linearity calibration coefficient d, scene dependent scale factor a, offset b, and cross-polarization factor c
Coefficients applied in a 2-step process:
Notes: It is a design goal to make the calibration as linear as possible. If the calibration is linear, then the two calibration points will uniquely determine a linear calibration equation, where the earth scene radiance can be obtained as linear interpolation from the two calibration points. This is shown by the straight line in this plot. However, in reality, the MSU instrument contains a week quadratic nonlinear term, and the final equation looks like this. The nonlinearity is measured by this nonlinear coefficient MU.

## Slide 7
CM SAF // SSM/I, SSMIS
Availability
Inter-calibration coefficients are fixed parameters and are currently available on request
FCDR contains original TB with all corrections applied plus extra data layer as Inter-calibration offset
Complete FCDR documented as per sensor ATBD and Product User Manual, plus Validation Report
DOI:10.5676/EUM_SAF_CM/FCDR_MWI/V003
Notes: It is a design goal to make the calibration as linear as possible. If the calibration is linear, then the two calibration points will uniquely determine a linear calibration equation, where the earth scene radiance can be obtained as linear interpolation from the two calibration points. This is shown by the straight line in this plot. However, in reality, the MSU instrument contains a week quadratic nonlinear term, and the final equation looks like this. The nonlinearity is measured by this nonlinear coefficient MU.