## Slide 1: Lunar Dataset Cataloging
Fangfang Yu1 and Xiangqian Wu2
1: ERT, Inc@NOAA/NESDIS/STAR
2: NOAA/NESDIS/Center for Satellite Application and Research (STAR)

## Slide 2: Outlines
Outcome of the data survey from 1st workshop
New data survey for 2nd workshop
  Goal
    Irradiance
    New applications
  New data
    New satellite instruments
    Ground measurements
    Expansion from radiometric calibration of VNIR wavelength
Feedbacks
  GEO: GOES-16/ABI, Himawari-8/AHI, COMS/MI, FY2-VISSR
  LEO: GCOM-C/SGLI, Terra/ASTER, MERBE, NOAA and Metop MHS
  Ground: NIST

## Slide 3: Objectives of New Data Survey
Collect information of new lunar observation data since after 1st workshop at Darmstadt, Germany in December 2014
  GIRO irradiance model as a common reference physical model for inter-calibration
Collect data to work on common method for the new applications of the Moon in VNIR bands
  MTF
  Radiance model
Other new applications of the Moon

## Slide 4: Outcome of the Data Survey from 1st Workshop
Courtesy of Fougnie, B.

## Slide 5: Data Survey Contents
General description of the satellite (orbit, mission duration, etc.)
General description of the sensor (spectral bands, spatial resolution, quantization, etc.)
Calibration method
  reference/document, if available
Lunar observations (or in plan)
  Description of the Moon acquisition (Maneuver)
  Phase angle range
  Sample images
  Sample data (including the observation time) and data accessibility (GLOD, public available?)
  Image processing procedure to derive smoothly edged moon or actual physical lunar images, if any
Lunar irradiation calculation (or in plan)
  Integration step
  Dark signal handling
  Oversampling consideration

## Slide 6: GOES-16
First NOAA Geostationary Operational Environmental satellite in the GOES-R Series
  Launched on November 19, 2016
  Key payload: Advanced Baseline Imager (ABI)
  Locations:
    Parked at 89.5W for PLT/PLPT tests.
    Moved from 89.5W to 89.3W between August 8, 2017 and Sept. 3, 2017.
    Plan to move from 89.3W to 75.2W for operation in December 2017.

## Slide 7: GOES-16 ABI
GOES-16 ABI SRF: https://ncc.nesdis.noaa.gov/GOESR/ABI.php
GOES-16 ABI MTF: to be presented in the coming 2nd workshop
ABI Band | Wavelength range (µm) | Central Wavelength (µm) | Angular Sample Distance (µrad) | Nominal earth image resolution (km) | Bit Depth
1 | 0.45-0.49 | 0.47 | 22x22.9 | 1 | 12
2 | 0.59-0.69 | 0.64 | 11x10.5 | 0.5 | 12
3 | 0.846-0.885 | 0.865 | 22x22.9 | 1 | 12
4 | 1.371-1.386 | 1.378 | 44x42 | 2 | 12
5 | 1.58-1.64 | 1.61 | 22x22.9 | 1 | 12
6 | 2.225-2.275 | 2.25 | 44x42 | 2 | 12
7 | 3.80-4.00 | 3.90 | 44x44.7 | 2 | 14
8 | 5.77-6.6 | 6.19 | 44x44.7 | 2 | 12
9 | 6.75-7.15 | 6.95 | 44x44.7 | 2 | 12
10 | 7.24-7.44 | 7.34 | 44x44.7 | 2 | 12
11 | 8.3-8.7 | 8.5 | 44x44.7 | 2 | 12
12 | 9.42-9.8 | 9.61 | 44x44.7 | 2 | 12
13 | 10.1-10.6 | 10.35 | 44x38.1 | 2 | 12
14 | 10.8-11.6 | 11.2 | 44x38.1 | 2 | 12
15 | 11.8-12.8 | 12.3 | 44x38.1 | 2 | 12
16 | 13.0-13.6 | 13.3 | 44x38.1 | 2 | 12

## Slide 8: GOES-16 ABI VNIR Band Calibration
Two-point on-orbit calibration targets:
  Spectralon Solar Diffuser
  Deep space
Quadratic detector responsivity correction
  Quadratic term (q) determined on-ground
Dalta et al. 2016, Comparison of the calibration algorithms and SI Traceability of MODIS, VIIRS, GOES and GOES-R ABI Sensors, Remote Sensing, 8(126), doi:10.3390/rs8020126, http://www.mdpi.com/2072-4292/8/2/126

## Slide 9: Moon Observations from GOES-16 ABI
Tracing or trending the Moon when the Moon transits across the ABI Field of Regard
Phase angle range: -90o – 90o
L1alpha data in netCDF format available at NOAA/CLASS
To be provided to GLOD
Earth

## Slide 10
B1 (047)
B2 (064)
B3 (087)
B4 (138)
B5 (161)
B6 (225)
ABI Lunar Images, Radiometrically Calibrated …

## Slide 11
B1 (047)
B2 (064)
B3 (087)
B4 (138)
B5 (161)
B6 (225)
… and Aligned with Relative Detector Position RDP)

## Slide 12: Irradiance Calculation
Irradiance:
Ω: Sample solid angle
Radiancei,j : calibrated radiance at (i,j) image coordinate
Calculations of the measured and physical areal sizes of the Moon, and estimation of the oversampling factor for the ABI-like instruments will be presented and discussed during the workshop on Nov. 14 (#2m)

## Slide 13: New Data Set for Solar Reflective Wavelengths

## Slide 14: Application in New Wavelength
Chair of MW GRWG sub-group encourages introducing MHS and planned ground observations provided by Dr. Burgdorf as the first cases in this workshop
MHS Lunar observations
  Moon appears in deep space view in certain months
  Narrow phase angle range (Phase angle >90o) for given local equator crossing time of satellite
  “Light curve” can be fitted with Gaussian
  Particularly suited for checks of inter-channel uniformity and photometric stability, since flux differences easier measured than absolute level
  Also useful for determination of pointing accuracy for sounding channels, because they cannot see Earth’s surface (Bonsignori 2017)
Model (Mo & Kigawa, 2007) of brightness temperature of Moon gives maximum values at full moon, independent of frequency
  Improvement requires observations over large range of phase angles
  All phase angles available with observations from ground
  Test observations planned with Swedish Kiruna Millimeter Wave Radiometer
- Courtesy of M. Burgdorf

## Slide 15: Summary
New high quality lunar observation data to enrich the data collection for calibration purpose
  Two new next-generation GEO satellite instruments
  More high spatial observations of the Moon
  New observation schemes of GEO and LEO instruments
Extension from multiple to hyperspectral measurements
Extension from spacecraft to ground
SI-traceable measurements
New uses of the Moon
  Common MTF method
  Radiance model
  Microwave calibration

## Slide 16: Discussions
Mistakes in the data presented?
  …
Missing instrument / dataset?
  …
Desirable information that may be available?
  BRDF for radiance calibration
    Merging AHI/ABI/AMI
    Other data?
    …
  …
…