## Slide 1: Lunar data preparation for PROBA-V
Stefan Adriaensen (VITO)
2nd GSICS/CEOS Lunar Calibration Workshop, Xi’an, China 13/11/20117 – 16/11/20117

## Slide 2: PROBA-V instrument
No active thermal control
No on-board calibration lamp
No solar diffuser
Design complexity
  3 Cameras
  2 focal planes:
    VNIR with 3 bands
    SWIR with 1 band but staggered strips

## Slide 3: PROBA-V Calibration
Absolute
Interband
Oceans
Deserts
DC Clouds
Antarctica
Greenland
Inter-pixel
Temporal
*Sterckx et al. IJRS, 2014; Sterckx et al. , TGARS, 2013; Govaerts et al., RSL, 2013
OSCAR* (Optical Sensor Calibration with simulated Radiances)
Relies on combination of various vicarious calibration methods to reduce uncertainty in the calibration results and to verify the different requirements
Yaw steering maneuver

## Slide 4: Moon Maneuver
Only center camera is considered
7 degrees phase before and after full moon
360 degrees pitch at 0.2deg/s
every band has different view angle
24.5 seconds between swir and nir
lunar scan takes about 2.6 seconds
moon
swir
blue
red
nir

## Slide 5: Processing steps
Input L1A
Extract
Radiance
Masking
Geometry
Total Irradiance
band

## Slide 6: L1A extraction
HDF5 file format : convert to image files (DN)
extract platform line data : line time and satellite position,integration time
SWIR
VNIR

## Slide 7: Conversion to Radiance
based on vicarious calibration techniques
radiometric model :
dark current calibrated using nightly ocean scenes every month
background radiance observed in the image is close to zero( <0.6% of avg moon pixel)

## Slide 8: Masking
threshold
Center of observation timestamp
Pixel solid angle
Radiance image
Mask
Satellite position
5% of max
radiance

## Slide 9: Number of selected pixels vs moon obs distance

## Slide 10: Solid angle
the pixel solid angle is calculated directly from the data
Pixel along track angle =
rotational_speed * (t_max - t_min) / nr_of_lines
Pixel across track angle =
( 2 * atan (moon_eq_radius / distance obs_moon) ) / nr_of_columns
Solid angle includes oversampling factor
Orientation of the moon in the image is currently neglected

## Slide 11: Provided to GLOD
basic processing is performed per observation :
    timestamp
    satellite position
    total irradiance
      recently updated +100 observations
      no imagettes have been included to GLOD

## Slide 12: Results : BLUE

## Slide 13: Results : RED

## Slide 14: Results : NIR

## Slide 15: Conclusions
PROBA-V data has been processed and compared with GIRO successfully
update current PROBA-V GLOD dataset is required
better performance might be achieved (cfr. orientation of the moon )
SWIR processing needs full review