## Slide 1
Lunar Data Preparation for
Himawari-8/-9 AHI
Masaya Takahashi
Meteorological Satellite Center
Japan Meteorological Agency
2nd GSICS/CEOS Lunar Calibration Workshop, 13-16 November, Xi’an, China

## Slide 2: Contents
Overview
  Mission Life Time, Sensor Configuration/Characteristics
  Himawari-8/-9 AHI Lunar Observation
Computation of Observed Lunar Irradiance
  Oversampling, Pixel IFoV, Radiance Calculation, Moon Pixel Selection
  Preliminary Lunar Calibration Results
Summary and Future Plans

## Slide 3: Mission Overview
Himawari-8
  Advanced Himawari Imager (AHI): next-gen. GEO imager w/ 3 VIS, 3 NIR, 10 IR bands
  Solar diffuser is equipped for VNIR calibration (but w/o SDSM)
  Full-disk observation every 10 minutes + 5 regional observations every 2.5/0.5 minutes
  Has been operational since July 2015, located at ~140.7 E
Himawari-9
  Launched on 2 Nov. 2016, Located at ~140.7 E, ~0.1 degrees apart from Himawari-8
  10 Mar. 2017: the satellite was put into in-orbit standby as back up for Himawari-8
  “Health Check” observations are periodically (~2 weeks, a few times / year) performed before the switchover in 2022
FY 2010 2015 2017 2020 2025 2029

## Slide 4: Himawari-8/-9 AHI
Wavelength [μm]
Wavelength [μm]
Spectral Response Functions of Himawari-8/AHI, GOES-16/ABI and Meteosat-10/SEVIRI
 | B01 | B02 | B03 | B04 | B05 | B06 | B07 | B08 | B09 | B10 | B11 | B12 | B13 | B14 | B15 | B16
Central Wlen [μm] | 0.47 | 0.51 | 0.64 | 0.86 | 1.6 | 2.3 | 3.9 | 6.2 | 6.9 | 7.3 | 8.6 | 9.6 | 10.4 | 11.2 | 12.4 | 13.3
Spatial Reso. [km] | 1 | 1 | 0.5 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
# of detectors | 676 | 676 | 1460 | 676 | 372 | 327 | 332 | 332 | 332 | 332 | 332 | 332 | 408 | 408 | 408 | 408
AHI Band Configuration

## Slide 5: Himawari-8/-9 AHI Lunar Observation
Lunar observation: based on the prediction of its position within AHI’s Field of Regard
Regional observation mode (1000 x 500 km for the earth scene) is used
1 observation / 30 seconds
Just one scan to observe the Moon
All 6 VNIR bands (0.47, 0.51, 0.64, 0.86, 1.6, 2.3 µm) are used for GIRO
Earth disk
AHI FoR
Himawari-8/AHI
(4 Mar. 2015 – 30 Oct. 2016)
26167 Obs. / 20 months

## Slide 6
Region 4, 5: mainly used for landmark observation, but region 5 is also used for lunar observation
Full Disk Observation
every 10 min. (23 swaths)
Region 1
2000 x 1000km
(NE Japan)
Every 2.5 min.
Region 2
2000 x 1000km
(SW Japan)
Every 2.5 min.
Region 3
1000 x 1000 km
(Target Area)
Every 2.5 min.
Region 4
1000 x 500 km
(Landmark Area)
Every 30 sec.
Region 5
1000 x 500 km
(Landmark Area)
Every 30 sec.
Pre-defined area
Flexible observation area
AHI FoR
Earth edge
Lunar observations
Band5 (1.6μm)
Full Disk / Regional Observation in 10 minutes Repeat Cycle

## Slide 7: Himawari-8/AHI Lunar Observations

## Slide 8: Oversampling, Pixel Solid Angle
Oversampling factor
N-S IFoV / N-S Sampling Distance
No E-W oversampling is assumed because E-W IFoV < E-W Sampling Distance
Pixel solid angle
E-W Sampling Distance * N-S IFoV
Both oversampling/Pixel IFoV: assumed to be constant
Future plans
Revisit of the definition of oversampling factor and pixel solid angle
Under-discussion within NOAA-JMA bilateral collaboration on ABI/AHI Cal/INR
Calculation of alternative factor (e.g. effective moon solid angle (Choi et al. 2016))
Validation of the pre-launch determined IFoV using on-orbit observation data

## Slide 9: Radiance
Level of image processing
Level 1A/1.0 equivalent data
Calibration used to convert DN to radiance
Quadratic calibration equation
Quadratic term: pre-launch determined value
Slope: solar diffuser / pre-launch determined value
Offset: deep space observation (updated at each full-disk swath / each lunar obs.)
Handling extraneous signals
Out-of-Filed Anomalous Response (OFAR, Griffith 2017)
Appears in Band 1 -3 (0.47, 0.51 and 0.64 μm)
P. Griffith, 2017: Himawari08 Out-of-Field Anomalous Response (OFAR), 8th Asia/Oceania Meteorological Satellite Users’ Conference, 18 - 20 October 2017, Vladivostok, Russia.

## Slide 10: Moon Pixel Selection
Enhanced Himawari-8/AHI lunar observation image (color scale: 0.1 – 30 % of reflectivity)
Band1 (0.47 μm) Band2 (0.51 μm) Band3 (0.64 μm) Band4 (0.86 μm)
19 August 2016
Based on DC thresholds
Needs to discriminate the Moon and Out-of-Field Anomalous Response (Griffith 2017)
OFAR: blurring occurs in Bands 1-3 (0.47, 0.51, 0.64 μm) which use silicon detectors
No effect in other bands which use HgCdTe detectors
Appears west of the Moon under the current observation configuration
GOES-R/ABI and GK-2A/AMI are unaffected by OFAR

## Slide 11
Moon Pixel Selection using Connected-component Labeling
DC threshold + Connected-component Labeling method is used
Connected-component Labeling method
Assign the same number (label) to adjacent pixels which exceed the threshold (e.g. DC=25)
Choose the label w/ the biggest # of pixels as the Moon pixels
Effectively distinct OFAR for positive lunar phase angles, but difficult for negative phase angles
Labelled pixels
Selected Moon pixels
Phase angle: -28.2 deg.

## Slide 12
Impacts of Moon-masking DC Threshold on Lunar Calibration
ΔIrr (%)
ΔIrr (%)
Lunar phase angle [deg]
Color: lunar phase angle [deg]
Initially, large DC thresholds (=35) were used to screen out pixels affected by OFAR
Deep space counts: ~20
Loss of dark pixels on the Moon -> incorrect phase angle dependence in AHI/GIRO (ΔIrr)
Difference of lunar irradiance between the observation and GIRO [%]
Band3 (0.64 μm)
Band3 (0.64 μm)

## Slide 13
AHI lunar irradiance vs. GIRO
ΔIrr (%)
ΔIrr (%)
Lunar phase angle [deg]
Color: lunar phase angle [deg]
DC threshold (=25) + Connected-component Labeling approach for the Moon masking
Unexpected phase angle dependence exists
Further lower DC threshold (~20) should be ideally used
Nonlinearity in AHI ? - to be investigated
Band3 (0.64 μm)
Band3 (0.64 μm)
Difference of lunar irradiance between the observation and GIRO [%]
Sub-sampled lunar observations (#439) are shown
ΔIrr is normalized by ΔIrr (t=0; 2015-06-08)
Calibration slope from solar diffuser obs. (mean of Mar-May 2015 results) is used for all the lunar obs.
Notes:

## Slide 14: Summary and Future Plans
Himawari-8/-9 AHI lunar observation
  6 VNIR bands (0.47, 0.51, 0.64, 0.86, 1.6, 2.3 μm)
  Available since March 2015 (Himawari-8)
  Himawari-9/AHI lunar observation: the quality is under checking
AHI lunar calibration
Revisit of oversampling / pixel IFoV is needed in collaboration w/ NOAA
Moon pixel selection should be updated (e.g. use of further lower DC threshold and lunar shape fitting)
Root cause of phase angle dependence in band 1-3 needs to be investigated
Himawari-8/AHI lunar observation data for GLOD
500-1000 lunar observation data are planned to be shared
Contents (e.g. observed lunar irradiance) will be periodically updated

## Slide 15
Thanks for your attention!

## Slide 16
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
2 12 22 32 42 52 62 72 82 92
Phase angle [deg]
Difference of lunar irradiance between the observation and GIRO [%]
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
ΔIrr (%)
ΔIrr (%)
Moon pixel selection
Larger DC threshold (=30)
Sensor degradation trend
Good agreements with other Cal/Val approaches
Time Series of ΔIrr of Himawari-8/AHI

## Slide 17: Time Series of ΔIrr of Himawari-8/AHI
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
2 12 22 32 42 52 62 72 82 92
Phase angle [deg]
Difference of lunar irradiance between the observation and GIRO [%]
Moon pixel selection
Lower DC threshold (=25) + Connected-component labeling
Sensor degradation trend
Good agreements with other Cal/Val approaches
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
ΔIrr (%)
ΔIrr (%)

## Slide 18
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
Himawari-8/AHI lunar phase angle dependence in ΔIrr
ΔIrr (%)
Difference of lunar irradiance between the observation and GIRO [%]
ΔIrr (%)
Lunar phase angle [deg]
Lunar phase angle [deg]
Lunar phase angle [deg]
MSG1/SEVIRI NIR1.6
MSG1/SEVIRI VIS 0.6
SEVIRI results from B. Viticchie at the Lunar Calibration Workshop in Dec. 2014
Good agreement with SEVIRI NIR1.6, but not with SEVIRI VIS 0.6
Moon pixel selection w/ larger DC threshold (~30)

## Slide 19
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
Himawari-8/AHI lunar phase angle dependence in ΔIrr
ΔIrr (%)
Difference of lunar irradiance between the observation and GIRO [%]
ΔIrr (%)
Lunar phase angle [deg]
Lunar phase angle [deg]
Lunar phase angle [deg]
MSG1/SEVIRI NIR1.6
MSG1/SEVIRI VIS 0.6
SEVIRI results from B. Viticchie at the Lunar Calibration Workshop in Dec. 2014
Good agreement with SEVIRI NIR1.6, but not with SEVIRI VIS 0.6
Moon pixel selection w/ lower DC threshold (=25) + Connected-component labeling

## Slide 20: JMA geostationary satellites
GMS (Geostationary Meteorological Satellite)
MTSAT (Multi-functional Transport SATellite )
Back-up operation of GMS-5 w/ GOES-9 by NOAA/NESDIS:
2003/05/22-2005/06/28
(GOES-9)
Aug 1981
GMS-2
(Himawari-2)
Aug 1984
GMS-3
(Himawari-3)
Sep 1989
GMS-4
(Himawari-4)
Mar 1995
GMS-5
(Himawari-5)
Feb 2005
MTSAT-1R
(Himawari-6)
Feb 2006
MTSAT-2
(Himawari-7)
Jul 1977
GMS
(Himawari)
Himawari
2014
Himawari-8
2016
Himawari-9
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸSS/L
ⒸMELCO
Satellite | Operation period
GMS | 1978 – 1981
GMS-2 | 1981 – 1984
GMS-3 | 1984 – 1989
GMS-4 | 1989 – 1995
GMS-5 | 1995 – 2003
GOES-9 | 2003 – 2005
MTSAT-1R | 2005 – 2010
MTSAT-2 | 2010 – 2015
Himawari-8 | 2015 – 2022
Himawari-9 | 2022 – 2029
launched on 7 Oct. 2014
Operation started on 7 July 2015
launched on 2 November 2016
Planned to be back up of Himawari-8 in March 2017

## Slide 21: Advanced Himawari Imager (AHI)
Band | Central Wavelength [μm] | Spatial Resolution [km] | # of detectors (*) | Levels of digital count [bit]
1 | 0.47 | 1 | 676 (3) | 11
2 | 0.51 | 1 | 676 (3) | 11
3 | 0.64 | 0.5 | 1460 (3) | 11
4 | 0.86 | 1 | 676 (6) | 11
5 | 1.6 | 2 | 372 (6) | 11
6 | 2.3 | 2 | 372 (6) | 11
7 | 3.9 | 2 | 332 (6) | 14
8 | 6.2 | 2 | 332 (6) | 11
9 | 6.9 | 2 | 332 (6) | 11
10 | 7.3 | 2 | 332 (6) | 12
11 | 8.6 | 2 | 332 (6) | 12
12 | 9.6 | 2 | 332 (6) | 12
13 | 10.4 | 2 | 408 (6) | 12
14 | 11.2 | 2 | 408 (6) | 12
15 | 12.4 | 2 | 408 (6) | 12
16 | 13.3 | 2 | 408 (6) | 11
AHI Field of View Center (VNIR)
ITT EXELIS(2013): AHI-8 EQUIPMENT MANUAL 2
CALIBRATION AND ALIGNMENT HANDBOOK Rev. J
*Number of redundant detector columns per side

## Slide 22: Typical Observation Schedule in 10 minutes Repeat Cycle
[sec]
Full Disk | Region 1 (NE Japan)
BB Obs. | Region 2 (SW Japan)
Space Look | Region 3 (Target Area)
 | Region 4 (Landmark Area)
 | Region 5 (Landmark Area)
Blackbody Obs.
[sec]

## Slide 23: VIS/NIR on-board Calibration using Solar Diffuser (SD)
Quadratic calibration equation in “L1A (L1.0) equivalent data” processing
Robsn: Observed radiance
CAn: Raw digital count
Cspn: Deep space raw digital count
qn, mn: Coefficients
n: Detector ID
r : Scan mirror reflection coef.
q, f : Incidence angle to SM
qn: pre-launch test value
mn:
Pre-launch test value (until 7 June 2015)
Values based on solar diffuser (SD) observations (since 8 June 2015). SD observation is performed every 2 weeks
Csp: updated by deep space observation at each Full-disk swath
aa

## Slide 24: VNIR Calibration Slopes derived from Solar Diffuser (SD) observations
SD observation: performed twice / month
June 2015: VNIR calibration slopes in L1 data were updated using Mar-May 2015 SD obs.
~0.5% degradation trends in Band1-4 (no SD degradation is assumed)
Time series of inverse of detector-averaged calibration slope from SD observations
Band1 Band2 Band3
(0.47μm) (0.51μm) (0.64μm)
Band4 Band6
(0.86μm) (2.3μm)
Band5
(1.6μm)

## Slide 25: Validation of On-board Calibration Slope
Band1 (0.47μm) Band2 (0.51μm) Band3 (0.64μm)
Band4 (0.86μm) Band5 (1.6μm) Band6 (2.3μm)
Updates of Cal. slope
Error bar: stdv. of slopes
~0.5%/year of degradation trends in Band1-4
~6% bias for Band5, ~4 % bias for Band6 based on ray-matching validation
Time series of ratios between Himawari-8/AHI observations and reference values

## Slide 26: Validation of On-board Calibration Method 1) Vicarious Calibration using RT Simulation
Comparison of observed and simulated radiance for multiple targets (collaboration research with the University of Tokyo and JAXA/EORC [Prof. Nakajima])
Targets:
Cloud-free ocean (rayleigh scattering) , liquid water cloud, *cloud-free land and *deep convective cloud
Radiative transfer calculation:
RSTAR (Nakajima and Tanaka [1986,1988])
Input data: Independent from GEO data
JMA Re-Analysis atmos. profiles (JRA-55/JCDAS)
Aerosol/Cloud optical thickness retrieved from MODIS L1B (M[O,Y]D02SSH)
MODIS BRDF (MCD43C2) for land target
Aura/OMI total column ozone, …
August 2015
Simulated reflectivity
Observed reflectivity
*Not implemented for Himawari-8/-9 AHI as of June 2017

## Slide 27
Inter-calibration based on AHI-VIIRS collocation (Quasi-SNO)
Calibration target: cloud pixels
Low radiance scene (e.g. cloud-free ocean) : not used
Spectral Band Adjustment Factor (SBAF) accounting for the spectral mismatch
Band1-5: from NASA Langley SBAF based on SCHIAMACHY (http://cloudsgate2.larc.nasa.gov/SBAF)
Band6: computed using RSTAR simulation
Band1 Band3 Band5
(0.47 μm) (0.64 μm) (1.6 μm)
Stats from 17 to 31 Oct. 2016
Validation of On-board Calibration Method 2) Ray-matching with S-NPP/VIIRS

## Slide 28
Results for AHI-8/-9 vicarious calibration, ray-matching and GEO-GEO comparison
Converted to (AHI-9/AHI-8 – 1) x 100 [%]
(AHI-9/AHI-8-1) x 100 [%]
0.47 0.51 0.64 0.86 1.6 2.3 [μm]
Good agreements among the three validation methods
Band1: AHI-9 is 4-6% brighter than AHI-8
Band2-4, 6: AHI-8/-9 diffs. are within 2%
Band5: AHI-9 is ~6% darker than AHI-8
Notes on calibration slope
AHI-8: derived from solar diffuser obs. in Mar-May 2015
AHI-9: pre-launch determined value
Could cause AHI-8/-9 discrepancies in the validation
Observation data: 14-28 Feb. 2017
Comparison of VNIR Calibration between AHI-8/-9

## Slide 29
AHI Band 1 (0.47 µm)
Brighter VIIRS at dark scenes
AHI-8 vs. VIIRS direct comparison (ray-matching)
AHI-8 Band1 (0.47 μm) vs. VIIRS M03 (0.46 µm)