## Slide 1
S. Wagner, EUMETSAT
M. Takahashi, JMA
T. Stone, USGS
Traceability of the GIRO to the ROLO: Definition of a benchmark

## Slide 2: Scope and purpose of the benchmark
  Definition of a reference synthetic dataset
  Assessment of the GIRO performances with respect to the current lunar calibration reference model ROLO:
    Verification / Validation of new developments
    Uncertainty assessment
     Traceability
  Uncertainty assessment / traceability to the GIRO for local implementations
  Possibility to perform a similar assessment for newly developed models with respect to the GIRO

## Slide 3: Parameters to vary
Geometry:
  Time: possibly the complete 18-year cycle with “feasible” time step (currently every 6 hours)
     Libration + phase coverage
  Satellite position:
    Earth centre (x=0., y=0., z=0.) or at the surface of the Earth
    In orbit at 800km or at 36000km from the Earth ground
   Extract the cases to cover the parameter space
Spectral Response Functions:
  Central wavelengths as for existing Ocean Colour sensors + geostationary imagers + additional bands in between the ROLO bands (in particular for short wavelengths)
  Narrow + large SRFs
  Spectral resolution down to 1nm at first. May require a higher resolution (0.1nm)!
  More shapes of the SRFs

## Slide 4: Overview of the benchmark generator
All input / output files: netCDF
 Conventions defined by GSICS + first LCWS in 2014)
Scripts: coded in Python + Shell script
Currently input are not saved (generation based on a template)
Only the output are saved
GIRO output = part of the GSICS Lunar Observation Dataset (GLOD)
Availability of the GIRO tool as part of the GLOD = to be discussed

## Slide 5: Geometries
  Started date: 1 January 2000 at 0:00 UTC
  End date: 31 December 2017
  Time step: 6 hours
  Location:
    X: 42000.0
    Y: 0.0
    Z: 0.0
     ~14000 cases in [2°, 92°] range
  To check the coverage of the geometries in the selenographic coordinate space, two other locations were tried:
    X: 0.0
    Y: 0.0
    Z: 0.0
    X: 31600.0
    Y: 28000.0
    Z: 0.0

## Slide 6: Selenographic coordinates coverage
(31600,28000,0) position
(42000,0,0) position
(0,0,0) position
-92 deg.
92 deg.
0 deg.
Phase angle

## Slide 7: Spectral Response Functions
  SRF generator = 4th order Chebyshev filter with a pass band ripple
  SRF widths:
    10nm, e.g. OLCI.
    30nm, e.g. MODIS or VIIRS and new generations of geostationary imagers (even though a bit broader).
    300nm, e.g. high-resolution panchromatic bands (e.g. PLEIADES) and some (older) GEO visible channel imagers.
  SRF spectral resolution = 1nm (as a start)  Planned to reach 0.1 nm
  Range = [350nm, 2350nm]
  Spectral shift:
    2.5 nm in [350nm, 1200nm], i.e about 340 SRFs
    10 nm in [1200nm, 2350nm], i.e about 115 SRFs

## Slide 8: Spectral Response Functions
Solely used at 550nm for the whole Saros cycle

## Slide 9: Spectral Response Functions
  Example of spectral shift

## Slide 10: Case reduction for testing all the SRFs + SRF shifts
  Idea = sub-sampling of the selenographic space
  For each sub-domain, a regular sampling of phase angles is taken
  SRFs + SRFs shifts are tested on that subset
   Currently ~280 dates / geometries (configurable)

## Slide 11: Where are we with the planning?
Framework defined for simulated the cases
Draft documentation ready
Draft dataset provided to USGS (T. Stone)
Still to be done:
  Finalising the traceability of the GIRO to the ROLO
  Refine the cases (e.g. higher spectral resolution) if needed
  Next GSICS annual meeting (TBC)
  Prepare a paper to serve a reference for the GIRO
   2018