## Slide 1: Lunar reflectance model based on SELENE/SP data
Toru Kouyama (AIST)
Matsunaga, Nakamura, Yamamoto, Yokota and Ishihara
SELENE/SP Team
Yokota et al., 2011. Lunar photometric properties at wavelengths 0.5–1.6 μm acquired by SELENE Spectral Profiler and their dependency on local albedo and latitudinal zones. Icarus215,639–660.
Kouyama et al., 2016. Development of an application scheme for the SELENE/SP lunar reflectance model for radiometric calibration of hyperspectral and multi spectral sensors, Planetary and Space Science.

## Slide 2: SELENE(KAGUYA) and SP
SELENE:
・Size: 2 x 2 x 5m, 14 science instruments
・Orbit: Polar orbit (non sun-synchronous)
Altitude: 100 km
Ground track repeat cycle: ~ 30 days
・Mission period: 2007 – 2009 (finished)
Observing lunar surface
with various solar incident and phase angle conditions.
(Spectral Profiler)

## Slide 3: SELENE(KAGUYA) and SP
(Spectral Profiler)
Spectral
Sensor type: Spectrometer
Point sensor
http://www.kaguya.jaxa.jp/en/equipment/tc_e.htm
Multi-band Imager
Terrain Camera
Notes: Sensor type: Spectrometer
Spectral range:
500-2600 nm
Spectral resolution:
6 nm (VNIR 520-960 nm)
8 nm (NIR-SWIR > 900 nm)
Observation swath
500 m

## Slide 4: SELENE(KAGUYA) and SP
http://global.jaxa.jp/press/2007/12/20071214_kaguya_e.html
(Spectral Profiler)
SP Data
MI image and SP footprints
Wavelength
Wavelength
Spatial (along track)
Notes: During the mission, SP obtained this kind of data globally and repeatedly.

## Slide 5
Reflectance spectrum
at a reference condition
φ=30°, i = 30°, e=0°
SP Lunar Reflectance model (Yokota et al., 2011)
Reflectance map (758nm, i=30, e=0, α=30°)
Integrating 70 million observation data covering whole lunar surface with various phase angle conditions
Notes: Including incident, emission and phase angle dependencies using empirical functions

## Slide 6
Spectral range:
512 – 1650 nm (160 channels)
Δλ = 6 - 8 nm
Grid interval (Spatial resolution)
0.5˚ x 0.5˚
SP Lunar Reflectance model (Yokota et al., 2011)
Reflectance map (758nm, i=30, e=0, α=30°)
Integrating 70 million observation data covering whole lunar surface with various phase angle conditions
Including parameters for reproducing incident, emission and phase angle dependence
Notes: Including incident, emission and phase angle dependencies using empirical functions

## Slide 7
ASTER/Band 2 (660 nm)
April 14, 2003
Simulated
Observed
ASTER vs SELENE/SP
SP model is a radiance base model
[Kouyama et al., 2016, PSS]

## Slide 8
April 13, 2003
April 15
April 18
Simulating Moon observations

## Slide 9
Phase angle dependence of SP model
@ 745.3 nm
ROLO
SP model
Disk reflectance
(Normalized by 30°)

## Slide 10
Phase angle dependence
@ 745.3 nm
*This structure is different in different wavelengths

## Slide 11: SP Model availability
http://darts.isas.jaxa.jp/planet/pdap/selene/
At this time, a “map” version of SP model has not been distributed from this archive. (This situation has been unchanged, Sorry…)
SP team has shared the model with NOAA, JMA, and other teams in JAXA based on communication.
Surface reflectance data (called SP Level2c), which is a source data set of the model, is available from JAXA data archive site.

## Slide 12
Stability of SP sensitivity during mission
The degradation of SP was not significant over the mission period (up to 1 %).
= Good performance for measuring relative degradation.
Comparison of four observations of
Apollo 16 landing site [Yamamoto et al., 2011]
Nov. 19, 2007
Mar. 12, 2009
SP model accuracy
Notes: Sensor stability during the mission

## Slide 13
Chart: Sensor sensitivity variation since 2016.08.19 (G & R bands)
| 42598 | 42601 | 42689 | 42718 | 42746 | 42777 | 42808 | 42866
G | 1.0009 | 1 | 0.99465 | 0.99212 | 0.99204 | 0.99423 | 0.99449 | 0.9931
R | 0.99891 | 1 | 0.99735 | 0.99533 | 0.99553 | 0.99471 | 0.99497 | 0.99256
Relative sensitivity degradation can be tracked.
Small satellite case
1%
[Kouyama et al., 2017, IGARSS]
SP model accuracy
Relative sensitivity
2016
2017

## Slide 14
SP reflectance shows a “redding” trend
darker in shorter wavelength
brighter in longer wavelength.
(cf. Ohtake et al., 2010 & 2013)
SP’s reflectance
Not good absolute accuracy.
Less consistency among different wavelengths.
[Ohtake et al., 2013]
SP model accuracy
Notes: This plot shows a comparison of observation results among many sensors at a same place
SP reflectance shows a steeper profile than those
As a result… In shorter wavelength region, SP tends to describe Moon reflectance darker.
感度偏差: sensitivity deviation

## Slide 15
Correction with ROLO
Curve fitted with ROLO-SP comparison
ROLO irradiance is based on Kieffer and Stone, 2005
Ratio (ASTER/SP)
[Kouyama et al., 2016, PSS]
Lunar Irradiance
SP model accuracy

## Slide 16
Chart: Lunar irradiance comparison (Normalized by 550 nm)
| 390 | 480 | 550 | 590 | 700 | 860 | 950
 | 0.39035 | 0.88935 | 1 | 1.0169 | 1.0052 | 0.77129 | 0.70993
Observed
Hayabusa-2
Better spectral consistency
SP: Not corrected
SP: Corrected
Correction with ROLO
SP model accuracy
[after Suzuki et al., 2017, Icarus]

## Slide 17
Other issues
Not good model accuracy in high emission angle and high latitude regions
Yokota’s recommendation: emission angle < 45 degrees.
Model
ASTER
SP model is a radiance model. Accuracy of image registration may affect uncertainty.

## Slide 18
Summary
A hyperspectral lunar reflectance model has been proposed based on SELENE/SP observations, and an application scheme has been also proposed.
Current SP model has not enough accurate for absolute calibration, while it can be used for relative calibration.
Radiance based model requires image registration.

## Slide 19
Backup slides
Thank you!

## Slide 20
ASTER/Band 2 (660 nm)
April 14, 2003
Simulated
Observed
ASTER vs SELENE/SP
SP model is a radiance base model
[Kouyama et al., 2016, PSS]

## Slide 21
Brightness Comparison: ASTER vs SELENE/SP
 | Band 1 (520-600 nm)
Correlation Coefficient | 0.992
Mean ratio (= Bias): Observed / Simulated | 1.27
Standard deviation (= Precision of each pixel) | 0.05
Standard error | <1e-3

## Slide 22
Brightness Comparison: ASTER vs SELENE/SP
 | Band 1 (520-600 nm) | Band 2 (630-690nm) | Band 3 (760-860nm)
Correlation Coefficient | 0.992 | 0.993 | 0.993
Mean ratio (= Bias): Observed / Simulated | 1.27 | 1.01 | 0.95
Standard deviation of ratio (= Precision of each pixel) | 0.05 | 0.04 | 0.04

## Slide 23
Incident angle
Emission angle
Geometry data
Highland, mare and middle albedo region map
Lunar radiance map
Reflectance map (i=30,e=0,α=30)
Phase angle at observation time
x Solar Irradiance

## Slide 24
Model equations
r: reflectance using i=30, e=0, α=30 as the basis condition [Yokota et al.,2011] (11)
i: incident, e: emission, α: phase anlge
Fsun: Sun light Flux (W/m2/um)
S: SRF
From SP model
f: Empirical function of phase angle dependencies
XL: Empirical function of sun-light scattering

## Slide 25
Model equations
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Correction terms for Limb darkening effect
Reflectance to be calculated
i: incident angle
e: emission angle
α: phase angle
Notes: c1=-0.019, c2=0.242x10-3, c3=-1.46x10-6

## Slide 26
Model equations
After Yokota et al., 2011, Eq (11)
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 27
Model equations
B: Shadow hiding opposition effect
P: Regolith phase function
h, c, g, B0: Model coefficients
After Yokota et al., 2011, Eq (11)
High land, mare and medium albedo
Reflectance to be calculated
XL: Lunar lambert function
f: Empirical function of phase angle dependencies
Correction terms for Limb darkening effect
i: incident angle
e: emission angle
α: phase angle

## Slide 28
[Kouyama et al., 2014, LPSC]

## Slide 29
Definition of three albedo groups of Moon surface

## Slide 30
Modeled radiance (W m-2 str-1 μm-1)
Observed radiance (W m-2 str-1 μm-1)
ASTER (Band 1) Large bias
Observed / Model
Relative Frequency
Mean (Obseｒved/Model) = 1.27
SD = 0.05
SE (= SD/√Number of pixels used) = 0.0002
ASTER@2003.04.14 vs Model (SELENE/SP)

## Slide 31
Band 1
Band 2
Band 3
1.0
0.7
0.9
0.8
0
3000
Day since launch
ASTER/VNIR degradation curves

## Slide 32
Chart: 
| 0.48 | 0.48399999999999999 | 0.48799999999999999 | 0.49199999999999999 | 0.496 | 0.5 | 0.504 | 0.50800000000000001 | 0.51200000000000001 | 0.51600000000000001 | 0.52 | 0.52400000000000002 | 0.52800000000000002 | 0.53200000000000003 | 0.53600000000000003 | 0.54 | 0.54400000000000004 | 0.54800000000000004 | 0.55200000000000005 | 0.55600000000000005 | 0.56000000000000005 | 0.56399999999999995 | 0.56799999999999995 | 0.57199999999999995 | 0.57599999999999996 | 0.57999999999999996 | 0.58399999999999996 | 0.58799999999999997 | 0.59199999999999997 | 0.59599999999999997 | 0.6 | 0.60399999999999998 | 0.60799999999999998 | 0.61199999999999999 | 0.61599999999999999 | 0.62 | 0.624 | 0.628 | 0.63200000000000001 | 0.63600000000000001 | 0.64 | 0.64400000000000002 | 0.65 | 0.66 | 0.67 | 0.68 | 0.69 | 0.7 | 0.71 | 0.72 | 0.73 | 0.74
Band 1 | 0 | 0.0069 | 0.0078 | 0.0073 | 0.0107 | 0.058 | 0.125 | 0.2911 | 0.4567 | 0.6717 | 0.8392 | 0.9381 | 0.9906 | 1 | 0.9662 | 0.89 | 0.876 | 0.8959 | 0.9029 | 0.9263 | 0.9184 | 0.9387 | 0.9501 | 0.954 | 0.9606 | 0.9528 | 0.9058 | 0.8687 | 0.774 | 0.6795 | 0.5206 | 0.2972 | 0.151 | 0.0918 | 0.052 | 0.0355 | 0.0098 | 0.0046 | 0.0037 | 0.0056 | 0.0037 | 0.0014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Band 2 | 0.0038 | 0.0032 | 0 | 0.0019 | 0.0031 | 0.0006 | 0.005 | 0.0049 | 0.0018 | 0.0136 | 0 | 0.1529 | 0.3429 | 0.5998 | 0.8024 | 0.9709 | 1 | 0.9758 | 0.9696 | 0.975 | 0.943 | 0.9077 | 0.9396 | 0.9426 | 0.9226 | 0.91 | 0.8935 | 0.8427 | 0.8031 | 0.7917 | 0.7702 | 0.7487 | 0.6619 | 0.5544 | 0.4596 | 0.4258 | 0.3708 | 0.2991 | 0.2166 | 0.1247 | 0.0623 | 0.0442 | 0.028 | 0.0118 | 0.0105 | 0.0054 | 0.0041 | 0.0007 | 0 | 0 | 0 | 0
Band 3N | 0.0022 | 0 | 0.0093 | 0.0258 | 0.048 | 0.0509 | 0.098 | 0.1907 | 0.3353 | 0.6379 | 1 | 0.9786 | 0.8982 | 0.9148 | 0.9778 | 0.9942 | 0.9783 | 0.9624 | 0.9355 | 0.9713 | 0.982 | 0.9976 | 0.9895 | 0.9751 | 0.9874 | 0.9694 | 0.9542 | 0.9489 | 0.9247 | 0.9609 | 0.9489 | 0.942 | 0.9297 | 0.8366 | 0.6943 | 0.4813 | 0.2958 | 0.1763 | 0.09 | 0.0547 | 0.0318 | 0.0258 | 0.0204 | 0.0075 | 0.0074 | 0.0049 | 0.0024 | 0.0024 | 0 | 0 | 0 | 0
SRF convolution
Simulated hyperspectral images
Simulated band image