## Slide 1
Min Min, Lin Chen, Ronghua Wu, Xiuqing Hu
National Satellite Meteorological Center, CMA
E-mail: minmin@cma.gov.cn
MTF Evaluation of FY-3C/MERSI using Lunar Observation

## Slide 2: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 3: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 4
MTF（or spatial quality）
MTF@Nyquist = 0.10
0.5
1.0
0.0
0.1
MTF@Nyquist = 0.30
0.5
1.0
0.0
0.3
MTF
MTF
Frequency
Frequency
Image Sharpness

## Slide 5
Traditional Edge and Pulse Methods
Choi 2002
Nyquist frequency
Notes: Spot, IKONOS, Fabric 布

## Slide 6
Choi 2002
Airport NW-SE runway

## Slide 7: MODIS SpectroRadiometric Calibration Assembly (SRCA)
Choi et al., 2014
Achieve on-orbit MTF test for MODIS imaging system
Notes: It is heavy and cost a lot.

## Slide 8: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 9
ok
FY-3C is a polar-orbit meteorological satellite. The MERSI sensor on FY-3C have 20 bands from visible to infrared bands.
The onboard blackbody calibration are performed for all infrared bands of FY-3C.
Inter-calibration and drifter track method are used to validate FY-3 IR channels.
MERSI
FY-3C/MERSI

## Slide 10
FY-3C/MERSI Bands
Notes: serious stripe effect

## Slide 11: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 12
MTF theory using edge

## Slide 13: Ice block in the Polar Region
Low Spatial Resolution
(250m/1000m)
It is impossible to make
or find an artificial target
to do MTF test for MERSI.
We use Ice block in
the polar region as a Sharp
Edge to do the MTF test.
Notes: It is very hard to find some valuable works about MTF test for FY-3C/MERSI from intelnet. Spatial Quality of MERSI is still lacking or unclear.

## Slide 14: FY-3C/MERSI SRF

## Slide 16: Selection of polar ice block edge for MTF test
Cited from Min Min, Cao Guangzhen, Xu Na et al, 2016. On-orbit spatial quality evaluation and image restoration of FengYun-3C/MERSI [J]. IEEE Transactions on Geoscience and Remote Sensing. 54(12): 6847-6858

## Slide 17
Long-term FY-3C/MERSI MTF results

## Slide 18
Averaged MTF result
Cited from Min Min, Cao Guangzhen, Xu Na et al, 2016. On-orbit spatial quality evaluation and image restoration of FengYun-3C/MERSI [J]. IEEE Transactions on Geoscience and Remote Sensing. 54(12): 6847-6858

## Slide 19: 27% Overlapped between two adjacent pixels at cross-track (Scan) direction
…………..
27% overlap
Scan Direction

## Slide 20: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 21
Lunar image in FY-3C/MERSI space view
Fig. 1. Lunar images of FY-3C/MERSI (a) Band03 and (b) Band05 in space view with 250 m resolution at 20:05 UTC on 21 November 2013.

## Slide 22
Lunar image restoration
Fig. 2. Lunar images of FY-3C/MERSI in space view (a) before and (b) after restoration. The red boxes represent the moon edge zones we use for calculating ESF.

## Slide 23
MTF result comparison along flight direction
Using polar ice block
Using lunar image
The results are a litter bit higher than those using polar ice block
Early Result on orbit
atmospheric extinction effect

## Slide 24
Using polar ice block
Using lunar image
MTF result comparison along scan direction
Early Result on orbit
The results are a litter bit higher than those using polar ice block

## Slide 25
MTF results for IR band
Number | Date | UTC Time | Lunar Phase Angle
1 | 2013-10-23 | 05:30 | 48.21
2 | 2013-11-21 | 20:05 | 45.71
3 | 2013-12-21 | 10:30 | 43.18
4 | 2014-01-20 | 09:25 | 44.42
5 | 2014-06-17 | 08:10 | 57.08
6 | 2014-07-16 | 00:50 | 49.15
7 | 2014-08-14 | 05:20 | 47.39
8 | 2014-10-12 | 10:35 | 49.58
9 | 2014-11-10 | 23:25 | 48.45
10 | 2014-12-10 | 12:10 | 45.30
Dates and UTC times of the lunar observations in SV and phase angles
Fig. 3. MTF values at the Nyquist frequency for TEB of FY-3C/MERSI from October 2013 to December 2014. The solid gray triangle and black circle respectively represent the MTF values sampled along flight and scan directions.

## Slide 26: Outline
What is MTF or Spatial Quality?
FY-3C/MERSI Introduction
MTF results using polar ice block edge
MTF results using lunar image
Summary

## Slide 27: Summary
Early MTF test results from polar ice block and lunar image show the same variation trend
MTF results using lunar image are a little bit higher than those using polar ice block due to atmospheric extinction effect.
Inherent Overlapped scan mode of FY-3C/MERSI induces the reduction of MTF or spatial quality, which are proved by both ice and lunar methods.

## Slide 28: Thank you
Q&A