## Slide 1: On-orbit Modulation Transfer Function Characterization of PROBA-V Using the Moon
Work done by : Ignacio Torralba Elipe (ESA-ESTEC)
Presentation : Stefan Adriaensen (VITO)
2nd GSICS/CEOS Lunar Calibration Workshop, Xi’an, China 13/11/20117 – 16/11/20117

## Slide 2: In orbit verification of PROBA-V MTF
MTF is a measure for the spatial imaging quality of a sensor
PROBA-V is a pushbroom line-sensor, so the MTF is derived from the line spread function.
This is done using lunar acquisitions near full Moon (7degrees phase)
radiance values are used

## Slide 3: ESF edge spread function
The method is based on the method by Françoise Viallefont-Robinet [2010]
Based on the selection of multiple lines in the lunar image, an edge spread function can be constructed with a resolution higher than the pixel resolution
edge spread function needs resampling for the fourrier transform (equidistant points) by means of Fermi-Dirac fitting

## Slide 4: ESF : PROBA-V moon edge selection
The position of the edge start line selection is done by hand as a starting point

## Slide 5: ESF : mismatch in selection

## Slide 6: Edge Spread Function

## Slide 7: Line Spread Function
The Line Spread Function essentially is the derivative of the ESF
The LSF is first normalised and then the Fourrier Transform is is calculated, resulting in MTF

## Slide 8: MTF : Results for PROBA-V
Results for 4 bands (BLUE, RED, NIR, SWIR)
Comparison with on ground measured MTF is shown
Results of 2 assessments are shown : 23062013 and 24072013

## Slide 9: MTF BLUE

## Slide 10: MTF RED

## Slide 11: PROBA-V MTF NIR

## Slide 12: PROBA-V MTF SWIR2

## Slide 13: Conclusion
MTF is verified in orbit for PROBA-V using lunar images
Proccessing could be done semi automatically
The retrieved MTF curves match well with the measured ones
Thanks to Ignacio Torralba Elipe (ESA)