## Slide 1: Lunar Observation Activities with a Small Satellite and a Planetary Exploration Satellite.
Toru Kouyama, AIST
2017.10.05
Hodoyoshi-1
Hayabusa-2

## Slide 2
Hodoyoshi-1 (2014-)
50cm
A small satellite developed and operated by Axelspace corporation
(Japanese venture company)
50kg
Image Acquisition Mode | Push-broom | 
Ground Resolution | 6.7 m | 
Spectral bands | Blue | 450-520 nm
 | Green | 520-600 nm
 | Red | 630-690 nm
 | Near Infrared | 780-890 nm
Osaka, Japan
Notes: Oversampling
Stray-light
Dark signal bias

## Slide 3
2016.08.16
2016.08.19
2016.11.15
2016.12.14
Hodoyoshi-1’s moon observations
(2016.8 – 2017.5)
2017.01.12
2017.02.11
2017.03.13
2017.05.11
α = -29 °
α = +10°
α = -10°
α = +10°
α = +10°
α = +10°
α = +10°
α = +10°
α: Phase angle
50cm
*after correcting oversampling effect
Notes: Oversampling
Stray-light
Dark signal bias

## Slide 4
Lunar calibration results
Chart: Sensor sensitivity variation since 2016.08.19 (G & R bands)
| 42598 | 42601 | 42689 | 42718 | 42746 | 42777 | 42808 | 42866
G | 1.0009 | 1 | 0.99465 | 0.99212 | 0.99204 | 0.99423 | 0.99449 | 0.9931
R | 0.99891 | 1 | 0.99735 | 0.99533 | 0.99553 | 0.99471 | 0.99497 | 0.99256
Lunar calibration for Hodoyoshi-1 can detect very small degradation (less than 1 %)!
1 % is enough for science use.
Using SP model, and normalized with 8/19 result
1%
Dashed line: Expected sensitivity variation
[Kouyama et al., 2017, IGARSS]

## Slide 5
Lunar calibration for Hayabusa-2
Observation
Simulation

## Slide 6
Chart: Lunar irradiance comparison (Normalized by 550 nm)
| 390 | 480 | 550 | 590 | 700 | 860 | 950
 | 0.39035 | 0.88935 | 1 | 1.0169 | 1.0052 | 0.77129 | 0.70993
Observed
Hayabusa-2
Better spectral consistency
SP: Not corrected
SP: Corrected
[after Suzuki et al., 2017, Icarus]
Consistency between bands

## Slide 7
Brightness ratio between Moons located at image center and at image corner
Without additional correction
With additional correction
10%
Corner
Center
Checking flat correction
[after Suzuki et al., 2017, Icarus]

## Slide 8
Summary
We (AIST) have collaborated with two small satellite missions and several planetary missions.
Discussion of importance of calibration and how we can achieve the calibration with a commercial company. -> I want to notice the importance of calibration in Japanese small satellite community.
Lunar calibration can be used for checking homogeneous of sensitivity in a 2D image sensor. (validating flat correction)

## Slide 9
Thank you !
Backup slides…

## Slide 10
Raw images

## Slide 11
ASTER/VNIR Lunar calibration results
(r = Observed brightness / Simulated brightness)
 | RCC(Ver 4) | Obata et al (2015) | Lunar Calibration
Band 1 | 0.972 | (0.972) | 0.970
Band 2 | 0.986 | 0.949 | 0.948
Band 3N | 0.923 | 0.942 | 0.943
Current
official
Vicarious
+ Cross
Our results
Degradation ratio from 2003 to 2017

## Slide 12
Sensor performance of Hayabusa-2
Consistency of sensitivity among different bands
Expected Moon brightness
Observed brightness
Keep good performance

## Slide 13
Lunar calibration procedure
① Correcting oversampling effect
Obtaining
Oversampling factor
Image analysis
Correction

## Slide 14
Lunar calibration procedure
② Simulating lunar observation
Input:
Observation date
Observation geometry
③ Comparing observation and simulation
Model calculation

## Slide 15
Phase angle (degrees)
0
30
60
90
-90
-60
-30
0
0.5
1
1.5
Normalized brightness
(Disk integrated)
Dependency on phase angle
Lunar brightness characteristics
Waxing
Waning

## Slide 16
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 3.5056 | 3.04 | 1.7368 | 0.6013 | -1.1117 | -2.2513 | -2.837 | -2.6325 | -2.3142 | -0.9157 | 0.75116 | 2.4273
Month in 2017
Brightness Deviation (%)
Dependency on Libration effect
Phase angle = -7°
Lunar brightness characteristics

## Slide 17
Chart: Sensor sensitivity variation since 2016.08.19 (B band)
| 42598 | 42601 | 42689 | 42718 | 42746 | 42777 | 42808 | 42866
B (based on G) | 0.98409 | 1 | 0.99336 | 0.99079 | 0.99212 | 0.99301 | 0.99327 | 0.99292
B (based on R) | 0.9637 | 1 | 0.99136 | 0.98862 | 0.99282 | 0.99046 | 0.99217 | 0.99216
Lunar calibration results
Note: Lunar brightness model (SP model) does not cover Blue band wavelength range.
Blue band sensitivity is deduced from comparison with Green and Red bands.
Discrepancy = Uncertainty
1%
Using SP model, and normalized with 8/19 result