## Slide 1: Evaluation of ABI Radiometric Characteristics Using Lunar Measurements
Fangfang Yu1, Xi Shao1 , and Xiangqian Wu2
GOES-16 is not declared operational. The ABI data are currently experimental and still undergoing testing.
1: ERT, Inc@NOAA/NESDIS/STAR
2: NOAA/NESDIS/Center for Satellite Application and Research (STAR)

## Slide 2: Normal Lunar Scans
MESO scan in mode 3 is used to collect the Moon data. Each MESO scan consists of two swaths
The Moon is scanned with one of the two swaths
ABI Moon data is in Level1Alpha format – calibrated but not navigated data
G16 ABI uses Side2 FPMs
ABI Mode 3 timeline
Band name | Central Wavelength (µm) | EW ASD (µrad) | NS ASD (µrad) | Columns | Row
B01 | 0.47 | 22 | 22.7 | 3 | 676
B02 | 0.64 | 11 | 10.4 | 3 | 1460
B03 | 0.87 | 22 | 22.7 | 3 | 676
B04 | 1.38 | 44 | 41.6 | 6 | 372
B05 | 1.61 | 22 | 22.7 | 6 | 676
B06 | 2.25 | 44 | 41.6 | 6 | 372

## Slide 3: Normal Lunar Scans: Chasing and Trending
Chasing:
  ABI consecutively scans the Moon as it transits across the space within the Field of Regard (FOR).
  The data is mainly used for the Response vs. Scan-angle (RVS) study, as well as trending analysis.
  Only conducted during the PLT/PLPT periods.
Trending:
  ABI scans the Moon within one meso-scan time window which is ~2 minutes.
  The data is used for the monitoring of VNIR solar calibration degradation.
  Will be conducted 2-3 times per month through the operational mission life.

## Slide 4: GOES-16 ABI Lunar Images
B01
B02
B03
B04
B05
B06
Phase angle ≈ 15 degree

## Slide 5: Enhanced Lunar Image Display
Albedo: [-0.1%, 0.5%]
Band01 Band02 Band03
Band04 Band05 Band06
Coherent noise at each band meets the specification
Ghosting/xtalking?
Ongoing effect to identify the source to accurately calculate the irradiance

## Slide 6: ABI Lunar North-South Scan (NSS)
ABI conducted series of North-South Scan (NSS) over the Moon
  All the detectors of the all 16 bands across the illuminated lunar edges from north to south
Used to examine the crossing talk effect in between detectors and bands
  Effort is still ongoing

## Slide 7: Band 1
Band 2
Band 3
Band 4
Band 5
Band 6
Examples of Lunar NSS Images

## Slide 8: Lunar NSS Radiance in 3D Demonstration: B1-3
Band 1
Band 2
Band 3
The lunar NSS radiance is generated with an off-line soft package which currently does not fully function yet

## Slide 9: Lunar NSS Radiance in 3D Demonstration: B4-6
Band 6
The lunar NSS radiance is generated with an off-line soft package which currently does not fully function yet
Band 4
Band 5
O/E Xtalking?
On-going effect to identify the source

## Slide 10: Discussion of the terms
OOF (Out Of Field) energy
= OFAR (Out of Field Anomalous Response)
  Blooming – detector problem (esp. old CCD)
    Optical/e-xtalking?
  Ringing – usually detector issue. Possible (but unlikely) resample.
    e-xtalking
  Ghosting – internal reflection (optical)
    optical xtalking (e.g. band-to-band xtalking)
  Overshooting/Undershooting - probably another name of ringing.
    E-xtalking
  Xtalking
    Optical xtalking
    Electronic xtalking
    Often out-of-band (OOB), in addition to OOF

## Slide 11: Conclusions
The moon image is unique to detect and assess the out-of-field (OOF) energy
  Source and target of the cross-talking energy
GOES-16 ABI lunar images do not show apparent out-of-field energy except at B06
  Accurate calculation of lunar irradiance need to understand the source of OOF energy
More accurate assessment of xtalking will be examined with the ABI lunar NSS data
  Detector-to-detector xtalking
  Band-to-band xtalking