## Slide 1: Detections of Radiometric Calibration Update/Anomaly with ABI vs. CrIS/IASI IR Inter-Calibration
Fangfang Yu1 and Xiangqian Wu2
GOES-16 is not declared operational. The ABI data are currently experimental and still undergoing testing.
1: ERT, Inc@NOAA/NESDIS/STAR
2: NOAA/NESDIS/Center for Satellite Application and Research (STAR)

## Slide 2: GEO-LEO Inter-Calibration for ABI MIR Bands
10/19/2017: updates of ABI Scan mirror Emissivity LUTs

## Slide 3: GEO-LEO Inter-Calibration for ABI LIR Bands
10/19/2017: updates of ABI Scan mirror Emissivity LUTs
08/02/2017: Metop-B IASI non-linearity correction
?

## Slide 4: Summary
The update of Metop-B IASI ground processing can be detected at the ABI LWIR bands using the daily mean Tb bias
  Both ABI and IASI are very stable
  Magnitude of the Tb bias jump is channel dependent
The residual of ABI scan mirror spatial uniformity corrections amplify the impact
  Observed from August 1 – Oct. 19, 2017
Update of the ABI scan mirror emissivity LUTs reduced the ABI Tb bias to CrIS and IASI, as expected
Need more study on B12 (9.6um) as Tb bias to CrIS and IASI is slightly larger than the other bands