## Slide 1
CLARREO Pathfinder Inter-calibration:
Requirements and Objectives
CLARREO Pathfinder Inter-Calibration Team
Presented by Tom Stone, USGS

## Slide 2
LEO and GEO data matching when available (e.g. MODIS and GOES-13).
Uniform and stable surface sites.
Instrument stability by observing the Moon (e.g. SeaWIFS).
Deep Convective Clouds, clear ocean & deserts: involve RT modeling.
Results from C. Roithmayr
Temporal matching: 30 minutes
Inter-Calibration of Sensors in RS: Current

## Slide 3
Inter-calibration of gain:
Type A uncertainty (random) is 5.11% (k=1): due to data matching.
Type B uncertainty (not random) is defined by the MODIS accuracy of 2% (k=1) [pre-launch].
Spectral Type B uncertainty: due to difference in spectral response.
Fundamental limitation
of current approach
Results from the GSICS Report
Inter-Calibration of Sensors in Reflected Solar: Current

## Slide 4
Threshold Science Requirements:
The CLARREO Pathfinder shall demonstrate the ability to use the
reflected solar spectrometer as an in-orbit transfer standard for inter-calibration of the reflectance bands of the VIIRS instrument and the
CERES instrument's shortwave channel. The uncertainty contribution
from inter-calibration approach should be limited to 0.6% (k=1)*
Baseline Science Objectives:
The CLARREO Pathfinder objective is to demonstrate the ability to use
the reflected solar spectrometer as an in-orbit transfer standard for inter-calibration of the reflectance bands of the VIIRS instrument and the CERES instrument's shortwave channel. The uncertainty contribution
from inter-calibration approach should be limited to 0.3% (k=1)
Ability to perform:
- Inter-calibration of imagers in GEO;
- Surface site characterization (e.g. deserts);
- Calibration of Lunar Spectral Reflectance.
Inter-Calibration Requirements & Objectives
* This is sampling uncertainty in addition to other uncertainties

## Slide 5
Inter-Calibration Concept: CERES & VIIRS
CLARREO Pathfinder Instrument provides high-accuracy reference on orbit
CLARREO Pathfinder Instrument has 2D pointing ability (pitch-roll)
CLARREO Pathfinder data matching with CERES and VIIRS on JPSS:
temporal matching within 10 minutes, on-orbit angular/spatial matching
Inter-calibration event prediction/planning ahead of time
CLARREO Pathfinder location on ISS: ELC-1 Site 3
A simplified visualization of
Inter-calibration event with
CERES and VIIRS on JPSS-1
Approach: inter-calibration by real time pointing off-nadir
Inter-calibration on-orbit operations are planned ahead of time

## Slide 6
Gimbal configuration: pitch - roll
Approximate gimbal range of motion at ISS ELC-1 Site 3.
Some FOR obscuration due to ISS accommodation.
Accommodation studies by the CPF team
100º
-50º
0º
100º
Starboard
Port
-105º
145º
0º
Wake
Ram
Pitch
Roll
+z
+x
+z
+y
RS Instrument Field-of-Regard from ELC-1 Site 3

## Slide 7
Instrument FOV = 10o
Time matching +/- 10 minutes
1356 inter-calibration opportunities over 1 year
Results from C. Roithmayr
Geolocation of the ISS ground track during each opportunity to take measurements for inter-calibrating JPSS cross-track sensors (CERES and VIIRS).
Inter-Calibration Events: Geolocation

## Slide 8
Simulation ISS ELC-1 Site 3:
10 minutes time matching
Instrument field-of-regard
Instrument FOV = 10o
No Instrument FOV obscuration
Event duration > 30 seconds
SZA < 75o
N good events = 1208
VIIRS:
100 samples every 5 seconds
(imager re-sampling)
CERES:
3 FOVs every 5 seconds
(large FOV)
Margin at about 55% for operations
not-available on average !
Inter-Calibration: Sampling & Margin

## Slide 9
Inter-Calibration Objectives: GEO imagers
Roithmayr et al., 2014
Sampling example:
10 days for GOES 75 W
(from P90 600 km orbit)
No sampling in the center due to singularity for the yaw motion. No such thing for the CPF pitch-roll configuration !
Latitude will be limited to 51.6o
SENSORS:
GEO imagers:
NOAA ABI on GOES-16
EUMETSAT
ESA GERB

## Slide 10
Inter-Calibration Objectives: Lunar Reflectance
CALIBRATION TARGET:
Moon: improve accuracy of lunar spectral reflectance
© 2017, C. Lukashin
NOTE:
ARCSTONE is a parallel project funded by the NASA ESTO to calibrate Lunar spectral reflectance from space with cubesat implementation.
Currently at TRL3
Expected TRL5 in September 2019
Reflectance of Lunar surface stable to < 10-8

## Slide 11
CALIBRATION TARGET:
Instrumented and not-instrumented Surface Sites (e.g. deserts)
Currently considered Surface Sites:
Inter-Calibration Objectives: Surface Sites
Railroad Valley Playa
  Lat: 38.497o
  Long: -115.690o
Baotou
  Lat: 40.851659o
  Long: 109.628904o
La Crau
  Lat: 43.55885o
  Long: 4.868872o
Gobabeb
  No data yet available?
Source: RadCalNet Quick Start Guide: https://www.radcalnet.org/resources/RadCalNetQuickstartGuide_20160915.pdf

## Slide 12
Product | Contents | Resolution | Granule
Level-1 Products for VIIRS CERES GEO (NOAA, ESA, etc.) Surface Sites Moon | Calibrated and geo-located CPF observations. | Full spectral and spatial resolution of the CPF RS Instrument. | Each granule contains single CPF inter-calibration event.
Level-4 Products for VIIRS CERES | Collections of CPF (Level-1), VIIRS, and CERES matched data (Level-1 & Level-2). | CLARREO (Level-1B) and VIIRS (Level-1 & Level-2, Clouds and Aerosols) data spatially convolved over IC sample. CLARREO Spectral re-sampling. CLARREO (Level-1) spatially convolved over CERES FOV’s PSF. CLARREO conversion to broadband reflectance. Scene ID from the CERES SSF. | Data processed by the CPF inter-calibration events.
Data Analysis VIIRS CERES | Inter-calibration results: Constraints on effective offset, gain, non-linearity, sensitivity to polarization, and spectral degradation. | Format is TBD | Format is TBD
Inter-Calibration Data Products
Nadir observations will be processed into Level-1B data product
Additional data analysis – by a separately funded science team

## Slide 13: Inter-Calibration: Current Work
CLARREO Pathfinder mission is extended Phase-A study period:
Refining inter-calibration planning and sampling:
- Orbital prediction and pointing
- ISS-related algorithms, obscuration, impact on pointing
- Definition of event priority and planning cycle
- Continue inter-calibration sampling studies
Definition of data products
PCRTM-based algorithms for angular and broadband modeling
Data product simulation for selected inter-calibration events
ATBD draft including:
- Required data inputs and interfaces
- Uncertainty budget for VIIRS inter-calibration
- Uncertainty budget for CERES inter-calibration
Theoretical and empirical PDM development and validation
PDM application software prototype
Coordination with DMT on algorithms implementation

## Slide 14
Roithmayr, C.M., and P.W. Speth, 2012: “Analysis of opportunities for intercalibration between
two spacecraft,” Advances in Engineering Research Vol. 1, Chapter 13, Edited: V.M.
Petrova, Nova Science Publishers, Hauppauge, NY, pp. 409 - 436.
Lukashin, C., B. A. Wielicki, D. F. Young, K. Thome, Z. Jin, and W. Sun, 2013: “Uncertainty
estimates for imager reference inter-calibration with CLARREO reflected solar spectrometer,”
IEEE Trans. on Geo. and Rem. Sensing, special issue on Intercalibration of satellite instruments,
51, n. 3, pp. 1425 – 1436.
Roithmayr, C. M., C. Lukashin, P. W. Speth, G. Kopp, K. Thome, B. A. Wielicki, and D.F. Young,
2014a: “CLARREO Approach for Reference Inter-Calibration of Reflected Solar Sensors:
On-Orbit Data Matching and Sampling," IEEE TGRS, v. 52, 10, pp. 6762 - 6774.
Roithmayr, C. M., C. Lukashin, P. W. Speth, D.F. Young, B.A. Wielicki, K. J. Thome, and G.
Kopp, 2014b, “Opportunities to Intercalibrate Radiometric Sensors from International Space
Station,” J. of Atm. and Oce. Tech., DOI: 10.1175/JTECH-D-13-00163.1.
Wu, A., X. Xiong, Z. Jin, C. Lukashin, B.N. Wenny, J.J. Butler, 2015: “Sensitivity of Intercalibration
Uncertainty of the CLARREO Reflected Solar Spectrometer Features,” IEEE TGRS, v. 53, 4741 - 4751,
10.1109/TGRS.2015.2409030
Sun W., C. Lukashin, and D. Goldin, 2015: “Modeling polarized solar radiation for CLARREO
inter-calibration applications: Validation with PARASOL data," J. Quant. Spectrosc. Radiat.,
v. 150, pp. 121 - 133.
Sun, W., R.R. Baize, C. Lukashin, and Y. Hu, 2015: “Deriving polarization properties of
desert-reflected solar spectra with PARASOL data,” Atmos. Chem. Phys., 15, 7725 - 7734,
doi: 10.5194/acp-15-7725-2015.
CLARREO Inter-Calibration: Key Publications