## Slide 1: New Regression Method for GEO-LEO-IR
Masaya Takahashi and Yusuke Yogo
Meteorological Satellite Center, Japan Meteorological Agency

## Slide 2
Current GEO-LEO IR adopts Least Squares method to derive radiance correction values (i.e. GSICS Correction)
  X (reference instrument) is assumed to be perfectly calibrated
  JMA proposed to use Reduced Major Axis which considers uncertainties in both X and Y
  Actually adopted in AHI Vicarious Calibration using MODIS
  Tested to derive Himawari-8/AHI vs. Metop-A/IASI Re-Analysis Correction
Motivation

## Slide 3: Three Ways of Calculating a Regression
Least squares regression is appropriate when there is uncertainty only regarding the y-variable. If both variables are subject to sampling and measurement error, major axis or reduced major axis regression is recommended. In the first two cases, the sum of the squared distances indicated by the green lines is minimized. In the final case, it is the areas of the triangles bounded by the horizontal and vertical green lines that are summed and minimized.
http://www.blc.arizona.edu/courses/schaffer/182/Giraffe/Regression.htm
Least Squares
Major Axis
Reduced Major Axis

## Slide 4
Least squares (LS)
  No error in X is assumed
  Y = aX + b is not equivalent to X = a’Y + b’
Major Axis regression (MA)
  Unit of X and Y should be the same
  Y = aX + b is equivalent to X = a’Y + b’
Reduced Major Axis reg. (RMA)
  X and Y are correlated
  Y = aX + b is equivalent to X = a’Y + b’
  Easy to calculate
The top left figure is from http://aoki2.si.gunma-u.ac.jp/R/scatter.html (in Japanese)
Radiance vs Radiance
AHI (3.9um, Tb < 230K) and IASI/A
LEO
GEO - LEO
N = 578
January 2016

## Slide 5
Reduced Major Axis Least Squares
Least Squares method seems reasonable
  If IASI calibration can be regarded as perfect
Need for investigations on big radiance differences b/w AHI and IASI at cold scenes
  Other issues (e.g. parallax) may exist in AHI IR inter-calibration

## Slide 6
Reduced Major Axis (RMA) Least Squares (LS) RMA – LS
AHI-8 TB Biases w.r.t. Metop-A/IASI at Standard Scenes
Big impacts on some bands (e.g. Band 07, 3.9 μm)
Need for further investigations to validate the differences b/w RMA and LS

## Slide 7
Questions?

## Slide 8
Reduced Major Axis (RMA) Least Square (LS) RMA – LS
AHI-8 TB Biases w.r.t. Metop-A/IASI at Cold Scenes (220 K)

## Slide 9: Unit of the GSICS Correction
Current contents
  Offset and slope to convert GEO radiance to LEO radiance in [mW m-2 sr-1(cm-1)-1].
  Tb bias at std. scene
  Conversion coefficients and equations between Tb and radiance
  Optional variables in MTSAT-2:
    Offset and slope to convert GEO DN to LEO radiance in [mW m-2 sr-1(cm-1)-1]
    LUT from GEO DN to LEO Tb [K]
Situation in AHI
  Himawari Standard Data (HSD, L1B equivalent) is based on radiance in [W m-2 sr-1 um-1 ].
  JMA/MSC web page provides conversion coefficients between rad[WN] and Tb[K].
  LUT approach (JMA optional B) is not reasonable for AHI any more.
    3.9 um band has 14 bits.
  HSD has “Inter-calibration information block” to contain the information (C).
GEO DN
GEO Tb [K]
GEO rad. [WN]
LEO rad. [WN]
LEO Tb [K]
LEO rad. [WL]
GSICS Correction
GEO rad. [WL]
A)
For “WL” users to obtain LEO radiance
C)
B)
HSD data format
C)

## Slide 10: For more convenient coefficients...
GEO DN
GEO Tb [K]
GEO rad. [WN]
LEO rad. [WN]
LEO Tb [K]
LEO rad. [WL]
Current GSICS Correction
GEO rad. [WL]
Many users will adopt the same unit as L1B data of each monitored imager.
For more convenient coefficients, why don’t we contain conversion coefficients from DN to corrected radiance, (A) or (C), depending on the unit of monitored sensor L1B data?
IASI, AIRS, Cris Meteosat?
[mW m-2 sr-1(cm-1)-1]
Himawari, GOES-R?,
MODIS, VIIRS
[mW m-2 sr-1um-1]
A)
C)

## Slide 11: How can we take regression?
Bias in “cold end”
  Uncertainty of brightness temperature (Tb) bias tends is larger in lower Tb range, especially in SWIR.
  Some meteorologists are interested in cold region.
  It is caused by non-linearity between radiance and Tb and is significant in shorter wavelength.
Is such the large bias true?
Planck’s law says...
 | 3.9 um | 6.2 um | 10.4 um
300 K | 0.6021 | 5.682 | 9.823
200 K | 0.00128 | 0.1187 | 0.9703
[W･m-2･sr-1･(μm)-1]
Tb bias is -5 K at 220 K, -15 K at 210K. The corrected radiance become minus in Tb < 207 K.
Energy is 1/470

## Slide 12: How can we take regression?
To take a regression in Tb space?
  It can bring reasonable-like averaged bias in lower Tb range, but ...
  GEO Tb and LEO Tb are not always linear, because radiance and Tb is not linear.
To separate Tb bins and take a regression in each bin?
  How to separate?
To set a valid Tb range?
  How to estimate the validity?
Band 7 (3.9 um)
Radiance vs Radiance
Tb vs Tb
Radiance vs Radiance
Tb vs Tb
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
LEO (IASI/A)
GEO (AHI)
Band 8 (6.2 um)
invalid
January 2016
January 2016