## Slide 1: Update on the NASA-Larc SBAF tool
Benjamin Scarinoa, David R. Doellingb, Arun Gopalana, Thad Cheea, Rajendra Bhatta, and Conor Haneya
aSSAI, One Enterprise Pkwy Ste 200, Hampton, VA 23666 USA
bNASA Langley Research Center, 21 Langley Blvd MS 420, Hampton, VA 23681-2199 USA
Global Space-based Inter-Calibration System 2018 Annual Meeting
19 - 23 March 2018 Shanghai, China
GRWG: VIS/NIR Sub-group
Thursday, March 22th, 15:50

## Slide 2: Outline
Developments summary
SBAF review
IR SBAF Example
Spectral Filtering
Summary

## Slide 3: 1-year Developments Summary
SCIAMACHY:
  Adjustable outlier filter and data range limiters
  Supports Uyuni PICS and ocean Ice/Water Cloud Earth spectra
  Axis control
GOME-2:
  Record expanded from 1 month to 9 years
  Version 1.0.C GOME-2 (FM3) / Metop-A (M02) signal degradation correction coefficients applied
  Enabled 2x-spatial resolution selection for measurements after July 2013
  More PICS
  Spectra plotting tool
  Reflectance option added, computed from Solar Mean Reference (SMR) spectra
Hyperion:
  IGBP and PICS pre-defined selection options
  Cloud filtering algorithm
  Spectra plotting tool with spectra range filtering and SRF convolution

## Slide 4: 1-year Developments Summary
IASI:
  Improved Planck Function extrapolation for NIR channels
  South Pole domain added
  SRF+Energy weighted IR brightness temperature correction coefficients, with linear correction, for conversion from radiances† (T*)
AIRS:
  AIRS SBAF tool
  With T*
Miscellaneous:
  Enabled spectra ASCII output on all spectra web tools
  J1-VIIRS, MSU-MR, FY-4, SMS, and INSAT-3DR instrument SRFs supported
†NOAA KLM User's Guide Section 7.1.2.2

## Slide 5: NASA Langley Satellite Calibration Webpage
satcorps.larc.nasa.gov
satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER

## Slide 6: NASA Langley Satellite Calibration Webpage
gsics.wmo.int
satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER

## Slide 7: Spectral Band Adjustment Factor (SBAF)
Derive reference- and target-sensor pseudo radiance/reflectance (Lp) via hyperspectral convolution over each RSR to account for band difference/out-of-band absorption
Derive reference- and target-sensor pseudo radiance/reflectance (Lp) via hyperspectral convolution over each RSR to account for band difference/out-of-band absorption
Every Earth scene has a unique spectral reflectance signature

## Slide 8: Spectral Band Adjustment Factor (SBAF)
Earth spectra plotting tool
(Sonoran Desert)
Spectral response function comparison tool
Derive Aqua-MODIS B1 and GOES-12 Ch1 pseudo radiance/reflectance (Lp) via SCIAMACHY convolution over each RSR to account for band difference/out-of-band absorption

## Slide 9: SCIAMACHY-based Visible SBAF Tool
Regression coefficient(s) define the SBAF
LMet-9-equivalent,MODIS = A2xLActual,MODIS2 + A1xLActual,MODIS + A0

## Slide 10: SCIAMACHY-based Visible SBAF Tool
Choose from common Earth target (e.g., desert PICS, DCC, IGBP)
Full database of instrument/channel RSRs
Units in either radiance or reflectance
Linear or non-linear characterization
SBAFs computed on the spot
Advanced subsetting options can lead to reduce SBAF uncertainty for known conditions

## Slide 11: SCIAMACHY-based Visible SBAF Tool
Regression coefficient(s) define the SBAF
LMet-7-equivalent,MODIS = A2xLActual,MODIS2 + A1xLActual,MODIS + A0
All-sky Tropical Ocean
Clear-sky Ocean
Bright Clouds
Met-7 pseudo radiance from convolution of Met-7 Ch. 1 SRF over the SCIAMACHY footprint spectra

## Slide 12: SBAF Dependency on Scene
All-sky tropical ocean (ATO) SBAF is a function of scene type
  Unique SBAF for clear ocean
  " " for clouds
  " " for thick clouds
Radiance is dependent on the scene type
2nd-order fit accurately defines an SBAF that represent the multiple scene conditions
Linear
2nd order
Force Fit
Regression | StdErr (%)
Linear through 0 | 4.0
Linear | 2.4
2nd order | 2.10
3rd order | 2.07

## Slide 13: SBAF Dependency on Scene
10% spectral-band-induced radiance difference between DCC and the Libyan Desert
DCC SBAF and equal reflectance (convolution over the solar constant) are similar because DCC are spectrally flat
Scene Type | SBAF
Clear ocean (ATO) | 0.912
Bright cloud (ATO) | 0.880
Libyan Desert (annual) | 0.783
DCC | 0.872
Equal reflectance | 0.876
Deep Convective Clouds
Libyan Desert

## Slide 14: Seasonal/PW Spectral Dependency
Libyan Desert seasonal SBAFs have reduced uncertainty compared to annual
Likely due to the seasonal water vapor burden (highest in summer)
I.E. - 2.4% Libya-4 SBAF difference between summer and winter seasons
Libya | SBAF | SE (%)
Winter | 0.795 | 1.01
Spring | 0.788 | 1.08
Summer | 0.776 | 0.84
Fall | 0.780 | 1.06
Annual | 0.783 | 1.34
Summer
Winter

## Slide 15: Seasonal/PW Spectral Dependency
PW
Season
Precipitable water (PW) load spectral difference follows seasonal spectral difference
Can have significant impact on SBAF for some bands (water absorption)

## Slide 16: Seasonal/PW Spectral Dependency
a) Simple forced linear SBAF for Libyan Desert for a full PW range
b-e) SBAFs for specified precipitable water intervals: 6% DSBAF
Uncertainy for each subset less than overall uncertainty
SBAF changes systematically with adjusted precipitable water
PW: 0-3 g cm-2
PW: 0-0.75 g cm-2
PW: 0.75-1.5 g cm-2
PW: 1.5-2 g cm-2
PW: 2-3 g cm-2

## Slide 17: Applications
SBAF reduces relative gain difference of multiple independent calibration methods over various Earth spectra
2.7%
0.4%
ATO-RM
ATO-RM

## Slide 18: IR SBAF Example
Spectra domains geared toward satellite coverage
SBAF available in either radiance or brightness temperature units
IASI
AIRS

## Slide 19: Applications
3rd-order relationship of WV channels resolved by 3rd-order SBAF application

## Slide 20: AIRS SBAF Example: 11-μm to 12-μm
Validation:
11 μm vs. 11 μm
Validation:
11 μm vs. 12 μm
Without SBAF
Bias: -0.01 K
SDD: 2.12 K
Bias: 2.69 K
SDD: 2.31 K
SBAF:
1st-degree forced [180 K]
SBAF:
1st-degree
SBAF:
2nd-degree
SBAF
3rd-degree

## Slide 21: AIRS SBAF Example: 11-μm to 12-μm
With
1st-degree forced SBAF
With
1st-degree SBAF
With
2nd-degree SBAF
With
3rd-degree SBAF
Validation:
11 μm vs. 11 μm
Validation:
11 μm vs. 12 μm
Without SBAF
(11-μm equivalent)
(11-μm equivalent)
(11-μm equivalent)
(11-μm equivalent)
Bias: -0.01 K
SDD: 2.12 K
Bias: 2.69 K
SDD: 2.31 K
Bias: -0.10 K
SDD: 2.31 K
Bias: -0.21 K
SDD: 2.39 K
Bias: -0.25 K
SDD: 2.30 K
Bias: -0.14 K
SDD: 2.28 K

## Slide 22: AIRS SBAF Example: 11-μm to 12-μm
Validation:
11 μm vs. 11 μm
Validation:
11 μm vs. 12 μm
With Piece-wise SBAF
(11-μm equivalent)
Bias: -0.01 K
SDD: 2.12 K
Bias: 0.00 K
SDD: 2.27 K
SBAF:
Piece-wise
(1/3)
SBAF:
Piece-wise
(2/3)
SBAF:
Piece-wise
(3/3)

## Slide 23: Hyperion Spectral Filtering
Hyperion “Water” Reflectance
Without Spectral Filter
SCIAMACHY “Clear-sky Topical Ocean”
Reflectance

## Slide 24: Hyperion Spectral Filtering
Hyperion “Water” Reflectance
With Low-Reflectance Spectral Filter
SCIAMACHY “Clear-sky Topical Ocean”
Reflectance
~clear ocean

## Slide 25: Hyperion Spectral Filtering
Hyperion “Water” Reflectance
With High-Reflectance Spectral Filter
SCIAMACHY “Approximate DCC”
Reflectance
~bright clouds

## Slide 26
Active of calibration tools development in support of proposal effort and for benefit of community
Scene-specific SBAF crucial to account for spectral induced radiance differences when inter-calibrating two sensors
Subsetting for known scene conditions, angles, etc., will significantly reduce uncertainty of SBAF
Spectral filtering can isolate conditions for a certain band based on dependency of another band
Summary

## Slide 27: Backup Slides

## Slide 28: GOME-2-based Visible SBAF Tool
Currently based on 4 seasonal months from 2008 and 2015
Balance between sampling and processing time
GOME-2 SBAF based on smaller footprint than SCIAMCHY
  40x80 km2 before July 2013
  40x40 km2 after July 2013
  SCIAMACHY is 30x240 km2
Homogeneity more likely in smaller footprints

## Slide 29
SBAF uncertainty 1.4% smaller using smaller footprints
SBAF does not change, however
GOME-2-based Visible SBAF Tool
40x80 km2
40x40 km2
40x80 km2
40x40 km2

## Slide 30: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval

## Slide 31: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval
Choose from pre-selections, enter own coordinates, or draw a box

## Slide 32: Hyperion-based Visible SBAF Tool
Map displays entire record of Hyperion ground measurements
Irregular distribution due to nature of tasked retrieval
Choose from pre-selections, enter own coordinates, or draw a box
Can be very selective

## Slide 33: Hyperion-based Visible SBAF Tool
Simple cloud filter based on standard deviation thresholds across decimated Hyperion swath
Can have significant impact on derived SBAF
No Cloud Filter
Cloud Filter
No Cloud Filter
Cloud Filter

## Slide 34: AIRS SBAF Example: 11-μm to 12-μm
SBAF:
3rd degree
SBAF:
Piece-wise
(1/3)
SBAF:
Piece-wise
(2/3)
SBAF
Piece-wise
(3/3)
Validation:
6.5 μm vs. 6.5 μm
Validation:
6.5 μm vs. 11 μm
Without SBAF

## Slide 35
With
3rd-degree SBAF
With
3rd-degree SBAF
AIRS SBAF Example: 11-μm to 6.5-μm
Validation:
6.5 μm vs. 6.5 μm
Validation:
6.5 μm vs. 11 μm
Without SBAF
(11-μm equivalent)
(6.5-μm equivalent)

## Slide 36: Spectral Radiance as a Function of Temperature (T*)
https://satcorps.larc.nasa.gov
https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SAT_CALIB_USER

## Slide 37: Spectral Radiance as a Function of Temperature (T*)

## Slide 38: IASI-based IR SBAF Tool Update
Users conducting Overshooting Convective Top studies found it helpful to construct piece-wise SBAFs using limited ranges of 11-μm BT
Works for any channel SBAF, not just 11-μm

## Slide 39: IASI-based IR SBAF Tool Update
A user suspected SBAF uncertainty was caused by CO2 absorption band just beyond 4.0 μm

## Slide 40: Applications
400 – 2500 nm
240 – 1750 nm
3600 – 15500 nm
240 – 790 nm
SBAF possible for 0.24-2.50 μm via SCIAMACHY, Hyperion, and GOME-2
  GOME-2 affords smaller footprint from shorter spectra range
IASI covers 3.60-15.5 μm
AIRS support grants enhanced scene selection for IR SBAFs
CLARREO Pathfinder, HySICS (??)
3740 – 4610 nm
6200 – 8220 nm
8800 – 15400 nm

## Slide 41
Solar Constant comparison tool
MODIS uses the MCST solar spectra to convert between reflectance and radiance
Important to use the same solar spectra when comparing multiple instruments