## Slide 1
Bertrand Fougnie, Sebastien Wagner, Tim Hewison
Calibration over Rayleigh Scattering
Needs and Open Questions

## Slide 2: Summary
Introduction – Why a Rayleigh Scattering Calibration
Definition : Rayleigh versus ocean target
Which potential needs ?
Main contributors and Inputs
RTM core performance
From LEO to GEO : open questions
Definition of priorities

## Slide 3: Introduction : Why a Rayleigh Scattering Calibration ?
Properties of the Rayleigh Scattering
(potentially used on the calibration after appropriate selection) :
  Spectral : “blue” with (lambda)-4 decrease law
  Brightness : moderate in the blue, to very dark in the red/NIR
  Directionality : very smooth signature
  Polarization : very significant polarized signature
3MI simulation

## Slide 4: Introduction : Why a Rayleigh Scattering Calibration ?
Properties of the Rayleigh Scattering
(potentially used on the calibration after appropriate selection) :
  Spectral : “blue” with (lambda)-4 decrease law
  Brightness : moderate in the blue, to very dark in the red/NIR
  Directionality : very smooth signature
  Polarization : very significant polarized signature
  Note : in single scattering approximation :
Geometrical range from space
Geometrical range from space

## Slide 5: Definition : Rayleigh versus Ocean target
Rayleigh Scattering Calibration or Ocean Target Calibration ?
  If RAY_Cal is usually performed over ocean, all oceanic targets are not suitable for “Rayleigh” calibration.
  Only a limited number of oceanic targets are appropriate
  The selection should avoid :
    Atmospheric turbid situations
    Sunglint perturbation
    Cloud pollution, including sub-pixel clouds detection
    Areas where the surface reflectance cannot be accurately known or predicted – this includes the marine contribution, as well as the surface whitecaps
    Neighbourhood of clouds and lands (vicinity effects)
  One selection stream was proposed in :
    GSICS Rayleigh ATBD Web Meeting (03/07/13)
    GSICS ATBD for Calibration over Rayleigh Scattering (Fougnie and Henry) 2013 (02/07/13)
  After selection : ~90% of the signal is due to Rayleigh Scattering
    Valid for all Visible bands (from 400 to 700nm)
    Other contributions are minor, but need to be properly evaluated

## Slide 6: Which Needs ?
From passed experience, the following aspects could be assessed :
  Absolute calibration (= the most demanding in term of modelling)
    Need an accurate modelling of every contributors
    Refined selection of measurements, accurate Radiative Transfer Model, appropriate inputs
  Cross-calibration (= could accommodate some approximations)
    Double-difference approach : use statistics
    relatively easy to derive if matchups are sufficiently similar
    Direct matching with geometrical and optionally temporal constrains
    limit the number of matchups + need of SBAF correction
  Temporal-calibration (= could accommodate some approximations)
    Less demanding in term of accuracy, but only accessible through important matchups
  Depending on the aspect, the optimization would be different
  IMPORTANT : The following anomalies on the radiometry impact the result : straylight, non-linearity, spectral out-of-band rejection, knowledge/evolution of the ISR, polarization sensitivity, variation of the calibration within the field-of-view…
   RAY_cal can be seen as “vulnerable” BUT this is also a powerful checking

## Slide 7: Main Contributors and Inputs
The TOA signal, to be computed and compared with the measured one, includes :
  Accurate computation of the Rayleigh scattering (>85%)
    Should include the polarization (single scattering assumption or fully)
    Importance of the Radiative Transfer Model (RTM)
    Monochromatic computation (using equivalent optical thickness) or line-by-line computation + spectral integration ?
  Aerosol background (~10% in the red with AOD << 0.1) :
    Selection of the best atmospherical non-turbid sites (“oceanic deserts”)
    Input model assumption
    or robust external source (AOD and model) – e.g. Copernicus CAMS
  Surface reflectance (~10% in the blue) :
    Oligotrophic (oceanic desert) & Mesotrophic waters recommended (Fougnie et al., 2010)
    Climatology, sufficiently realistic – e.g. Globcolour
    or external source - e.g. Copernicus CMEMS
  Gas absorption :
    In general minor contributors, but to be corrected

## Slide 8: The RTM core performance
The Rayleigh scattering (90% of the TOA signal), must be computed with, as much as possible, a high level of accuracy
  Inclusion of the polarization & multiple scattering
  Specular surface contribution including coupling terms
Unified RTM Radiative Transfer Model
  If a common GSICS method is agreed, a unique reference RTM or set of LUT (generated by this reference RTM) has to be adopted
  If any other RTM used, they should be “traced” to this GSICS reference RTM
  At least the same “Rayleigh” definition must to be considered
Computing time may be important
  For NRT operational computations
  LUT approach can also be easily used if critical

## Slide 9: From LEO to GEO – Open questions
The method has already been extensively used for many LEO sensors
  According the GSICS ATBD V1 : POLDER, VGT, MERIS, OLCI, MODIS…
  Statistical results are better if a maximum of geophysical conditions can be well mixed
The generalisation to GEO sensor still has to be consolidated
  Not all sites are accessible
  Viewing geometries are always the same (only the solar geometry is changing)
  Use of a NIR/SWIR band to constrain the aerosol content (not designed for low OC signal)
  Possibility and representativeness of exogenous aerosol estimation as backup

## Slide 10: Definition of priorities
The efforts to be made depend on the priorities
EUMETSAT priorities :
  1/ Absolute calibration for Sentinel-3 sensors
  2/ Absolute calibration for MSG/SEVIRI and MTG/FCI
  3/ Cross-calibration of LEO/LEO or GEO/GEO
GSICS needs (To be discussed) – What are the common priorities ?
  Cross-calibration LEO/LEO through double-difference
  Cross-calibration LEO/GEO
  Absolute calibration