## Slide 1
Report from ROSHYDROMET
Presenter - Alexey Rublev
State Research Center “PLANETA”, ROSHYDROMET
Russia
GSICS-EP-22, Online Meeting
30 March 2021

## Slide 2: Participation in EP, GDWG, GRWG
Points of contacts/meeting participants:
  EP : Alexander Uspensky
  GRWG: Alexey Rublev
  GDWG: Sergey Uspensky
Main contribution to GDWG actions
  Provision of near-real-time MTVZA-GY/ Meteor-M #2-2 data to EUMETSAT
  Provision of near-real-time IKFS-2/ Meteor-M #2 data to EUMETSAT
Main contribution to GRWG actions
  Development of post-launch calibration procedure for Russian scanners and sounders (MSU-MR, MTVZA-GY, IKFS-2, MSU-GS)
  Development of post-launch HEO-GEO calibration procedure for MSU-GS/Arktika-M #1 scanner
  Development of the Russian meteorological Cal/Val system portal with access to long-time archive of satellite instruments data covering test regions selected worldwide (https://planet.rssi.ru/calval)

## Slide 3: Russian Meteorological Satellite Systems
Federal Space Program for 2016-202)

## Slide 4: Satellite/Instrument Summary
2021

## Slide 5
Meteor-M #2 Intercalibration
Performance: MSU-MR
LEO-GEO intercalibration
IR channels vs SEVIRI/Meteosat-10 (-11)
LEO-LEO intercalibration
shortwave channels vs AVHRR/Metop-A
Date | к1 | к2 | к3
05.2020 | 1.34 | 1.41 | 1.43
06.2020 | 1.40 | 1.40 | 1.40
07.2020 | 1.36 | 1.47 | 1.41
08.2020 | 1.50 | 1.47 | 1.66
09.2020 | 1.51 | 1.50 | 1.66
10.2020 | 1.35 | 1.35 | 1.50
11.2020 | 1.30 | 1.26 | 1.34
12.2020 | 1.16 | 1.34 | 1.27
01.2021 | 1.27 | 1.32 | 1.36
02.2021 | 1.24 | 1.27 | 1.30
Channel | N pixels | Bias | RMSbias
5 (10.8mm) | ~15000 | -1.22 K | 0.72K
6 (12.0mm) | ~15000 | -1.35K | 0.78K
Channel 5
MSUmr – SEVIRI, K
Day number of year, 01.2016-02.2020
Day number of year, 01.2016-02.2020
MSUmr – SEVIRI, K
Channel 6

## Slide 6
Meteor-M #2-2 Intercalibration
Performance: MSU-MR
LEO-GEO intercalibration
IR channels vs SEVIRI/Meteosat-10 (-11)
LEO-LEO intercalibration
shortwave channels vs AVHRR/Metop-A
Date | к1 | к2 | к3
09.2020 | 1.24 | 1.21 | 1.39
10.2020 | 1.17 | 1.13 | 1.19
11.2020 | 1.08 | 1.12 | 1.16
12.2020 | 1.14 | 1.11 | 1.16
01.2021 | 0.99 | 1.02 | 1.11
02.2021 | 1.08 | 1.06 | 1.09
Channel | N pixels | Bias | RMSbias
5 (10.8mm) | ~15000 | 0.06 K | 1.03K
6 (12.0mm) | ~15000 | 0.76K | 0.96K
Channel 5
MSUmr – SEVIRI, K
Day number of year, 2020
Day number of year, 2020
MSUmr – SEVIRI, K
Channel 6

## Slide 7: 2019-2021 LEO-GEO: IKFS-2 vs SEVIRI under sea surface
TbIKFS-2, K
TbIKFS-2, K
Y=3.53+ 0.988х
BIAS= -0.097 K
RMSbias= 0.357 K
TbIKFS-2, K
TbSEVIRI, K
Ch 10.8 μkm
Y=8.098+ 0.97x
BIAS= 0.022 K
RMSbias= 0.256 K
TbIKFS-2, K
TbSEVIRI, K
Ch 13.4 μkm
TbIKFS-2, K
TbSEVIRI, K
T\bSEVIRI, K
TbSEVIRI, K
Ch 7.3 μkm
Ch 8.7 μkm
Ch 9.7 μkm
Y=8.512+ 0.971x
BIAS= 0.081 K
RMSbias= 0.37 K
Y=10.125+0.962xBIAS= -0.262 K
RMSbias= 0.231 K
TbIKFS-2, K
TbSEVIRI, K
Ch 12.0 μkm
Y=5.02+ 0.983x
BIAS=-0.017 K
RMSbias= 0.311 K
Y=10.125+ 0.964x
BIAS= -0.166 K
RMSbias= 0.39 K

## Slide 8: Absolute post-launch calibration of MTVZA-GY/Meteor-M #2-2 channels
Absolute post-launch calibration is based on relationships between observed radiances (antenna temperatures) and RTM-simulated radiances (Brightness Temperatures).
The calibration relationships for BT were obtained for special test sites in October 2019 using RTM of RTTOV type and GFS NCEP data as input. The emissivity of the ocean surface was specified in acoordance with FASTEM-5 model in depedence of wind speed.
The maximum BT discrepancies with simulated RTM BT (20.02.2020) are observed in the scanner channels with horizontal polarisation 18.7, 23.8, 36.7 GHz.
20.02.2020
17.01.2021
The calibration coefficients for BT obtained in October 2019 were used during 2020-2021. It was demonstrated rather good agreement between measured and calculated BTs as well as stable MTVZA-GY operation.
25.12.2020

## Slide 9
MSU-GS vs VIIRS INTER-CALIBRATION
(visible channels)
ELEKTRO №2
ELEKTRO №3
https://www.seas.harvard.edu
The use of deep convective clouds
Calc SBAF between spectral bands of reference (VIIRS) and calibrated instruments (MSU-GS) bands
Comparison of TOA reflectance measured by both instruments

## Slide 10
Evaluation of MSU-GS/Elektro-L #3 spatial resolution vs AHI/ Himawari-8measurements (10.4 vs 10.8 μm)
AHI 4 km
(MSU –GS nominal resolution)
AHI 2 km
MSU-GS
Averaging
Defocusing to bring to MSU-GS image
Synchronized images from two scanners, May 19, 2020

## Slide 11
6 October 2020.20:00 UTC
Intercalibration of the MSU-GS (10.70 μm) channel
vs AMI 10.5 μm channel
TAMI= 21.62+ 0. 928TМСУ
12 December 2020.16:00 UTC
Intercalibration of the MSU-GS (10.70 μm) channel
vs AHI 10.4 m
vs AMI 10.5 m
TAHI= 18.769+ 0. 938TМСУ
TAMI= 19.769+ 0. 933TМСУ

## Slide 12
Iceland
Ground track of Arctica-M #1
(highly elliptical orbit of “Molniya” type)
Longitude of the ascending node  = 335°(155°)
In the operational part of the orbit (three hours on each side of apogee), the satellite is north of 55° N;
The satellite in these orbits moves most of its time over the northern hemisphere and passes quickly over the southern hemisphere.
Red is operational part
Orbital period is 12 hours

## Slide 13
RGB image
Channel 1 (0.5-0.65) μm, Channel 2 (0.65-0.8) μm, Channel 3 (0.8-0.9) μm
29.03.2021 00:59 UTC
26.03.2021 00:59 UTC
West
East
IR channel 9 (10.2-11.2) μm
Arctika-M #1 satellite images

## Slide 14
Cloud motion animation
Western orbit, channel 9

## Slide 15: Cal/Val site of Russian hydrometeorological instruments
http://planet.rssi.ru/calval/
Welcome !
Spectral Response Functions
(IR bands)

## Slide 16
Thanks for attention!