## Slide 1
T. Hewison, S. Wagner, A. Burini, O. Perez Navarro, M. Burla, F. Pereda Garcimartin
Mission Integrated Calibration Monitoring Inter-Calibration System (MICMICS)

## Slide 2: Meeting Evolving Needs for Calibration Support
INRC Cal team uses diverse tools to:
  Generate calibration coefficients
  Monitor the calibration
  Perform inter-calibration
Developed to meet different needs
  Primarily for Meteosat imagers
  e.g. SSCC, Lunar Calibration System, Meteosat-IASI GSICS Processor
MSG/ SEVIRI
DCC GSICS processor
Meteosat-IASI GSICS processor
Lunar Calibration System
SEVIRI Solar Channel Calibration

## Slide 3: Meeting Evolving Needs for Calibration Support
INRC Cal team uses diverse tools to:
  Generate calibration coefficients
  Monitor the calibration
  Perform inter-calibration
Developed to meet different needs
  Primarily for Meteosat imagers
  e.g. SSCC, Lunar Calibration System, Meteosat-IASI GSICS Processor
Planning to integrate these functions
  (plus future developments)
  into Mission Integrated Calibration Monitoring Inter-Calibration System (MICMICS)
MSG/ SEVIRI
MICMICS
MICMICS
Mission Integrated Calibration Monitoring Inter-Calibration System

## Slide 4: Meeting Evolving Needs for Calibration Support
MSG / SEVIRI
S3 / SLSTR
MTG / FCI
MTG / LI
S3 / OLCI
EPS-SG / ICI
EPS-SG / 3MI
EPS-SG / VII
MICMICS
EPS-SG / MWI
MFG / MVIRI
INRC Cal team uses diverse tools to:
  Generate calibration coefficients
  Monitor the calibration
  Perform inter-calibration
Developed to meet different needs
  Primarily for Meteosat imagers
  e.g. SSCC, Lunar Calibration System, Meteosat-IASI GSICS Processor
Planning to integrate these functions
  (plus future developments)
  into Mission Integrated Calibration Monitoring Inter-Calibration System (MICMICS)
To meet needs for future missions
  Commissioning and Cal/Val
  More multi-mission L2 products
  Generation of FCDRs
  Growing importance of Radiometric Consistency

## Slide 5: Benefits of MICMICS
Initiated development of integrated system
  to meet the requirements for monitoring imagers’ calibration
  to compare and inter-calibrate these imagers
  to rationalise resources and efforts to:
    develop and maintain the system
    produce fast and consolidated feedback on mission performances
Other advantages of MICMICS include:
  exploiting complementary nature of diverse calibration systems, by
  facilitating the use of their results to validate each other,
  combining them to generate more robust results, covering a broader range of conditions.
  Consolidate the tools to analyse their results, and
  incorporate alternative calibration coefficients into L1 datasets via ground segments.
  Some components also serve as EUMETSAT’s contribution to GSICS.

## Slide 6: Scope of MICMICS
What will it do?
Radiometric calibration of imaging instruments with no on-board calibration unit (e.g. SEVIRI warm channels)
Near-real-time monitoring (including analysis of the medium and long-term stability) of the radiometric calibration
Support to re-analysis and FCDR generation
Which instruments/bands will it cover?
All channels of EUMETSAT imaging instruments
Selected third party reference instruments (e.g. GSICS reference instruments)
 Support to scientific enhancements to improve accuracy
What it will NOT do
Monitoring of short-term variations of the onboard calibration, e.g. between two repeat cycles
Radiometric noise monitoring
Monitoring of housekeeping parameters (temperatures, voltages, etc.)
Geometric factors (including stray light) + navigation

## Slide 7: Potential Instruments for MICMICS
Deployment phases:
  Prototype : 2019/20
  Phase 2 : 2020/21
  Phase 3 : 2021/22
  Phase 4 : 2023
Satellite Programme | Sensor | Function | Deployment phase
MSG | SEVIRI | Monitor & inter-calibrate & Calibrate | Prototype (v1)
EPS | IASI | Reference | Prototype (v1)
Sentinel-3 | OLCI | Monitor & inter-calibrate | Prototype (v1)
Sentinel-3 | SLSTR | Monitor | Prototype (v1)
MTG | FCI | Monitor & inter-calibrate | Phase 2 (v2)
MTG | LI | Calibrate & inter-calibrate | Phase 2 (v2)
JPSS | VIIRS | Reference | Phase 2 (v2)
JPSS | CrIS | Reference | Phase 2 (v2)
MFG | MVIRI | Recalibrate | Phase 2 - TBD
EPS-SG | VII | Monitor | Phase 3
EPS-SG | 3MI | Monitor & inter-calibrate | Phase 3 - TBD
EPS-SG | IASI-NG | Reference | Phase 3
EPS | GOME-2 | Reference | Phase 3 - TBD
EPS-SG | MWI/ICI | Monitor | Phase 3 - TBC
Sentinel-4 | UVN | Monitor & Reference | Phase 4 - TBD
MTG | IRS | Monitor | Phase 4 - TBD
Unconfirmed applications are shown in italics and/or TBD.

## Slide 8: MICMICS
Cal Coefficient Injectors
Reports
Web
OPS DBs
MICMICS Boundary
Calibration Output
Ext Data
GSICS
Site Data
Calibration Processing Modules
Data Buffer
Inst. Info
Data Acceptance Modules
L1 data
Reference Instruments’
L1 data
Intermed. results
Data Analysis and Reporting
Alerts
Events
Reprocessing

## Slide 9: MICMICS
CPMs:
DCC GEO/LEO + LEO/LEO
GSICS Rayleigh Scat
GIRO + Lunar Inter-Cal
IR GEO/LEO + LEO/LEO
Cal Coefficient Injectors
Reports
Alerts
Events
Reprocessing
Web
OPS DBs
Data Analysis and Reporting
MICMICS Boundary
Calibration Output
Ext Data
GSICS
Site Data
Calibration Processing Modules
Data Buffer
Inst. Info
Data Acceptance Modules
L1 data
Reference Instruments’
L1 data
Intermed. results
Of interest for GSICS
Intermed. results:
E.g. collocations
Reports:
Standards for GSICS reporting
DAR:
New version of the GSICS plotting tool (including VNIR)

## Slide 10: Spectral Band Applicability of MICMICS Vicarious Calibration Methods
Function | Target Method | UV | VIS | NIR | SWIR | TIR | FIR | MW | MICMICS Availability
Vicarious Calibration | Sun-glint | I | I | X | X | X | X | X | TBD
 | Deep Convective Cloud | ? | A T I | T | ? | X | X | X | 2019
 | Snow/Ice | ? | (T) | (T) | (T) | (T) | X | X | TBD
 | Deserts | ? | A T I | A T I | A T I | X | X | X | 2019
 | Tropical Forest | X | X | X | X | X | X | T I | TBD
 | Moon | (A) (T) (I) | (A) T I | (A) T I | (A) T I | X | X | (T) | 2019
 | Rayleigh/ Ocean | ? | A T I | T I | ? | X | X | T | 2021
 | NWP+RTM | X | X | X | X | T | T | T | 2021
Spectral Band Applicability of Vicarious Calibration Methods:
A : Absolute, T : Trending (in time), I : Inter-channel (in band), S : Spectral, ( ) : Needs development, X : N/A
MICMICS could provide:
independent validation of GS operational tools
backup for added resilience
offline monitoring
inter-calibration capabilities for routine comparison, e.g. with METimage, VIIRS, OLCI and SLSTR, using standard GSICS methods

## Slide 11: Spectral Band Applicability of MICMICS Vicarious Calibration Methods (2)
Function | Target Method | UV | VIS | NIR | SWIR | TIR | FIR | MW | MICMICS Availability
Inter- Calibration | Double-Differencing using vicarious results above | T | T | T | T | T | T | T | 2021
 | Multispectral Comparisons (SNO/SCO, Ray-matching) | T (I) (S) | T (I) (S) | T (I) (S) | T (I) (S) | T I (S) | T | T | 2019 (2022) (2022)
 | Hyperspectral Comparisons | (T) | (T) | (T) | (T) | (T) (I) (S) | (T) | (T) | TBD (2022)
Statistical Calibration | Histogram Analysis |  | (T) | (T) | (T) | (T) | (T) | (T) | TBD
Calibration Change Alerts | Any of the above |  |  |  |  |  |  |  | 2021
Recalibrate archive | Any of the above |  |  |  |  |  |  |  | TBD
Append Cal coefficients to L1 files | Any of the above |  |  |  |  |  |  |  | 2021?
Spectral Band Applicability of Vicarious Calibration Methods:
A : Absolute, T : Trending (in time), I : Inter-channel (in band), S : Spectral, ( ) : Needs development, X : N/A

## Slide 12: Summary of MICMICS
Mission Integrated Calibration Monitoring & Inter-Calibration System
  will perform and monitor imagers’ calibration
  of onboard and vicarious calibration systems,
  for optical imagers on current and future missions
  in near-real-time in EUMETSAT’s Offline Environment
  to compare and inter-calibrate these imagers
  Analyse of their medium- to long-term trends
  Supports generation of Fundamental Climate Data Records
  Rationalises resources and efforts
  Coordinates calibration activities across RSP

## Slide 13
Thank you