## Slide 1
Introduction to Mini Conference & GSICS
Xiuqing Hu, Dohyeong Kim, Fangfang Yu
GRWG Chair

## Slide 2
Overview of GSICS

## Slide 3: Background of GSICS
The Global Space-based Inter-Calibration System (GSICS) :
initiated in 2005 by the WMO and the CGMS
was recognized in 2009-2011 as a Pilot Project in the Demonstration Phase of the WMO Integrated Global Observing System(WIGOS)
GSICS
SCOPE-CM
Satellite
Data
Consistent
Calibrated
observations
Essential
Climate
Variables
User &
Organizations
Satellites
& Sensors
GCOS

## Slide 4: GSICS?
Space-based observations from various satellite missions must be precisely calibrated with similar methods against common references
Poor or inhomogeneous calibration results in degraded performance and lower benefits
CGMS members are collaborating within GSICS to develop and apply “best practices” for homogeneous calibration
ensures consistent calibration of satellite measurements and tie the measurements to SI reference standards
defines and implements procedures for operational, in-orbit satellite inter-calibration;
relates the measurements of one instrument to those of a reference instrument with a stated uncertainty.
The overlapping records of two satellite instruments can be compared once a number of effects, such as diurnal cycle, are taken into account.
GSICS inter-calibration allows biases to be removed among satellite measurements.
coordinates the systematic generation to correct the individual calibration(Level 1)
a range of activities related to:
  Instrument Level 1 data monitoring
  comparison with references
  routine generation of corrections in near real-time
  provision of algorithms enabling recalibration of archived data
  traceability to absolute calibration standards
  prelaunch instrument characterization
  post-launch instrument validation
  documentation on state-of-the-art calibration techniques
Why GSICS?
What is GSICS?
Scope of GSICS?

## Slide 5: Who benefits from GSICS ?
Satellite operators
  Sharing development effort and resources (calibration references, datasets, software tools)
  Capacity building (best practices for instrument monitoring, traceability, sensor comparison and correction)
  Improved instrument assessment, faster identification and correction of anomalies, facilitating commissioning and operation
  Interoperability within the CGMS constellation
Satellite data users
  Improved calibration
  Interoperability through inter-calibration
  Assessments, reports, for better understanding
  Algorithms enabling to reprocess data records
  GSICS leverages the value of individual missions

## Slide 6: Evolving scope of GSICS
Started with IR calibration corrections (GEO-LEO)
Continued with VIS/NIR domain
Now addressing also the UV and MW domains
Started with Near Real-Time correction functions
Added Re-analysis corrections
Considering now a wider variety of deliverables depending on user requirements
  New special session reprocessing/Recalibration will initiate in this annual meeting
  Space weather instrument inter-calibration from CGMS-44 last year
  And others…

## Slide 7: GSICS Services and Tools
General information services
Specific tools
  GSICS portal maintained by WMO (http://gsics.wmo.int)
  GCC website maintained by the GSICS Coordination Center
  GSICS related websites maintained by each member agency
  GSICS User Messaging Service managed by the GCC
  GSICS Product Catalogue
  GSICS Quarterly newsletter
  GSICS User Workshop
  GSICS Wiki providing access to technical documentation (ATDB of each product and recording presentations from the GRWG and GDWG meetings)
GSICS Data and Products Servers (at EUMETSAT, NOAA, CMA)
GSICS product generation framework and products format checker
GSICS Implementation of the ROLO Model (GIRO) lunar calibration software and associated GSICS Lunar Observation Dataset
Various software tools(Bias plotting tool)
New tool is ready by CMA for extracting SNO and PICS sub-dataset from some typical instruments (MODIS, MERSI)

## Slide 8: GSICS deliverables
Core GSICS inter-calibration products
Instrument behaviour assessment
Instrument correction algorithms
Science resources
Solar & lunar spectra
Target characteristics
Calibration datasets
etc.
Spectroscopy database, RTM
Standards & procedures
Near Real Time corrections
Time–centered corrections
Bias adjustment sequences(archive)
GSICS tools
Monitored instrument
Metadata & Data Formats
Standard vocabulary
Procedures
etc.
References (benchmarks)
Users
User services
SNO matchup
Ray matching
Bias monitoring
Plotting, readers
etc.
Registration, messaging
Product catalogue
Data servers
wiki, website
Documentation info, etc.

## Slide 9: GSICS Members
USGS/NOAA
NASA/NIST
ROSHYDROMET
CMA
IMD/ISRO
JMA/JAXA
KMA
EUMETSAT
Obs. ESA, CEOS(WGCV)
ASSO. GPM X-cal
WMO
14 Members Worldwide
CNES

## Slide 10: GSICS Structure
GSICS Exec Panel
GSICS Coordination Center
GSICS Research Working Group
GSICS Data Working Group
UV Sub-Group
IR Sub-Group
WGCV IVOS
WGCV MWSG
GPM X-CAL
WGCV ACSG
VIS/NIR Sub-Group
Microwave Sub-Group
CGMS satellite operators
CGMS satellite operators
CGMS satellite operators
CGMS satellite operators
WMO

## Slide 11
Highlight of GSICS activities

## Slide 12: IR Product Development within GSICS (IR)
GEO-LEO IR hyperspectral
  Progress existing products to Operational Status
  Promote new products to Demonstration Status
  Application of Prime GSICS Correction concept
    To merge multiple reference instruments
    To allow corrections to cover diurnal cycle
Scope potential new GSICS products/deliverables
  Alternative inter-calibration algorithms
  Retrieved SRFs
  GEO-GEO inter-calibration (part of GEO-ring)
  LEO-LEO inter-calibration
Traceability of Reference Instruments
  Plans for TANSO-FTS/2 & CLARREO
  GSICS IR Reference Sensor Traceability and Uncertainty Report

## Slide 13: DCC calibration Status (VIS/NIR)
Started in 2014
  NASA Langley provided all GPRCs verification data to validate the proper implementation according to ATBD submitted in 2011
The DCC method has been implemented by all GPRCs by 2015 and reported on their status and issues of the implementation
The DCC methodology provides excellent estimate of the relative degradation of the monitored instrument, however the GEO domain specific DCC methodology noise can be reduced by adjusting DCC methodology components as needed
1) DCC BRDF
  KMA has also evaluated RTM based method developed by SNU
  CNES has defined the more Lambertian part of the BRDF
2) DCC deseasonalization
  NOAA, EUMETSAT, CMA have developed methods
3) DCC statistics and identification (to provide sufficient sampling)

## Slide 14: Improving the lunar reference
Improvement of the reference standard for lunar calibration
  to improve absolute accuracy
  to reduce residual geometry dependencies (phase, librations)
The reference irradiance is generated for each observation of the Moon taken by an instrument by computing the lunar model(ROLO, GIRO)
Requirements for Absolute Lunar Calibration Reference
  reprocessing the ROLO telescope dataset using new algorithms
  incorporating reliable new observational data e.g. PLEIADES
  lunar radiometry e.g. SNPP VIIRS
  collecting new radiometric measurements of the Moon
  requirements:
    high-accuracy, with traceability to SI
    full spectral coverage at moderate spectral resolution
    photometric geometry coverage (phase and librations) sufficient for high-precision modeling

## Slide 15: Operational coordination
Development Phase
GOES-sounder, FY2E-2H, FY-4A
EUM (MET-7), JMA(Himawari-8), KMA(COMS), ISRO(INSAT-3D)
Pre-operational Phase
GOES-13, 15 (NRT&RAC). GOES-11, 12 (NRT)
Operational Phase
EUMETSAT(Meteosat 8-11/IASI)
Demonstration Phase
GSICS Procedure for Product Acceptance
(based on QA4EO, a series of reviews over period of ~1.5yr)

## Slide 16: Where to get the data?
GSICS Bias Monitoring
  Hosted on websites of GSICS Processing & Research Centres (GPRCs)
  http://gsics.tools.eumetsat.int/plotter/
GSICS Corrections
  − GSICS Data & Products Servers
  − THREDDS-based system
  − NetCDF format
  − WMO GTS standard file names
  − Unidata & CF conventions
  See gsics.wmo.int for links
GTS = Global Telecommunication System
CF = Climate and Forecast

## Slide 17: Conclusions
GSICS is maturing into a system for generating inter-calibration products
suitable for integrating into operational processing
First products have been declared operational
Continuing to develop new inter-calibration products
While cooperating with related activities
To integrate GSICS into WIGOS
To support Architecture for Climate Monitoring from Space
Today: Examples of potential future activities & interactions
Rest of the Week: Focus on development of GSICS deliverables

## Slide 18
Mini Conference

## Slide 19
Mon am | Mini Conference |  |  |  | 
 | Chair: Philippe Goryl, Minutes: XXX |  |  |  | 
8:10 | Coffee and Registration |  |  |  | 
8:25 | Mitch Goldberg | NOAA | GSICS |  | 0:05
8:30 | Philippe Goryl and Nicolaus Hanowski | ESA | Welcome address | 1a | 0:05
8:35 | Xiuqing (Scott) Hu | CMA | Introduction to Mini Conference & GSICS | 1b | 0:15
8:50 | Jerome Bouffard | ESA | Logistics information | 1c | 0:10
9:00 | Henri Laur | ESA | ESA EO Programme | 1d | 0:30
9:30 | Pascal Lecomte | ESA | ESA CCI (Climate Change Initiative) Programme | 1e | 0:15
9:45 | Xiangqian (Fred) Wu | NOAA | GOES-16/-17 ABI Calibration Performance and Updates | 1f | 0:15
10:00 | Philippe Goryl | ESA | Fiducial Reference Measurements Concept | 1g | 0:15
10:15 | Jonas Von Bismarck | ESA | Aeolus Mission Status | 1h | 0:20
10:35 |  |  | Coffee break |  | 0:25
11:00 |  |  |  | 1i | 0:20
11:20 | Jerome Bouffard | ESA | Toward FCDR and uncertainties information for Altimetry | 1j | 0:20
11:40 | Stefan Adriaensen | VITO | Lunar Calibration Update | 1k | 0:20
12:00 | Bill Bell | ECMWF | ECMWF Copernicus Activities Related to Inter-calibration | 1l | 0:30
12:30 | Nigel Fox | NPL | Quality Assurance for EO and CEOS Activities | 1m | 0:30

## Slide 20: Notes to speakers
Please follow file naming convention: 1a_Hewison_Introduction.pptx/pdf/ppt
Presentations will be uploaded to the GSICS Wiki
  Unless you tell me not to
All slots are strictly 20min
Please leave at least 5min for questions
The chair will give a warning after 13min
Thank you!

## Slide 21
Thank you!