## Slide 1: ABI Calibration Performance
X. Wu
NOAA/NESDIS/STAR and GOES-R CWG
2019-03-04
Photo courtesy GOES-R Program

## Slide 2: Acknowledgement & Disclaimer
Mason Black, Changyong Cao, Jim Carr, Monica Coakley, Monica Cook, Frank DeLuccia, Jon Fulbright, Bruce Gibbs, Mat Gunshor, Song Guo, Dave Igli, Liz Kline, Vladimir Kondratovich, Dan Lindsey, Joel McCorkel, Frank Padula, Haifeng Qian, Alan Reth, Matt Seybold, Tim Schmit, Bin Tan, John van Naarden, Zhipeng Wang, Robert Wolfe, Hyelim Yoo, and Fangfang Yu
Personal opinion, not official positions, policy, or decisions of the NOAA or the U. S. Government.

## Slide 3: GOES-16 ABI Full Validation June 2018
Photo courtesy GOES-R Program

## Slide 4
GOES-17 ABI Provisional Nov. 2018
Photo courtesy GOES-R Program

## Slide 5: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 6: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 7: Navigation Accuracy
Chart: Navigation Errors For Selected Channels Not During Eclipse (μrad)
Baseline | 10.4 | 10.1 | 10.5 | 10.3 | 10.6 | 10.4 | 11.4 | 11.3 | 11.9 | 12.5
G16 Full | 3.92 | 0.72 | 2.69 | 1.9 | 5.5 | 3.2 | 8.2 | 4.5 | 9.4 | 5.1
G17 Prov M3 | 2.9 | 3.8 | 5.9 | 4.5 | 14.7 | 12.4 | 19 | 15.4 | 20.8 | 22.3
G17 Prov M4 | 3.5 | 4 | 4.8 | 5 | 13 | 15.4 | 18.1 | 13.2 | 15.8 | 16.7
G17 Prov M6 | 3.4 | 2.9 | 6 | 3 | 11 | 9.4 | 10.1 | 12.8 | 15.4 | 16.2
Met MRD.
Better than G16 @ Provisional (not shown) but not yet at par with G16 @ Full Validation.
Similar conclusions for accuracy during eclipse, Channel-to-Channel, Frame-to-Frame, and Swath-to-Swath co-registration (not shown).

## Slide 8: VNIR Stars Comparison (PM – CENRAIS, 7/10)
Legend: VNIR star residuals by GRITT (blue) in EW (upper panel) and NS (lower panel) directions are in good agreement with the mean (solid) and 3-σ (dashed) of the CENRAIS-measured VNIR daily navigation residuals (in red).
-0.07
-0.55
2.5 m!
Verified the method of evaluation.

## Slide 9: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 10: VNIR Noise
Chart: Signal-to-Noise Ratio (SNR) @100% (except for 0.64 Low). Higher is better.
| 0.47 | 0.64 | 0.64 99% | 0.64 Low*10 | 0.86 | 1.38 | 1.61 | 2.25
MRD | 300 | 150 | 300 | 200 | 300 | 300 | 300 | 300
Baseline | 349 | 247 | 311 | 442 | 470 | 937 | 564 | 1008
G16 Prov Min | 650.24 | 260.8 | 350 | 300 | 563.02 | 875.94 | 447.08 | 885.79
G16 Prov Mean | 1140.62 | 427.17 | 430 | 480 | 766.75 | 1057 | 606.86 | 1050.47
G17 Prov Min | 970 | 373 | 393 | 658 | 267 | 333 | 604
G17 Prov Mean | 1164 | 473 | 488.5 | 774 | 1082 | 619 | 1088
Band 1-3 are comparable to G16.
For Channels 4-6, means are comparable to G16, suggesting BDS issue.

## Slide 11: VNIR Noise Stability

## Slide 12: VNIR Accuracy
Chart: Difference From Reference (%)
| 0.47 | 0.64 | 0.86 | 1.38 | 1.61 | 2.25
G16 Prov | 4.2 | 7.3 | 1.7 | -5 | 4.5 | -0.2
G16 Full | 4.7 | 6.7 | 1.5 | -0.5 | 3.8 | 0.5
G17 Prov | -0.66 | 8.85 | 0.42 | -3.18 | 5.45 | -2.8

## Slide 13: VNIR Accuracy Stability
Gain Variation
Good Instrument.
Unstable Ground.
Post-Drift

## Slide 14: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 15: LHP Anomaly & FPM Temperature
GOES-16
58.3K – 58.5K
GOES-17
81K – 105K
And other optical parts, including
Internal Calibration Target
Scan mirrors.

## Slide 16: IR Noise
Chart: Noise Equivalent delta Temperature (NEdT, mK) @300K. Lower is better
| 3.9 | 6.19 | 6.95 | 7.34 | 8.5 | 9.61 | 10.3 | 11.2 | 12.3 | 13.3
MRD | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 300
Baseline | 70 | 20 | 19 | 31 | 24 | 30 | 58 | 33 | 37 | 107
G16 Prov Mean | 80 | 13 | 15 | 25 | 18 | 20 | 28 | 25 | 22 | 29
G17 Prov Max | 106.6 | 95.4 | 84 | 151.8 | 121.2 | 368 | 92.7 | 73 | 138.1 | 1107.4
G17 Prov Mean | 88.3 | 22.5 | 22.2 | 42.6 | 22.6 | 110 | 36.5 | 30.2 | 94 | 349.6
All worse than G16, as expected.
Especially for longer wavelength channels.

## Slide 17: IR Bias under “Best” Condition
Chart: G17ABI (Gain Set=1)/G16ABI vs. CrIS/IASI, Night Time
| B07 | B08 | B09 | B10 | B11 | B12 | B13 | B14 | B15 | B16
NPPCrIS-G17 | 0 | 0.475 | 0.049 | -0.035 | 0 | -0.083 | -0.124 | -0.152 | 0.015 | 0.449
N20CrIS-G17 | 0 | 0.477 | 0.086 | 0.002 | 0 | -0.064 | -0.057 | -0.099 | 0.061 | 0.469
IASI-B - G17 | -0.023 | -0.102 | 0.054 | -0.029 | -0.02 | -0.118 | -0.07 | -0.081 | 0.046 | 0.413
IASI-A - G17 | -0.078 | -0.18929 | 0.020238 | -0.064163 | -0.0015954 | -0.11085 | -0.042056 | -0.067746 | 0.052315 | 0.44892
NPPCrIS-G16 | 0 | 0.234 | -0.15735 | -0.074418 | 0 | -0.05728 | -0.08174 | -0.019712 | -0.025854 | -0.16577
IASI-B - G16 | -0.021109 | -0.13552 | -0.15538 | -0.080591 | -0.08099 | -0.1187 | -0.07383 | -0.010661 | -0.016439 | -0.19574
Overall within ~0.1K for most channels. Comparable with G16, except for B16
Limited coverage of ABI B07 & B08 by CrIS.

## Slide 18: Time-Series of GEO-LEO IR Inter-Calibration (best condition: Gain Set=1, Night-time Collocations)
Long-term stable

## Slide 19: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 20: Typical GOES-17 ABI NEdT
INST-CAL CWG
The NEdT is converted to 300 k. Its ICT temperature dependency is clearly reduced for bands 8-15.

## Slide 21: Typical G17 ABI FPM Temp and Performance
ICT look saturation
SL look saturation
NEdT exceed Spec.
Gain set I
INST-CAL-ENG FPM temperature has known ~1.5 K cold bias
Gain set III: increased NEdT

## Slide 22: Estimate of G17 ABI Performance
Courtesy of Vendor-flight for modeled FPM temperatures

## Slide 23: GOES-17 ABI Actual Performance Band 8
scan mirror temperature LUT insufficiency
cryocooler anomaly 1 & 2
Late gain set III turned on
data gap
data gap due to orbit drift
1

## Slide 24: GOES-17 ABI Actual Performance All Bands

## Slide 25: GOES-16 ABI Actual Performance All Bands

## Slide 26: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 27: The Problem: Unstable Thermal
IR (and MW) sensors need frequent calibration.
  Before the thermal environment has changed too much.
G17 thermal can change too fast.
  Cannot be calibrated more frequently.
~300 counts in ~600 min. or 0.25 cnt/splk
~8000 counts in ~300 min. or 13 cnt/splk

## Slide 28: The Solution: Predictive Calibration
Instead of using the last measurement until the new one is available, extrapolate the last two to a future time, i.e., predictive.
Other relevant information:
  Wish to interpolate, but can’t wait.
  Tried but abandoned nonlinear predictions.
    Likely because of measurement noise.
  Similar to those for Imager & Sounder since 1990’s.
  Recovered significant amount of data (see next).

## Slide 29
2018-08-29 data.
CONUS (frequent comparison)
Cos(VZA) difference < 2%.
Pixel-to-pixel for the two satellites
The Results: GEO-GEO Evaluation

## Slide 30
Stray light
Sun Glint
Forward and backward scattering
Excellent agreement, with the expected (and symmetric) differences.
Ignore for now whether and why predictive is cooler than operational.

## Slide 31
Improved by the Predictive Cal
Artifacts that can be corrected easily
Effort to guess the gain when the blackbody look is saturated

## Slide 32: Outline
Start with GOES-17 ABI L1b Provisional:
  A good summary of GOES-16 ABI performance since it was used as reference
Loop Heat Pipe (LHP) Anomaly
  Geometric calibration – Not affected.
  VNIR calibration – Not affected (well, not quite).
  IR calibration – Seriously affected, so focus on the stable period first.
Progress since then
  Estimate and actual performance
  Predictive calibration
  Dependence of VNR gain on FPM temperature
  De-striping

## Slide 33
Task ABI NSS
Uniform Target
How It Works
Apply grel to L1β
Improved Image Quality
Derive Relative Gains
Conduct NSS Data Analysis
All Detectors Over a Given Target

## Slide 34
Channel 1
Original
Average Streaking Metric Ratio: 0.00390

## Slide 35
Channel 1
Destriped
Average Streaking Metric Ratio: 0.00260

## Slide 36
Channel 2
Original
Average Streaking Metric Ratio: 0.00768

## Slide 37
Channel 2
Destriped
Average Streaking Metric Ratio: 0.00224

## Slide 38
Channel 3
Original
Average Streaking Metric Ratio: 0.01096

## Slide 39
Channel 3
Destriped
Average Streaking Metric Ratio: 0.00438

## Slide 40
Channel 4
Original
Average Streaking Metric Ratio: 0.02118

## Slide 41
Channel 4
Destriped
Average Streaking Metric Ratio: 0.00505

## Slide 42
Channel 5
Original
Average Streaking Metric Ratio: 0.01078

## Slide 43
Channel 5
Destriped
Average Streaking Metric Ratio: 0.00412

## Slide 44
Channel 6
Original
Average Streaking Metric Ratio: 0.01575

## Slide 45
Channel 6
Destriped
Average Streaking Metric Ratio: 0.00546

## Slide 46: JARS Special Issue on INSTRUMENT CALIBRATION AND PRODUCT VALIDATION OF GOES-R
The R-Series of Geostationary Operational Environmental Satellite (GOES-R) is a new generation of satellite that the National Oceanic and Atmospheric Administration (NOAA) operates to provide continuous surveillance of the land, ocean, and atmosphere of the United States of America and its environment. GOES-R was launched in November 2016. It became operational as GOES-16 in December 2017, supporting NOAA’s GOES-EAST mission. GOES-S was launched in March 2018. It will become operational as GOES-17 in January 2019, supporting NOAA’s GOES-WEST mission. With the successful deployment of GOES-R instruments and dissemination of its products, the Journal of Applied Remote Sensing will devote a special section to document the instrument calibration and product validation of GOES-R sensors. Calibration of all instruments onboard the GOES-R are welcome, including Advanced Baseline Imager (ABI), Extreme Ultraviolet and X-ray Irradiance Sensor (EXIS), Geostationary Lightning Mapper (GLM), Magnetometer (MAG), Space Environment In-Situ Suite (SEISS), and Solar Ultraviolet Imager (SUVI). Validation of all GOES-R products are welcome, including Level 1b, Level 2, and beyond. Relevant studies of similar instruments and products, for example the Advanced Himawari Imager (AHI) onboard the Japan Meteorological Agency (JMA) satellites and the Advanced Meteorological Imager (AMI) onboard the Korea Meteorological Agency (KMA), are also encouraged to submit. To submit to this special section, please prepare the paper according to JARS guidelines and submit via the online submission system ( https://jars.msubmit.net). Cover letter should indicate that the submission is intended for this special section. Papers in this special section have the option of publishing with open access. Papers will be peer reviewed in accordance with the journal’s established policies and procedures. Peer review will commence immediately upon manuscript submission, with a goal of making a first decision within 6 weeks of manuscript submission. Special sections are opened online once a minimum of four papers have been accepted. Each paper is published as soon as the copyedited and typeset proofs are approved by the author.

## Slide 47: Summary
G16 performs nominally.
  Strong support for G17 evaluation via GEO-GEO.
G17 geometric calibration performs nominally.
  Greatly helped by lessons learned from G16.
G17 VNIR calibration performs nominally overall.
  Need to correct the dependence of VNIR gain on FPM temperature
G17 IR calibration is compromised by the LHP anomaly.
  When the FPM temperature is stable:
    Bias is comparable to G16 except for B16.
    Noise is much higher than G16, sometime higher than requirements, but remain useful for many applications.
  When the FPM temperature is unstable:
    L1b cannot be generated for some channels during some hours of the day and day of the year.
    Performance are being estimated and monitored.
    Predictive calibration can recover some of the lost data.
Encouraging progress in de-striping using the NSS.