## Slide 1: Lunar irradiance measurement and modelling for absolute radiometric calibration of EO sensors
Stefan Adriaensen (VITO), M. Bouvet (ESA), Emma Woolliams (NPL), Claire Greenwell (NPL), Maria Garcia Miranda(NPL), Carlos Toledano (Univ. Valladolid), Alberto Berjón (Univ. Valladolid), África Baretto (Univ. Valladolid)
ESA – ESRIN- GSICS – 04/03/2019
Lunar Calibration Update

## Slide 2
Presentation outline
Project Overview
  Goal/Purpose
  Consortium and tasks
Instruments
Location
Instrument Calibration
Operations
Measurements
Uncertainty
Modelling
Model vs measurements
Comparison with EO sensors

## Slide 3
Project Overview : goal
Define a strategy for lunar irradiance measurements
Acquire and calibrate a capable instrument
Install at a location with optimal atmospheric conditions and make operational
Store the irradiance measurements in a database system
Model the irradiance based upon knowledge, target sub 2% absolute radiometric accuracy
Compare the model irradiance with space based lunar irradiance measurements

## Slide 4
Project Overview : consortium and tasks

## Slide 5
Instruments
Irradiance measurements
  the Sun-Sky-Lunar photometer CE318 from CIMEL designed for night aerosol retrieval and adapted specifically for this project:
  Spectral channels: 340, 380, 440, 500, 670 870, 936, 1020, 1640 nm
  Double filter wheel for polarimetric measurements
  Modification of firmware for polarimetric capabilities in direct lunar observation configuration
  Installed and operational since April 2018
Spectral Measurements (for spectal smoothing the model output)
  ASD field spectrometer ( >1800nm)
  Pandora 2S

## Slide 6
Location
On Island Tenerife (Spain) in the North Atlantic Ocean
Pico Teide (3555 m)
Izaña : Atmospheric Research Center (2391 m)
Very stable and ‘clean’ atmosphere
+100 measurements per year
  Sahara dust events
  Weather conditions on the Peak Teide
Aerosol Optical Loading (500nm) between 0.007 and 0.1

## Slide 7
Location

## Slide 8
Instrument Calibration
Full instrument calibration conducted at NPL, in cooperation with Uva
  Linearity
  Irradiance & Radiance Responsivity
  Temperature characterization
  Reference plane
NPL SI traceability
Miners lamp
Calibration Setup : irradiance responsivity measurement

## Slide 9
Operations
Develop an automated processing scheme for deriving lunar spectral irradiance measurements
Archive the raw data
Process the raw data into lunar spectral irradiance measurements
Build a database of lunar spectral irradiance measurements

## Slide 10
Measurements
Nighttime irradiance measurement of the Moon
Well calibrated instrument
Iterative Langley plot
Based upon relationship
              V instrument output signal
              atmospheric attenuation (lunar zenith angle)
              V0 top of atmosphere signal
TOA irradiance can be determined from a set of 2 (or more) measurements
Atmosphere condition is assumed constant : linear regression for relationship between instrument and TOA signal
Changes in atmosphere are minimized due to high altitude
Correction for change in phase, sun – earth - moon distances

## Slide 11
Measurements
About 400 irradiance measurements
Combination
  2 datasets of 2 instruments
Clean but outliers
Plot : irradiance against phase angle
Increased uncertainty in low phase angles
440nm

## Slide 12
Uncertainty
calibration
Langley TOA signal
model

## Slide 13
Modelling
Based upon the work done by USGS : Kiefer and Stone 2005
  Phase angle
  Solar selenographic lon, observer selenographic lat and lon
Linear and non-linear part in the equation
  Specific regression methods for both parts
  First linear part, non-linear part based upon residuals
Outliers need filtering, big influence on regression result
Iterative procedure : removal of the outliers, then refit
Conversion of reflectance to irradiance using solar irradiance

## Slide 14
Model vs measurements

## Slide 15
Comparison with EO sensors and model
Currently under development
Similar approach as Kieffer and Stone but less spectral bands in the model
Spectral smoothing based upon EO instrument spectral response
ASD measurements to asses Apollo sand spectra and possibly replace
PROBA-V and PLEIADES lunar acquisitions are currently baseline
  Candidates from GLOD
  GIRO
Lunar irradiance image PROBA-V 06/09/2017

## Slide 16
Thank you !