## Slide 1
Google
Quality Assurance for EO and CEOS activities Professor Nigel Fox
Head of Earth Observation, Climate and Optical, NPL
Chair CEOS WGCV IVOS sub-group

## Slide 2: CEOS WGCV IVOS: Vision
To facilitate the provision of ‘fit for purpose’ information through enabling data interoperability and performance assessment through an ‘operational’ CEOS coordinated & internationally harmonised Cal/Val infrastructure consistent with QA4EO principles.
Pre-flight characterisation & calibration
Test – sites - post-launch Cal/Val
Comparisons – satellites/validation systems
Agreed methodologies
Community Good Practises
Interchangeable/readable formats
Results/metadata - databases
Key Infrastructure to be established and maintained independent of sensor specific projects and/or agencies

## Slide 3: Work plan
Structured into themes and led by ‘champions’
Look to develop good practises
  Organise comparisons
  Shared learning (research activities)
  Shared infrastructure / tools / Methods
  Recommendations as needed
THEMATIC AREAS
Land surface reflectance
Ocean colour (link to IOCCG, VC-OCR etc)
Surface Temperature (link to VC-SST, GHRSST)
Geo spatial image quality
Atmospheric Correction (Link to AC subgroup)
RT codes (context of IVOS use in calibration)
PROJECTS
RadCalNET
PICSCAR (with GSICS)
Lunar (with GSICS)
Surface Temperature Comparisons (with VC-SST & LPV)
Ocean Colour Comparison (with VC OCR) ARD (with LSI-VC)
Vocabulary
Harmonised Level 1 community reference (with GSICS)
SI traceable reference satellite (with GSICS)

## Slide 4: Satellite Data Products: Knowledge/information
Desire
Many sensors
Similar products
Observations on
demand’ (nano-sats)
Trustable for decades
User confidence
Challenges
Different algorithms
Limited validation data
Data similar but different
Scene/pixel dependent Uc
Lack of standardisation /
interoperability
Europe

## Slide 5
Core principles of CEOS QA4EO are starting to be implemented in new: missions, data sets and associated Cal/Val activities across all agencies (not necessarily using the name), although some additional metrological rigour at an early stage could reap major benefits in the future.
Significant effort still needed to ensure the principles can be fully implemented, particularly for Level 2 and higher.
and ins support of Analysis Ready Data, New space providers etc.
Sensor to sensor interoperability and short/long time series of data, not only for climate but other operational services, are of increasing importance. These require the creation of Fundamental (Climate) Data Records, F(C)DR ideally incorporating historic data from sensors which were developed prior to the Cal/Val rigour now expected.

## Slide 6
(Draft definition under consideration by CEOS/CGMS Working Group Climate during 2018:) An FCDR consists of a long, harmonised record of uncertainty-quantified sensor observations that are calibrated to physical units and located in time and space, together with all ancillary and lower-level instrument data used to calibrate and locate the observations and to estimate uncertainty.
How to define a Fundamental
(Climate) Data Record? (FCDR)
Note
The term Fundamental Data Record may be applied to records meeting similar standards to an FCDR, but which is either too short to be informative about climate variability and change, or whose contents are relevant for purposes not considered to be climate applications. (Logically, one should define FDR as the baseline concept and add climate-specific requirements to define FCDR, and this may yet be recommended.)

## Slide 7: Fundamental Climate Data Records (FCDRs) are the foundation of all satellite derived climate information
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Calibrated radiances (L1)
Raw satellite data (L0)
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Through processing and analysis they are used to derive climate information for decision makers
Creating an FCDR

## Slide 8
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Calibrated radiances (L1)
Raw satellite data (L0)
Metrological rigour for climate data requires metrological processes for FCDRs
(Similar for FDRs used for other applications)
Traceable uncertainties allow trust in data
Flow of uncertainty from FCDR to final product
Uncertainties due to each processing step
Raw satellite data (L0)
Calibrated radiances (L1)
Liability
Insurance
Decision
Climate index / information
Gridded CDR (L3)
Climate data record (L2)
Analysed / processed (L4+)
Traceable Uncertainties

## Slide 9: What is Traceability?
Documented evidence of degree of consistency with international std & Uc budget
i.e.COMPARISONS
GUM

## Slide 10: Lead project to establish QA framework for EU C3S

## Slide 11: Quality Assurance Report
The QAR will document the type of uncertainty characterisation and its method:
through validation
partial algorithm propagation
statistical
fully metrologically propagated

## Slide 12: Quality Assurance Report
Every measurement has an uncertainty.
To validate the satellite data, the satellite measurement and its uncertainty should be compared with the reference data and its uncertainty.
The confidence in each measurement allows you to compare the two more meaningfully.

## Slide 13: Quality Assurance Report (QAR)
Why have a QAR?
Standardised form makes it easy for users to compare data products
Covers key product information and contains references to more detailed information
Aims to guide product producers on the information that should be provided with a data product

## Slide 14
-> To understand whether the product producer provides sufficient information to allow a user to fully understand the status of the data product and to determine if best practices are being followed in generating the product
Quality Assurance Evaluation

## Slide 15: QA matrix adapted for Level 1 and 2 products

## Slide 16
Band Integrated Radiance
Time (years)
Maintain sensor characteristics in viewing ‘reference’ do not force sensor A to appear to be sensor B otherwise likely to have scene dependent biases
Need to consider the measurement equation of sensor and how it interacts
Incorporating pre-flight information
Notes: EMMA

## Slide 17: Measurement Function Analysis

## Slide 18: Uncertainty Tree
Given the measurement equation we then need to investigate all the possible sources of uncertainty that feed into the final total
Involves thinking about each term in the measurement function and breaking it down into all sub-processes down to the originating process for uncertainty
We represent this process by an Uncertainty Tree Diagram

## Slide 20
Physical effects
Physical effect
Physical effect
Physical effect

## Slide 21
Physical effects
Physical effect
Physical effect
Physical effect

## Slide 22
Physical effects
Physical effect
Physical effect
Physical effect
Physical effect
Physical effect

## Slide 23
Physical effects
Physical effect
Physical effect
Physical effect
Physical effect
Physical effect
Assumptions and approximations in measurement function

## Slide 24: +0 Term
Appears in a number of places
Intended to force investigation of assumptions
  To think about and characterize known unknowns
  Mostly via Type-B uncertainty estimates
Not measured but via expert knowledge (including modelling)

## Slide 25
AVHRR

## Slide 26
Water Leaving Radiance (System Vicarious Calibration for Ocean Colour Sensors

## Slide 27: Effects Table Reporting

## Slide 28
Table descriptor |  | Comments
Name of effect |  | A unique name
Affected term in measurement function |  | Name and standard symbol
Instruments in the series affected |  | Identifier
Correlation type and form | Pixel-to-pixel [pixels] | One of the types
 | from scanline to scanline [scanlines] | 
 | between images [images] | 
 | Between orbits [orbit] | 
 | Over time [time] | 
Correlation scale | Pixel-to-pixel [pixels] | As needed to define type
 | from scanline to scanline [scanlines] | 
 | between images [images] | 
 | Between orbits [orbit] | 
 | Over time [time] | 
Channels/bands | List of channels / bands affected | Channel names
 | Error correlation coefficient matrix | A matrix
Uncertainty | PDF shape | Functional form
 | units | Units
 | magnitude | 
Sensitivity coefficient |  | Value, equation or parameterisation of sensitivity of measurand to term
Notes: What you end up with is a report that contains the uncertainty tree diagram and then an effects table for each of error effect identified, with required explanation

## Slide 29: L1 interoperability
VISION;
To work towards establishing a community agreed reference (s) (potentially, to reflect different applications/observation characteristics) for level 1 TOA radiances/reflectances and the means of how sensors can and should link to it and subsequently communicate results
Objective is to provide a ‘reference’ which allows satellite operators and potentially their customers to readily obtain information relating to the radiometric calibration (initially Level 1) of a sensor and its relationship with others in a consistent manner but interpretation (and any other actions) is responsibility of individual agencies who have appropriate expertise
Users
  satellite operators (public agencies and commercial) – informing them on calibration status
  Users of L1 data products (e.g. L2 data producers, producers of data cubes, climate data records ..) to help obtain consistency across sensors and between bands – over time and for sensor independent products

## Slide 30: A to B via C How? Uc?
Transfer of comparisons
“Chains of comparisons”
Combining all available data
?
A
B
C
Moon/PICS
PICS?
Defined Ref sensor?

## Slide 31: What are the elements of a system to deliver?
Understanding user needs and the characteristics of sensors that would use the ‘service’
- who wants it?, why? and what must it be able to do?
- data cubes, ARD, FCDR creation, data gaps, constellations
A means to formulate a reference (s) and assign its associated uncertainty
– Internationally acceptable standard (proxy for SI)
- Test-site, Reference sensor, virtual sensor, combo….
The means to link sensor measurements to the reference and its associated uncertainty (‘Comparison’) – The process
    Tools to achieve (SBAFs, Ref. Solar Irradiance, Mathematics…),
Communication of information (data, results and methods)
– Useability and awareness
Governance, review mechanisms, quality control, maintenance…
.- Community acceptance

## Slide 32
Angles of illumination and observation
Chart: 
TOA reflectance/
radiance
Chart: 
Spectral response function
Atmospheric transfer
- standardise?
- comparison (ASIX)
- New ‘community code’
‘Eradiate’
’
Spectral BRDF of ground
- high resolution spectral reflectance
TOA spectrometer / measurements?
- Community model? Parametrisation inputs
Solar Irradiance
PICSCAR
PICSCAR
Then consider the ‘real world’

## Slide 33: RadCalNet
Baotou
La Crau
Railroad Valley
TOA nadir-view hyperspectral (400 - 2350 nm) reflectance every 30 minutes Individual site measurements documented & traceable
Modelling of TOA nadir-view reflectance
Site permanent monitoring (radiometry and atmosphere/weather)
Site Characterisation
Gobabeb
Operational and open to public In July 2018
First two week 16 new users,
13 countries
26 downloads
Now >200 users

## Slide 34: PICSCAR
Project to collaborate on characterising PICS for monitoring stability and sensor
to sensor comparison, also linkable to RadCalNet for traceability
- BRDF model (use of and development)
- Spectral characteristics
- Atmosphere
- Homogeneity
Much community interest
~ 20 participants in workshop:
Comparisons with standardised data
Comparisons with different
surface BRF models
Spectral characteristics to allow tailoring for sensor spectral
bands
- Sat spectrometer data
      - measuring sand samples

## Slide 35: PICSCAR portal to be linked from Cal/Val portal

## Slide 36: PICS characteristics/results Comparison tools

## Slide 37: Establish good practise and community references (MTF)

## Slide 38
Dome C
RadCalNet
PICS
Natural Phenomena
TRUTHS/CLARREO/
China
SI
SI
Ocean Colour
Achieving SI Traceable Cal infrastructure /methods
Establish minimal set of references/methods
Target: Combine information weighted by Uc for particular sensor and application noting individual sensor characteristics
For each method dominant source of uncertainty is systematic ‘absolute level’
and
often unknown effects caused by time differences of observations (e.g. atmosphere, solar/view angle etc
Much of latter can be randomised by multiple observations/corrections <<1%
SNO (or angle matched) can reduce random component significantly minimising number of match-ups needed
Anchors absolute level of methods at TOA constraining models to reduce uncertainties.

## Slide 39: SI traceable validation (FRM4…) mitigate against data gaps & test/anchor FDRs
FRM4SAR
Fiducial Reference Measurements (FRM) are a sub-set of ‘in-situ’ measurements of satellite measured parameters (L1/L2) that can be compared to those independently derived from a satellite to:
Validate the sensor performance and any processing chain
Provide a means to bridge any potential data-gaps
Facilitate interoperability between sensors and
anchor/establish FDRs
    Providing they are of sufficient accuracy!
    (Noting that the comparison process has its own uncertainty)
    FRMs MUST:
    Have documented evidence of metrological traceability to SI (or appropriate international community standard) including full uncertainty budget (instrumentation and useage), which must be at a level commensurate with the application.
    be independent of any satellite geophysical retrieval process.
    Be carried out following community agreed protocols

## Slide 40: Importance of comparisons
Use guidance and best practises of NMIs

## Slide 41
10 types of comparison with 12 participants from 4 continents
8 best practices or protocols
Improved confidence, reliability and global consistency in validation of satellite derived Surface Temperature (Ocean, Land and Ice)
Community Improved knowledge of uncertainty evaluation
Legacy database to store future results
www.FRM4STS.org
WGCV supported by
Has delivered to CEOS agencies and sub-bodies

## Slide 42: 2016 Radiometer comparison
Miami University (USA)
ONERA (France)
University of Valencia (Spain)
University of Southampton (UK)
Qing Dao (China) -1
Qing Dao (China) -2
RAL (UK)
CSIRO (Australia)
KIT (Germany)
DMI (Denmark)
GOTA (Canary Islands
JPL NASA (USA)
Ian Barton (Australia)
MAERI (UofM) viewing NPL ammonia Heat pipe
SISTER (RAL) viewing NPL
ammonia Heat pipe
240 K to 318 K

## Slide 43
Selection of Results of Lab
Radiometer comparison to SI

## Slide 44: WST comparison
University of Valencia (Spain)
University of Southampton (UK)
Qing Dao (China) -1
Qing Dao (China) -2
RAL (UK)
CSIRO (Australia)
KIT (Germany)
DMI (Denmark)
GOTA (Canary Islands)
JPL NASA (USA)
Day & night measurements
Vagaries of UK weather!

## Slide 45: Difference from mean for SST designed radiometers only

## Slide 46: Comparisons of instruments
Ensuring measurements validating of Ocean colour
Are internationally consistent and traceable to SI
Uncertainty analysis with support
Ocean platforms and ship transects
www.frm4soc.org

## Slide 47
Error
is not
Uncertainty
the same as
But also many terms have different interpretations e.g. Harmonisation, bias, Ancillary data ……
IVOS Activity: Also to support wider CEOS WGCV initiative NPL is creating and administering a ‘Wikki’ web page (via Cal/Val portal) to discuss/define terminology and establish ‘thesauras’ of definitions as necessary also with simple graphic/videos to make clear concepts. Incorporating other initiatives such as H2020: FIDUCEO
Small international task group established
Terminology

## Slide 48
Conclusion: FCDRs & FDRs
With more than 35 years of Earth Observation heritage there are many potential FCDRs,
A metrological approach will provide older sensor data with improved accuracy, uncertainties and traceability enabling backward extension of FDRs
Implementing a metrological approach in the near term will provide the next generation of sensors with traceability to ensure ‘fitness for purpose’, multi-reuse of data and risk mitigation
International interoperability through a common transparent QA framework for both agencies and commercial providers will maximise utility & societal benefit.