## Slide 1: GRWG VIS/NIR sub-group briefing report
GSICS VIS/NIR Sub-Group Report, presented by David Doelling
GSICS annual meeting, Frascati, Italy, March 4-8, 2019

## Slide 2: Wish to thank ESA-ESRIN for hosting GSICS meeting
Good to see many European agency based calibration presentations
  Hope to gain new calibration insights

## Slide 3: GSICS and CEOS IVOS recommended solar spectra
Short term approach to construct a solar spectra based on the best solar spectra datasets, which have been scaled to a common TSI reference in the more temporal stable part of the spectra.
  Based on web meetings during late 2017 and early 2018
Kurt Thome suggested that we should be consistent with CEOS and use the Thuillier solar spectra until a new is decided upon
Odele Coddington is presenting the TSIS-1 total and spectral (200-2400 nm) solar irradiance observations VISNIR lunar(4h) and UV group (8d)
Tom Stone leading a discussion on solar spectra for VIS/NIR calibration (4i)

## Slide 4: NPP-VIIRS NOAA V2 product as the GSICS official VIS/NIR Reference
NOAA is the official source of NPP-VIIRS data
At the NOAA VIIRS science team meeting (Aug 2018), we heard that the NOAA team has a version 2 NPP-VIIRS calibration,
  However, due to reprocessing and archive limitations it is uncertain when the dataset will become available.
  Solution to process locally NPP-VIIRS V2 granules over the GSICS calibration domains.
We have Sirish Uprety representing NOAA to present the availability of the NPP-VIIRS NOAA V2 calibrated dataset. (4k)
  Currently being processed at U Maryland and available
We will discuss this in the VIS/NIR session on Wednesday afternoon, the best way to proceed on making this data available (4m)

## Slide 5: Rethinking L1B calibrated radiance datasets
Currently, every time the L1B imager data is reprocessed, which can be yearly, you have to download the whole dataset (TB’s) all over again, which also may take years and resources
If the user could only download the dataset once and apply calibration modules, could save reprocessing and storage requirements
  Must ensure accurate calibrated radiances when applying calibration module
The remote sensing instrument community would release a level 1b dataset that contains all of the required on orbit instrument measurements.
  The calibration module can then be downloaded and applied to update calibration, for example the Terra-MODIS WV detector striping anomaly
  The instrument providers would then provide a calibration module and test dataset to ensure proper implementation, similar to GOME-2 and SCIAMACHY
Two reservations from processing agencies
  the users do not want to apply the calibration module, for small number of granules the calibration could be processed as ordered
  The onboard calibration parameters (detectors, RVS, mirror degradation) are too extensive and perhaps the instrument calibration team loss of control of the dataset
When reviewing papers that use dataset, make sure the authors attribute the project name, product name, version number and doi.

## Slide 6: Spectral Band Adjustment Factor Status
There are 3 VIS/NIR hyperspectral datasets that can be used for SBAF
  SCIAMACHY 30x240 km FOV, mostly complete visible spectra (except > 1.6µm), high resolution spectra
  GOME-2 40x80 km FOV, limited visible spectra, high resolution spectra
  Hyperion 30m FOV, complete spectral range, low spectral resolution, limited sampling
NASA-Langley SBAF tool (web site here)
  You can now plot scene specific spectra, as well as the band specific scatter plots to obtain the SBAF factor
  Spectral band filtering feature. For example use the 1.6µm channel to differentiate between ice and water clouds to compute the SBAF factor for the 0.65µm channel if your sensor has a 1.6µm channel
Rajendra Bhatt will present the updates to the NASA SBAF tool (4q)

## Slide 7: Lunar Calibration Status
Planning 3rd GSICS/CEOS-IVOS lunar calibration workshop in Fall 2019
  to follow the desired two-year timeframe
  Scott will discuss this as part of talk 10b on Friday
Using the Moon to character the sensor MTF effort is being lead by NOAA
On-going benchmarking against ROLO è establishing GIRO’s traceability to the ROLO

## Slide 8: GIRO and GLOD status
GIRO:
  JMA, USGS, KMA, JAXA, CNES, ESA signed agreement (to date)
  VITO being processed
  Draft license sent to ASI (Italian Space Agency) (PRISMA mission due to launch early March)
  JAXA: GIRO successfully applied to GCOM-C/SGLI
GLOD:
  Dataset still to be consolidated and distributed.
  Received data from JAXA for GCOM-C/SGLI

## Slide 9: DCC Calibration Status
Write a GSICS DCC calibration methodology/implementation paper that combines the efforts of all GPRCs
  First on the agenda for the VIS/NIR discussion (4v)
  High priority
Obtain demonstration product status this year
Begin to implement DCC methodology for GEO SWIR bands
DCC product file convention is nearly finalized
Bias plotting package is being developed

## Slide 10: Combining VIS/NIR method calibration gains
Combine the multiple calibration approaches to provide users calibration coefficients with the least uncertainty for their application
GSICS to provide to both lunar and DCC calibration coefficients, as well as an optimized blend
Some methods are suited for stability or calibration transfer, the uncertainties will vary by wavelength
Some methods are best suited for certain retrievals,
  ocean color/aerosols would rely more on Rayleigh scattering

## Slide 11: New VIS/NIR approaches
Advance the Rayleigh scattering approach
  EUMETSAT/Bertrand Fougnie to present and begin formulating Rayleigh scattering approach during VIS/NIR section, should be performed with the UV group
  JMA Rayleigh scattering (4o)
GPRC VIS/NIR priorities
  During the VIS/NIR section we hope to obtain the GPRC priorities in order to prioritize and combine VIS/NIR efforts
The VIS/NIR group has calibration approach leads
  DCC: Dave Doelling
  Lunar: Tom Stone
  Lunar MTF: Fangfang
  If you would like to lead VIS/NIR GSICS calibration approach we would like to discuss this at the VIS/NIR discussion at the end of Wednesday (4v)

## Slide 12: VIS/NIR discussion topics
Working with NOAA to obtain NPP-VIIRS V2 calibrated data
GSICS multi-GPRC DCC calibration paper
Rayleigh scattering calibration approach next steps
Web meeting agenda
GPRC VIS/NIR upcoming priorities