## Slide 1
S. Wagner
In collaboration with
A. Burini, M. De Bartolomei, B. Fougnie, O. Hautecoeur, T. Hewison, E. Kwiatkowska, B. Viticchie
S3B OLCI Lunar Observations

## Slide 2: OLCI : some basics…
Source : ESA web site
Source : ESA web site
Across track = 740 detectors

## Slide 3: OLCI : some basics…
Source : ESA web site
Source : ESA web site
Across track = 740 detectors
Imaging CCD = Spatial x Spectral content
Digital processing  21 bands (+ 1 smear band) over the spatial dimension

## Slide 4: OLCI : some basics…
Cyan = MERIS heritage
Yellow = new bands
Source : ESA web site
Source : ESA web site

## Slide 5: OLCI : some basics…
Cyan = MERIS heritage
Yellow = new bands
Only camera to see the Moon
Very narrow bands
Source : ESA web site
Source : ESA web site

## Slide 6: Moon observation with S3B OLCI
Manoeuvre performed on July 27, 2018
Purpose:
  Straylight correction analysis (ESA / ACRI)
  Moon calibration (EUMETSAT)
Acquisition  between ~5:20 UTC and ~5:25 UTC
Moon phase : -6.46 degrees
Viewing camera = Camera 4
Extract from the original image

## Slide 7: Data preparation for the GIRO
αn
αn-1
βn
f
Irradiance
i = lines (along track)
d = detector index
= solid angle for each detector = (αn - αn-1) . βn
= radiance
OSF = oversampling

## Slide 8: Data preparation for the GIRO
Irradiance
i = lines (along track)
d = detector index
= solid angle for each detector = (αn - αn-1) . βn
= radiance
OSF = oversampling

## Slide 9: Data preparation for the GIRO
Oversampling = ellipse fitting + axis ratio (moon is assumed round)
Not ideal but ok for first-order assessment
Proper calculation needed using integration time + acquisition geometry
Example: Band 1

## Slide 10: Data preparation for the GIRO - oversampling
Inter-band variability peak-to-peak ~1.5%
(excluding Oa21)
Band 21 (without and with enhanced contrast)
Very clean (not perfect) signal for Bands 1 to 20
Band 21 shows clearly the limitation of the method

## Slide 11: Data preparation for the GIRO
Acquisition time for the Moon = interpolation of the time to the central moon acquisition (~5:22UTC)
Satellite position calculated at that time, using orbit propagation  J2000 reference frame
Spectral response functions: 2 cases
  Mean SRF
  SRF for camera 4, detector at the Moon center

## Slide 12: Data preparation for the GIRO
Full set envelop for camera 4
Channel SRF (all cameras)
SRF “sensing” the Moon
Set of SRF for the imagette

## Slide 13: Results – OLCI vs GIRO irradiance

## Slide 14: Results – OLCI vs GIRO irradiance
Relative bias

## Slide 15: MODIS and Pleiades vs “ROLO”
X. Xiong et al., SPIE Proceedings Vol. 9241, 2014
Slightly larger biases than observed for MODIS and PLEIADES

## Slide 16: MODIS and Pleiades vs “ROLO”
X. Xiong et al., SPIE Proceedings Vol. 9241, 2014
Slightly larger biases than observed for MODIS and PLEIADES

## Slide 17: Results – OLCI vs GIRO normalised irradiance
OLCI observation
GIRO simulation

## Slide 18: Results – OLCI vs GIRO normalised irradiance
GIRO drops down whereas OLCI has a smooth behaviour
Significant difference with a change in convexity for the GIRO, not seen with OLCI
Flatter spectral behaviour for OLCI
OLCI observation
GIRO simulation

## Slide 19: Results – OLCI vs GIRO normalised irradiance

## Slide 20: Results – OLCI vs GIRO normalised irradiance
GIRO drops down whereas OLCI has a smooth behaviour  also observed in SCIA
GIRO and SCIA in agreement

## Slide 21: Conclusions and way forward
Good quality of the acquisitions
Some spectral behaviours may require further investigations
Results for Oa21 not understood yet
Reducing the uncertainties on the measurements
  Oversampling factor  ellipse fitting shows some variability + does not work for Oa21
  What about the straylight corrections + offset levels ?  Image reprocessing?
Uncertainties on the GIRO simulations
  SRFs used by the GIRO (first assessment show a limited impact, but varies from band to band)
  Reflectance spectrum smoothing mechanism: investigation on the internal GIRO mechanics to check the model behaviour for very narrow SRFs (Oa13 at 2.5nm, Oa14 at 3.75nm and Oa15 at 2.5nm).
OLCI QWG recommended performing more lunar observations with S3A and S3B for all cameras (29-30 Nov 2018).

## Slide 22: What about SLSTR?
S1
S2
S3
S4
S5
Applicability of the method to SLSTR data still to be assessed
S6

## Slide 23: What about SLSTR? Just a simple try…

## Slide 24
Thank you

## Slide 25
Werhli Spectrum as implemented in the GIRO