## Slide 1: Ice Radiance Method for Sensor Monitoring and Intercomparison
Outline
Justification for using ice surfaces
The monitoring technique
TOA reflectance model
Intercomparison results for OMI, TropOMI, MODIS, OMPS
Glen Jaross | NASA Goddard Space Flight Center
Jeremy Warner | Science Systems and Applications, Inc.
GSICS Meeting – 6 Mar, 2019

## Slide 2: What products benefit most from scene-based calibration ?
Cloud Fractions (λ-independent radiance errors)
  Cloud studies
  Energy balance and UV irradiance
  Cloud height: errors are directly proportional to cloud fraction (low cloud amounts)
  Gas vertical column amounts: Air Mass Factor errors directly related to cloud fraction. ( 3% - 5% column NO2 error per 5% cloud error; low cloud amounts)
Aerosol Properties (λ-independent and λ-dependent radiance errors)
  0.015 error in single-scatter albedo per 1% radiance error
  Optical Depth error 0.06-0.12 per 1%/100 nm λ-dependent radiance errors
Other broad spectral dependences, e.g. NDVI

## Slide 3: Where is scene-based calibration less effective ?
Spectral fitting algorithms (e.g. DOAS)
  Insensitive to low-order-in-λ calibration errors
  Conversion from slant to vertical column still sensitive
Gas abundances (slant column)
  Need knowledge of abundance to calculate expected radiances, but gas abundance depends upon calibration
Limb scattering and Occultation
  Normalizing radiances at a reference height nearly eliminates sensitivity to underlying scene reflectance
  Most instruments do not have a nadir view

## Slide 4
East Antarctica is a good radiance calibration target
Pros
High Reflectance
  high direct / diffuse TOA radiance ratio reduces uncertainty due to atmospheric variations (e.g. aerosols)
  reduced cloud influence
Stable Reflectance (polar vortex keeps ice clean)
Low Aerosol Loading
Small cloud fractions
Uniform reflectance over a large area
  excellent statistics
  applicable to heritage instruments
TOMS / Earth Probe (1996)
90 %
100 %
360 nm Lambertian Reflectivity
Cons
Not totally immune to aerosols
Useful range is 330 nm – 800 nm
  limited by ozone absorption in atmosphere and water absorption in surface
Polar orbiters only
High solar zenith angles magnify small errors
Limited seasonal use

## Slide 5
TOMS Earth Probe
360 nm Lambert-equiv. Reflectivity (1996)
Areas with Slope<0.005 radians
Data Selection Region
Region selected for
low surface slope
high reflectivity
uniformity
little cloud cover

## Slide 6
Time Dependence of radiometric calibration
Seasonal Cycle:
Solstice data are from higher latitudes than at other times (clouds more prevalent ?)
Restrict results to near solstice
Assume reflected signal depends only on SolZA and SatZA
Select reference period near solstice and bin signal in SolZA (and in cross-track swath, if applicable)
Likewise bin other periods (daily or weekly) in the data record
Compute mean in each bin and compute ratio to reference bins
Repeat for Greenland (adjust by 1%)
TOMS / Nimbus 7 (nadir view, 380 nm)
Greenland
Antarctica
×
Reference Period
Normalized Radiance
Nimbus TOMS was calibrated via a Rayleigh scatter method
Pinatubo Effect

## Slide 7
cloud = 5 at 440 mb
Are clouds an issue ?
Modeled nadir-scene
357 mn
775 nm
albedo ratio
GOME (Jan. 2000) nadir-scene
357 mn
775 nm
albedo ratio
Either the cloud model is wrong,
or …
Clouds are statisticallyunimportant

## Slide 8
TOMS / Earth Probe
TOMS / EP experienced anomalous scan mirror degradation affecting solar calibrations
TOMS / Earth Probe 360 nm
Greenland
Antarctica
This TOMS calibrated using solar diffuser measurements
Normalized Radiance

## Slide 9
OMI / Aura
OMI experienced blockage in the nadir detector rows starting early 2009
Greenland
Antarctica
OMI has had no post-launch calibration corrections
62º < SolZA < 67º
360 nm, nadir
354 nm, West swath edge

## Slide 10
OMPS / Suomi NPP
Antarctic radiances are entirely consistent with solar calibration results
Antarctica
No calibration corrections have been applied to OMPS
62º < SolZA < 67º
380 nm, nadir
YEAR
Normalized Radiance
1.02
1.00
0.98
2012
2013
2014
2015
2016
2017
2018
2019
360 nm

## Slide 11
Measurements by Warren et al. at Dome C, 2003-2005
Spectral BRDF of surface 0.35 – 2.5 m
Solar Zenith Angles 52 - 87
Measure spectral transmission of sunlight into snow
in support of radiometric validation for SPOT4
Validation of Absolute Satellite Radiometry
Our Approach
Develop a 2 steradian directional reflectance (BRDF) model for the Antarctic surface (see JGR, 113, 2008)
  surface measurements of total hemispheric reflectance measurements; wavelength-dependent
  surface measurements of reflectance anisotropy; independent of wavelength
Create a look-up table of sun-normalized Top-of-the-Atmosphere (TOA) radiances for all satellite observing conditions using a radiative transfer model (RTM)
Compute ratio between each measurement and table entries; average results
Notes: A common standard means it’s easy to intercompare sensors even if the standard itself is not accurate (it has relative accuracy)

## Slide 12
Warren et al. Reflectance anisotropy derived from 1986-1992 data
Spectral Albedo Measuremnts at South Pole, 1986
 = 600 nm
Sol. ZA = 80
BRDF is likely constant:
300-800 nm
Surface properties based upon reflectance measurements by Warren et al.
BRDF derived from parameterization of measured reflectance anisotropy (Warren et al., JGR 103, E11, 1998)

## Slide 13
Surface BRDF model vs. Solar Zenith Angle
SolZA=40
SolZA=50
SolZA=60
SolZA=85

## Slide 14
RTM handles ozone poorly at  < 330 nm
Comparison between MODIS, OMI, TOMS and model radiances
RTM does not include Ring Effect or O2-O2 abs.
OMI / Aura (Collection 2)
MODIS / Aqua
TOMS / EP
O2O2 Absorption
How do we know this result is correct ?
Nadir-view Results

## Slide 15
OMI Results vs. Solar Zenith Angle
Measured – Model difference should be independent of SolZA
Plot suggests probable radiative transfer errors
  surface BRDF model
  treatment of atmosphere
Results obtained below SolZA = 70º fall within a 2.2% uncertainty estimate
OMI Level 1b (Coll. 2) 7 Dec – 4 Jan, 2004
Proposed use range (1330 orbit)

## Slide 16
62 < SolZA < 68
83 < SolZA < 86
Spectral dependence is consistent with BRDF that is too Lambertian
Apparent error increases at long  as predicted
OMI Results vs. Solar Zenith Angle
Non-Lambertian / Lambertian Reflectance Ratio (model)

## Slide 17
Based on one day of TropOMI data
TropOMI wavelength-dependent error
Wavelength dependence caused by pre-launch calibration errors
( Coll. 3 )

## Slide 18
OMPS / SNPP cross-track dependence
Binned Pixel Position
Fine structure is likely from entrance slit roughness
Comparison with other data (Rayleigh scatter method) confirms dependence
Change in swath dependence consistent with known BRDF error

## Slide 19: Summary
Permanent ice (Antarctica & Greenland) ideal for long-term monitoring (but not short-term)
Model calculations of TOA radiances over Antarctica are good to approximately 2% at solar zenith angles < 70º (best near Dec. 21)
Provides validation of radiometric characteristics of nadir-viewing sensors up to ~750 nm
Wavelength-to-wavelength radiometry is better than 2%, but not useful for absorption spectroscopy
Future Work :
Refine BRDF for improved performance at high SolZA and SatZA
  extends useful period away from solstice
  needed for sensor channels that saturate at low SolZA
  needed for comparisons with east side of swath - afternoon orbits (west side for morning orbits)

## Slide 20
Spares

## Slide 21
Modified BRDF model
Warren et al. parameterization
Modified “forward” parameterization
MISR / Terra comparison to Warren model
Lambertian
Warren
Strong
Forward
TOMS / Meteor3 comparison to three models (𝜙 = 0º)

## Slide 22
Model TOA Reflectance Error Budget
Surface BRDF model represents single largest error source

## Slide 23
Developed a 2 steradian BRDF model
Existing parameterization from
Warren et al.
J. Geophys. Res., 103, 1998
s  50 o  67 all 
Extrapolate function for use at s > 50
Invoke reciprocity ( s > 67 o< 67 )
Fill remaining “hole” ( s < 67 o< 67 )
  assume  s2 dependence for all o < 67
  derive  (s=0) at each o < 67 from a quadratic parameterization of observed scattering phase fn. (Warren, et al., ibid)
s
- 67
+ 67

 (s= 0)
o

## Slide 24
BRDF is most important at longer wavelengths
Simulated Nadir-scene albedos
Solar Zenith Angle = 75
Column Ozone = 325 DU
BRDF plays bigger role as
diffuse / direct ratio decreases
Lambertian
Non-Lambertian
Non-Lambertian / Lambertian Radiance Ratio

## Slide 25
X-track dependence is mostly Lambertian near SolZA = 50
Results near 50 are least affected by BRDF errors
BRDF surface slices at   67

## Slide 26
Same time and geographic location
OMI radiances compared directly to MODIS / Aqua band 3
MODIS has broad bandwidth
(459 <  < 479 nm) which includes O2-O2 absorption
OMI
MODIS

## Slide 27
Preliminary SCIAMACHY Results
SCIAMACHY Level 1b ( v5.04 )
18 – 24 Dec., 2004
Provided by R. van Hees, SRON
}
Ozone Absorption ignored
Comparison with RTM over Sahara (from G. Tilstra, KNMI)