## Slide 1: Evaluating NOAA-20 and S-NPP VIIRS Radiometric Consistency
Sirish Uprety and Changyong Cao
With contributions from
Wenhui Wang, Slawomir Blonski and Xi Shao
GSICS Annual Meeting
March 06, 2019
Frascati, Italy

## Slide 2: Background
After successful launch of NOAA-20 in Nov. 18, 2017, VIIRS has gone through extensive calibration and validation.
To ensure the calibration quality is well within specification, VIIRS radiometric performance needs to be continuously monitored and independently validated.
This study evaluates the radiometric consistency of operational NOAA-20 and S-NPP VIIRS by comparing nadir reflectance using:
  SNO over polar region
    SNPP bias relative to MODIS
    N20 bias relative to MODIS
    Bias between SNPP and N20: Double differencing
  Extended SNO (SNOx) over desert and ocean
    SNOx extended over African desert and tropical ocean
    Bias between SNPP and N20: Double differencing (similar to SNO)
  PICS (such as Libya 4)
    NOAA-20 and SNPP VIIRS are compared with Landsat OLI
  Deep Convective Cloud (DCC)

## Slide 3: VIIRS Spectral Bands (RSB)
11 moderate bands (0.412-2.25 m), 3 imagery bands, 1 Day/Night band (DNB)
VIIRS |  | MODIS | 
Band | Wavelength (µm) | Band | Wavelength (µm)
M1 | 0.402 - 0.422 | 8 | 0.405 - 0.420
M2 | 0.436 - 0.454 | 9 | 0.438 - 0.448
M3 | 0.478 - 0.498 | 10 | 0.483 - 0.493
M4 | 0.545 - 0.565 | 4 | 0.545 - 0.565
M5 I1 | 0.662 - 0.682 0.600 - 0.680 | 1 | 0.620 - 0.670
M7 I2 | 0.846 - 0.885 0.850 – 0.880 | 2 | 0.841 - 0.876
M8 | 1.230 - 1.250 | 5 | 1.230 - 1.250
M10 | 1.580 - 1.640 | 6 | 1.628 - 1.652
M11 | 2.225 - 2.275 | 7 | 2.105 - 2.155

## Slide 4: Radiance and Reflectance Comparison
NOAA-20 and S-NPP VIIRS uses different solar models
  S-NPP uses Kurucz spectrum (MODTRAN 4.0)
  NOAA-20 uses Thuillier solar model.
Comparing radiance can result in bias due to differences in solar irradiance model.
  Figure indicates bias for most of the bands; M2 suggests large bias of more than 3%.
This study compares VIIIRS reflectance products which is independent of solar model.

## Slide 5: NOAA-20 Spectral Bias Relative to S-NPP
SNPP and N20 RSRs are not identical and can have minor differences.
  Results in spectral bias
  Spectral Band Adjustment factors (SBAF) used based on Sciamachy
    Ref: NASA Langley tool (https://www-pm.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SBAF)
  Spectral bias for all bands are on the order of 1% or less except M4 (desert: ~3.2%).
  Spectral Bias= (N20 - SNPP)×100%/SNPP
Target | M1 | M2 | M3 | M4 | M5 | M7 | M8 | M10 | I1 | I2
South Pole | 0.3% | 0.1% | 0.1% | -0.8% | 0.2% | -0.4% | 0.0% | 0.5% | 0.3% | -0.4%
DCC | 0.0% | 0.7% | 0.2% | -0.4% | 0.0% | -0.4% | -0.1% | 0.7% | 0.2% | -0.4%
Libyan Desert | -1.1% | 0.0% | 0.1% | 3.2% | 0.3% | 1.0% | 0.1% | 0.2% | 1.5% | 0.8%

## Slide 6: Evaluating NOAA-20 and S-NPP Consistency using Polar SNOs
Both NOAA-20 and SNPP have SNOs with AQUA.
Study uses SNOs from both SH and NH.
Near identical solar and sensor geometry for both sensors.
Double differencing shows the radiometric consistency between SNPP and NOAA-20 VIIRS.
VIIRS operational data and AQUA MODIS C6 is used in comparison.
SNO

## Slide 7: NOAA-20 VIIRS M1 Bias (Polar SNO)
Bias trends changing over time.
After H-factor update (March 23, 2018), NOAA-20 is lower than S-NPP by ~-2.7%
Red: N20 Bias relative to MODIS
Bias= (V-M)*100%/M
Blue: SNPP Bias relative to MODIS
Radiometric consistency between N20 and SNPP
M1
N20 Bias: ~-3%
NOAA-20 Drop: H-factor update

## Slide 8: NOAA-20 VIIRS M4 Bias (Polar SNO)
NOAA-20 reflectance lower than S-NPP by ~3%
M4
N20 Bias: ~-3%

## Slide 9: NOAA-20 VIIRS M5 and M7 Bias (Polar SNO)
9
Large bias exists for M5 (-5.5%) and M7 (-3.5%) because S-NPP VIIRS M5 and M7 calibration are biased high by ~2%.
N20 Bias: -5%
M5
M7
N20 Bias: -3.5%

## Slide 10: NOAA-20 VIIRS I1 and I2 Bias (Polar SNO)
I1 bias is low (-2.5%) compared to I2 (-3.7%)
I2 and M7 have similar RSRs and their bias agree very well.
N20 Bias: ~-2.5%
N20 Bias: ~-3.7%
I1
I2

## Slide 11: Evaluating NOAA-20 and S-NPP Consistency using Extended SNO (SNOx) over Saharan Desert
SNOs extended to low latitude Saharan desert and tropical ocean.
Allows instrument comparison over desert sites within few minutes of time difference.
Technique is regularly used to monitor S-NPP Bias relative to MODIS
  https://ncc.nesdis.noaa.gov/VIIRS/VIIRS_MODIS_Intercomparison.php
NOAA-20 VIIRS and AQUA MODIS can be compared using SNO-x.
Double differencing needed to evaluate NOAA-20 and S-NPP consistency.
SNO-x Ref: Uprety et al. 2013, Jtech
SNO
STK Image

## Slide 12: M1-4 Bias Trends (Desert SNOx)
M1-4 bias for NOAA-20 ranges from -1.5% to -3%.
SNOx bias over Saharan desert consistent with SNO bias over polar region.
N20 Bias: ~-2.5%
N20 Bias: ~-2.5%
Large SBAF (~-3.2%) increases uncertainty in bias.
N20 Bias: ~-1.5%
N20 Bias: ~-1.5%

## Slide 13: M5 and M7 Bias Trends (Desert SNOx)
Both M5 and M7 NOAA-20 VIIRS biases are lower than SNPP.
Bias agrees with polar SNO to within 0.5%
M5 and M7 suggest large bias because S-NPP VIIRS M5 and M7 are biased high by about 2%.
N20 Bias: ~-5%
N20 Bias: ~-4%

## Slide 14: M8 and M10 Bias Trends (Desert SNOx)
NOAA-20 VIIRS is lower than SNPP for both M8 (~-3%) and M10 (~-2%).
N20 Bias: ~-3%
N20 Bias: ~-2%

## Slide 15: Ocean SNOx (M1-3 Bias Trends )
Comparison performed over clear sky tropical ocean using SNOx.
Uses VIIRS high gain only
M1-3 suggest bias on the order of -2% more recently.
HG (over ocean) and LG (Polar SNO and Desert SNOx) Bias are consistent.
M1
M2
M3
N20 Bias: ~-1.5%
N20 Bias: ~-1.5%
N20 Bias: ~-2.5%
Ocean

## Slide 16: M6 Comparison over Ocean
NOAA-20 agrees with S-NPP to 6-7%
M6 has with larger uncertainty.
Uses VIIRS high gain only over clear sky using SNOx
M6

## Slide 17: M5, M7 Bias using Pseudo-invariant Calibration Sites (PICS) Libya 4 Desert Site

## Slide 18: Bias over Libya 4 Relative to OLI
Note: Both NOAA-20 and SNPP VIIRS are scaled using SBAF to account spectral difference relative to OLI.
NOAA-20 Bias:-4.0% at 25° solar zenith
NOAA-20 Bias:-4.5% at 25° solar zenith

## Slide 19: Bias over Libya 4 Relative to OLI
Note: Both NOAA-20 and SNPP VIIRS are scaled using SBAF to account spectral difference relative to OLI.
NOAA-20 Bias:~-4.0% at 25° solar zenith
NOAA-20 Bias:~-4.5% at 25° solar zenith
M5
M7

## Slide 20: NOAA-20 and S-NPP DCC Ratio (VNIR and SWIR Bands)
All NOAA-20 bands are biased low, consistent with previous results.
Courtesy from Wenhui Wang, GST@ NOAA/STAR

## Slide 21: Summary
Study suggests that NOAA-20 VIIRS observed reflectance is consistently lower than S-NPP for all RSB.
Larger bias exists for M5 (~-4.5%) and M7 (~-4%) because S-NPP VIIRS M5 and M7 calibration are biased high by ~2%.
Results from multiple independent validation methods agree to within 1% for most bands.
Root cause is most possibly attributed to prelaunch calibration and investigation ongoing.
VIIRS bias will be regularly monitored and reported to the users.

## Slide 22: Questions?