## Slide 1
Tim Hewison
Slides from Jörg Ackermann
Status for PVRB on 13. Feb. 2019
Metop-C AMSU & MHS Radiometric Quality Status Update

## Slide 2: Metop-C AMSU and MHS Status
Metop-C launched 7 Nov 2018
In 9:30 orbit (same as Metop-A & -B), but with different phasing:
SIOV & Commissioning in Tristar configuration
  During commissioning, based on early user feedback, decision made to remain in a Tristar phasing configuration or to shift Metop-C 180 degrees opposite Metop-B (original A/B configuration) with Metop-A in-between (“trident” configuration – see Figure 1, right).
Recommend to start Level 1 dissemination as ‘Pre-Operational’

## Slide 3: Results: AMSU/MHS Radiometric Performance (NeΔT BOL)
NE∆T < Red line = Requirement

## Slide 4
AMSU

## Slide 5: Results: AMSU channels 3, 7, 8, 9, 10 Radiometric Performance Evolution (NeΔT)
Variations related to both, gain changes and NE∆T instabilities.
Cause is still unknown.

## Slide 6: Result: AMSU channels 3, 7, 8, 9, 10 Gain Evolution (Counts/K)

## Slide 7: Results: AMSU Ch.7 Instability on 17. Nov. 2018
Higher Noise is visible in the L1B product:

## Slide 8: Results: AMSU Ch.7 Monitoring in ECMWF System
Courtesy: Niels Bormann

## Slide 9: Results: M03 AMSU Mean Bias (Obs-B)
Courtesy: Niels Bormann

## Slide 10: Results: M03 AMSU Stdev (Obs-FG)
Courtesy: Christina Koepken, DWD

## Slide 11: Results: M03 AMSU vs. N-19 AMSU
Results:
AMSU channel 1, 2, and 15 brightness temperatures are about 1 K warmer, when compared with NOAA-19 AMSU (this observation is very similar to an earlier M02 vs. N-19 comparison)
The cause for the channel 8 discrepancy (2 SNO’s over Antarctica) is not understood yet
The remaining channels fit very well within a corridor of 0.8 K

## Slide 12
MHS

## Slide 13: Results: MHS Geolocation Assessment
Ascending:
Descending:
right
mid
left
left
mid
right

## Slide 14: Results: MHS Channels 3 and 4 Striping
First Orbits (L1B):
Early Orbit (L0):
Striping Indices
for all MHS
instruments:
Notes: It’s always there and nearly independent of NeDT.
Root cause unknown

## Slide 15: Result: MHS Channels 3 and 4 Radiometric Performance Evolution (NeΔT)

## Slide 16: Results: M03 MHS Mean Bias and Stdev (Obs-B)
Courtesy: Niels Bormann
Notes: noise on MHS-C really higher than MHS-A & -B for channels 3 and 4, it is significantly higher

## Slide 17: Results: M03 MHS Stdev (Obs-FG)
Courtesy: Christina Koepken, DWD

## Slide 18: Results: M03 MHS vs. N-19 MHS
Results:
Large scatter of Ch.3 due to high noise (NeDT~ 2.5 K) of NOAA-19 MHS channel 3
Cause for the channel 2 scatter (SNO over Antarctica) is due to a large surface terrain inhomogeneity
Remaining channels fit very well within 1 K

## Slide 19: Result: AMSU and MHS Mean Bias (Obs-B)
Courtesy: Brett Candy and Nigel Atkinson

## Slide 20: Conclusions
The L0 and L1B products are complete and processed in NRT without gaps
The feedback from the user community (ECMWF, DWD, UKMO) is positive
AMSU channels 7 and 8 exhibit occasionally sudden noise increase that can last for more than one orbit
AMSU channel 3 radiometric instabilities are superimposed by a performance degradation
MHS channels 3 and 4 are unstable (NeΔT between 0.7 K and 1.2 K)
  and show a significant striping
Continuous monitoring of product quality is highly demanded
Trial dissemination for Metop-C AVHRR/AMSU, and MHS Level 1 data
  will start on 28 Feb via EUMETCast Europe with “pre-operational” status