## Slide 1: GPM X-Cal LUT’s as MW Deliverable
Rachel Kroodsma, Wes Berg and Manik Bali
MW Break Session (5n)/ 6th March 2019
2019 Annual Meeting
Frascati, Italy

## Slide 2: Disclaimer
"The contents of this presentation are those of the authors and do not necessarily reflect any position of the US Government or the National Oceanic and Atmospheric Administration."

## Slide 3: Outline
Introduction
GPM-X and SSMI LUT
Deliverable Acceptance Matrix
Summary

## Slide 4: Introduction
The GSICS Microwave Subgroup has made strong trust in creating a platform wherein inter-calibration knowledge can be shared between members.
In the light of this goal three initiatives were taken
Engage the Microwave Calibration community to publish calibration research in GSICS Newsletter
Share knowledge through GSICS deliverables and Products ( Inter-cal coefficients )
What is a GSICS Deliverable
GSICS Deliverables are entities that are useful in instrument monitoring and calibration
http://gsics.atmos.umd.edu/bin/view/Development/Microwave-Deliverable

## Slide 5: GSICS Deliverable
Objective of the LUT
All of the intercalibration offsets from the tables are applied to calibrated brightness temperatures from the operational Level 1B data. For many of the sounders the Level 1B is referred to as the Sensor Data Records, or SDR files. The exception to this is the DMSP sensors, which used as input 1Base files produced by the Precipitation Processing System (PPS) at the NASA Goddard Space flight center. The input 1Base files for the SSM/I and SSMIS instruments apply a number of calibration corrections described in Berg et al. (2018).
How it was created
Details can be found in the attached paper Berg et al 2016 and Berg et al 2018. In summarry
The calibration tables are based on tie points, for which the given intercalibration offset applies to a specified scene temperature. The first value in the table for each channel is the number of tie points. A value of zero indicates no intercalibration is applied. A value of 1 indicates a constant intercalibration offset is applied (this is the case for most of the water vapor sounding channels). If there are two or more tie points, the applied intercalibration offset is interpolated between the specified scene temperature of the tie points. The offset for the lowest tie point is used below the scene temperature of that tie point and the offset for the highest tie point is used above the scene temperature of that tie point as the intercalibration offsets are not extrapolated. Software is provided in both IDL and Fortran90 to read and apply the calibration tables.
How to use it
Fortran and IDL Codes that aid in using the tables are provided
References:
Berg, W.; Kroodsma, R.; Kummerow, C.D.; McKague, D.S. Fundamental Climate Data Records of Microwave Brightness Temperatures. Remote Sens. 2018, 10, 1306.
Berg, W., and Coauthors, 2016: Intercalibration of the GPM microwave radiometer constellation. J. Atmos. Oceanic Technol., 33, 2639–2654, doi:10.1175/JTECH -D-16-0100.1.

## Slide 6: Use of LUT in GSICS
Wes Berg has provided

## Slide 7: Summary

## Slide 8
Thank You