## Slide 1: GSICS: A WIGOS Component
Mitch Goldberg, GSICS EP Chair
Kenneth Holmlund (GSICS EP Vice-Chair)
Toshiyuki Kurino (GSICS Secretariat)
INTER-COMMISSION COORDINATION GROUP ON WIGOS
Task Team on WIGOS Data Quality Monitoring System (TT-WDQMS)
Third Session
GENEVA, 4-6 DECEMBER 2018

## Slide 2: WMO Integrated Global Observing System (IGOS)
Provides an over-arching framework for the coordination and optimized evolution of global space-and surface-based observing systems
WIGOS focuses on the interoperability and compatibility through the application of internationally accepted standards and best practices.
Data compatibility will also be supported by the use of standardized data representation and formats.
WIGOS aims to improve the quality and availability of data and metadata in order to develop capacity and to improve access to data.

## Slide 3: How is GSICS Integrated into WIGOS
GSICS is a pivotal element of the WMO Integrated Global Observing System (WIGOS), as it enables interoperability of different missions contributing to the space-based component of WIGOS.
GSICS 2020 Document: https://gsics.wmo.int/documents/GSICS_Vision-for-GSICS-in-2020s.pdf
GSICS included as a WIGOS component
Reference: http://www.wmo.int/pages/prog/sat/meetings/documents/GSICS-EP-16_Doc_06-01_reference-documents.pdf by Jérôme Lafeuille
V. INTER-CALIBRATION
Instruments should be inter-calibrated on a routine basis against reference instruments or calibration sites. The routine and operational inter-calibration and corrections shall be performed in accordance with standards as agreed by the Global Space-based Inter-calibration System (GSICS). ( Reference: WMO-No 1160 Manual on the WMO Integrated Global Observing System(WIGSO))

## Slide 4
Regulatory document

## Slide 6: GSICS and WDQMS Goals Overlap
The purpose of the WDQMS is to monitor, evaluate and trigger corrective actions relating to departures of actual WIGOS data quality from expected WIGOS data quality
GSICS goals overlaps with the WIGOS Data Quality Monitoring System (WDQMS). This has resulted in Actions and Counter Actions between GSICS and WIGOS that have expedited the integration of GSICS with WIGOS
GSICS Monitoring Strategy
Monitoring instrument performances,
Operational inter-calibration of satellite instruments,
Tying the measurements to absolute references and standards, and
Recalibration of archived data.
Reference: gsics.wmo.int
Reference: CGMS-46-WMO-WP-17
Reference: CGMS-46-WMO-WP-17

## Slide 10: Satisfying WDQMS requirements - link to each agency landing page – (but they are different)

## Slide 11
GSICS Collaboration Servers (THREDDS)
Servers provide a set of services for GSICS user community to support data exchange and access to relevant inter-calibration products (all in NetCDF)
GSICS inter-calibration products
Source (e.g. L1 subset for monitored/reference instruments) for inter-calibration
Intermediate dataset (e.g. GEO-LEO collocation) for inter-calibration
Mirroring products among the servers
Collaboration ongoing
ISRO’s new THREDDS server
Expected to be 4th GSICS Collaboration Server
Collaboration for update the server configuration ongoing
ISRO

## Slide 12: New Visualization Feature on GSICS Product Catalog - more than 50 products
https://www.star.nesdis.noaa.gov/smcd/GCC/ProductCatalogImages.php

## Slide 13
NOAA commented that GSICS already contains monitoring capabilities from which WDQMS could benefit. Further discussion revealed that incident management aspects should be included as well. An action on WMO was raised to address these (CGMS-46 Final Report).
WIGOS Action on GSICS
GSICS Action on WIGOS
GSICS and WDQMS -Moving ahead into the Future
A.WMO.20160602.4 | WMO Secretariat to invite comments on the GSICS Basic Documents from WIGOS community - GSICS FUNCTIONS AND ORGANIZATION - GSICS USER GUIDE Using GSICS Products and Services - GSICS USER REQUIREMENTS DOCUMENT | WMO Secretariat | EP-19 | In progress: WIGOS will refer the GSICS documents into WIGOS document
GSICS has prepared the following documents
GSICS FUNCTIONS AND ORGANIZATION
GSICS USER GUIDE Using GSICS Products and Services
GSICS USER REQUIREMENTS DOCUMENT
GSICS Vision 20/20 Document
Action CGMS-46 | (WMO) To liaise with GSICS on implementing GSICS monitoring capabilities in WDQMS, to include incident management capabilities, and report back to WG-IV, proposing a way forward CGMS-47 | WMO Secretariat | EP-19 | In progress: WIGOS will refer the GSICS documents into WIGOS document
Idea is to synergize GSICS monitoring capabilities, its processes ( documents above) and its plans with WIGOS. To do this we invite WIGOS to review our GSICS mission documents( see Action A.WMO.20160602.4)

## Slide 14: Need to map existing and future documents to these requirements
Regulatory document

## Slide 15: SUMMARY
Integration of GSICS with WIGOS is underway
Actions:
Demonstrate use of GEO-LEO shorter product catalog with monitoring tool for GSICS WDQMS (GCC, GDWG)
  Each agency needs to make sure the GEO-LEO collocated data are routinely delivered to GSICS Collaboration Servers
Map existing documents to WIGOS requirements (GCC, GRWG, GDWG)
Assess need to develop new documents (GCC, GRWG, GDWG).

## Slide 16: Backup

## Slide 17
GSICS Annual State of the Observing System
Annual assessment of observing system performance with respect to reference instruments using a common template

## Slide 18
 | Channel Name (Central Wavelength in m) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Radiance as Tb (K) | 286.0 | 234.6 | 243.9 | 254.6 | 283.8 | 259.5 | 286.2 | 286.1 | 283.8 | 269.7
Metop-A/ IASI | Mean Bias (K) | -0.11 | -0.173 | -0.212 | -0.129 | -0.05 | -0.216 | 0.036 | 0.045 | -0.04 | 0.078
 | Stdv. of Bias (K) | 0.008 | 0.012 | 0.009 | 0.014 | 0.012 | 0.017 | 0.018 | 0.019 | 0.017 | 0.015
S-NPP/ CrIS | Mean Bias (K) | -0.07 | -0.16 | -0.24 | -0.15 | N/A | -0.23 | -0.02 | -0.01 | -0.01 | 0.03
 | Stdv/ of Bias (K) | 0.039 | 0.011 | 0.012 | 0.026 | N/A | 0.013 | 0.013 | 0.012 | 0.010 | 0.005
Summary Statistics of Himawari-8/AHI IR Calibration Performance in 2017 (All uncertainties are k=1)
Calibration Performance: Himawari-8/AHI Infrared Bands
The statistics are derived from Himawari-8/AHI GSICS Re-Analysis Correction (ATBD)
Standard Radiance: typical scene defined by GSICS for easy inter-comparison of sensors’ inter-calibration biases

## Slide 19
 | Channel Name (Central Wavelength in m) | BAND07 (3.9) | BAND08 (6.2) | BAND09 (6.9) | BAND10 (7.3) | BAND11 (8.6) | BAND12 (9.6) | BAND13 (10.4) | BAND14 (11.2) | BAND15 (12.4) | BAND16 (13.3)
 | Std. Scene Tb (K) | 286.0 | 234.5 | 244.0 | 254.5 | 284.0 | 259.5 | 286.0 | 286.0 | 283.5 | 269.5
Metop-B/ IASI | Bias at Std. Scene(K) | -0.167 | -0.196 | -0.218 | -0.170 | -0.204 | -0.227 | -0.210 | -0.141 | -0.153 | -0.294
 | Stdv. of Bias (K) | 0.120 | 0.082 | 0.093 | 0.108 | 0.147 | 0.110 | 0.160 | 0.165 | 0.169 | 0.160
S-NPP/ CrIS | Bias at Std. Scene(K) | - | - | -0.259 | -0.202 | - | -0.160 | -0.227 | -0.167 | -0.176 | -0.282
 | Stdv of Bias (K) | - | - | 0.045 | 0.052 | - | 0.047 | 0.073 | 0.073 | 0.073 | 0.094
Summary Statistics of GOES-16/ABI IR Calibration Performance in December 2017 (All uncertainties are k=1)
Calibration Performance: GOES16/ABI Infrared Bands
Time series of GOES-16 ABI daily mean Tb bias to SNPP/CrIS and Metop-B/IASI for ABI B12
Scene dependent Tb bias to SNPP/CrIS for ABI B16
Scene dependent Tb bias to Metop-B/IASI for ABI B16
The uncertainty and statistics are calculated following the GSICS standard GEO-LEO IR inter-calibration algorithm
GOES-16 ABI IR calibration is very stable with mean Tb bias to CrIS/IASI less than 0.3K. No significant scene dependent Tb bias to the reference instruments for all the IR channels
GOES-16 ABI post-launch test started in Jan. 2017 and became operational on 18 December 2017. L1B data are available to the public since after the provisional maturity on 1 June 2017.
Stable reference and monitored instruments can quickly detect and identify calibration events (e.g. Metop-B/IASI and GOES-16 ABI Ground updates) and validate the algorithm (e.g. ABI cal. algorithm update in October 2017)
Metop-B/IASI cal. algorithm update
G16 ABI cal. algorithm update

## Slide 20
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.57 | -0.16 | +0.38 | +0.01 | -0.08 | +0.04 | +0.01 | +0.35
Standard Deviation of Bias (K) | 0.03 | 0.05 | 0.08 | 0.05 | 0.07 | 0.04 | 0.03 | 0.40
Mean Drift Rate of Bias (K/yr) | -0.07 | -0.10 | -0.22 | -0.04 | -0.14 | -0.05 | -0.05 | +0.35
Summary Statistics of Meteosat-8/SEVIRI IR Calibration Performance in 2017 (All uncertainties are k=1)
The statistics are derived from Meteosat-8/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-8/SEVIRI IR Bands
Time series of Meteosat-8/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 21
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.36 | -0.13 | +0.09 | +0.01 | -0.03 | +0.03 | -0.01 | -1.41
Standard Deviation of Bias (K) | 0.08 | 0.12 | 0.15 | 0.11 | 0.18 | 0.11 | 0.13 | 0.16
Mean Drift Rate of Bias (K/yr) | -0.23 | -0.34 | -0.39 | -0.08 | -0.44 | -0.13 | -0.21 | -0.46
Summary Statistics of Meteosat-9/SEVIRI IR Calibration Performance in 2017 (All uncertainties are k=1)
The statistics are derived from Meteosat-9/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Meteosat-9 operated in Rapid Scan Service during most of this period, which increases the bias uncertainties
Calibration Performance: Meteosat-9/SEVIRI IR Bands
Time series of Meteosat-9/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 22
Channel Name | IR3.9 | IR6.2 | IR7.3 | IR8.7 | IR9.7 | IR10.8 | IR12.0 | IR13.4
Standard Radiance as Tb (K) | 284 | 236 | 255 | 284 | 261 | 286 | 285 | 267
Mean Bias (K) | +0.36 | -0.17 | +0.07 | -0.04 | +0.07 | +0.03 | +0.04 | -1.40
Standard Deviation of Bias (K) | 0.08 | 0.03 | 0.03 | 0.03 | 0.02 | 0.02 | 0.02 | 0.11
Mean Drift Rate of Bias (K/yr) | -0.25 | -0.08 | +0.05 | +0.03 | -0.01 | -0.02 | -0.01 | -0.35
Summary Statistics of Meteosat-10/SEVIRI IR Calibration Performance in 2017 (All uncertainties are k=1)
The statistics are derived from Meteosat-10/SEVIRI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Decontaminations introduce calibration jumps – most obvious in the IR13.4 channel due to ice contamination
Calibration Performance: Meteosat-10/SEVIRI IR Bands
Time series of Meteosat-10/SEVIRI Tb biases w.r.t. Metop-A/IASI at standard radiance

## Slide 23
Calibration Performance: COMS/MI Infrared Bands
 | MetOp-A/IASI |  |  |  | MetOp-B/IASI |  |  | 
Channel Name | IR3.8 | IR6.8 | IR10.8 | IR12.0 | IR3.8 | IR6.8 | IR10.8 | IR12.0
Std Rad as Tb (K) | 286 | 238 | 286 | 285 | 286 | 238 | 286 | 285
Mean Bias (K) | 0.16 | -0.02 | 0.12 | 0.004 | 0.15 | -0.06 | 0.11 | 0.004
Stdv of Bias (K) | 0.03 | 0.01 | 0.05 | 0.02 | 0.02 | 0.01 | 0.04 | 0.03
Mean Drift Rate of Bias (K/yr) | -0.14 | - | -0.12 | -0.01 | -0.15 | - | -0.14 | -0.04
Summary Statistics of COMS/MI IR Calibration Performance in 2017 (All uncertainties are k=1)
The statistics are derived from COMS/MI Operational GSICS Re-Analysis Correction vs. Metop-A/IASI, Metop-B/IASI, Aqua/AIRS, Snpp/CrIS
Biases defined for Standard Radiance: typical scene for easy inter-comparison of sensors’ inter-calibration biases
Operation of MI with shifted WV SRF of 3.5cm-1 started in 5 December 2017.
 | Snpp/CrIS |  |  |  | Aqua/AIRS |  |  | 
Channel Name | IR3.8 | IR6.8 | IR10.8 | IR12.0 | IR3.8 | IR6.8 | IR10.8 | IR12.0
Std Rad as Tb (K) | 286 | 238 | 286 | 285 | 286 | 238 | 286 | 285
Mean Bias (K) | - | -0.23 | -0.03 | -0.02 | -0.19 | -0.30 | -0.02 | 0.02
Stdv of Bias (K) | - | 0.01 | 0.14 | 0.08 | 0.07 | 0.02 | 0.14 | 0.09
Mean Drift Rate of Bias (K/yr) | - | - | +0.03 | +0.03 | +0.19 | - | -0.005 | -0.007