## Slide 1: New Russian Cal/Val portal on meteorological satellite instruments and products State Research Center “PLANETA”, ROSHYDROMET, Russia
Presenter: Alexander Uspensky, Principal Scientist
2019 GSICS Data and Research Working Groups Annual Meeting
Frascati, Italy, 06 March 2019

## Slide 2
CAL/VAL System Performance for Satellite Data and Products
Russian meteorological satellites of ELECTRO-L and METEOR-M series data
Data calibration
Data inter-calibration
Thematic processing
Validation
Satellite products
Numerical weather prediction
Standard measurements
Cal/Val examples
Roshydromet’ observation sites
Test sites
1. Zotino
2. Peterhof
3. Valday
4. Gelendjik
5. Polyarny
Foreign satellite data
NOAA/AVHRR METEOSAT/SEVIRI TERRA/MODIS
Data inter-calibration for channel
10.2-11.2 m over sea surface
Sea surface temperature validation
vs ship measurements
Bias = -0,01° К
RMSE = 0,9° К
SST derived from
METEOR-M/MSU-MR
- METEOSAT-10/SEVIRI data
- ELECTRO-L/MSU-GS data
- ELECTRO-L/MSU-GS data
(after intercalibration)
1
3
2
5
4
dТ=ТПО-Тсуд
© SRC Planeta

## Slide 3
Calibration (Inter-calibration) | Validation | Archive
Cal/Val portal for SRC Planeta GSICS Processing
and Research Center (GPRC)
The portal is focused on the Cal/Val data for the Russian on meteorological satellite instruments and products (from polar-orbiting METEOR-M series and geostationary ELECTRO-L series). It is divided into three sections: Calibration, Validation, and Archive.
09/08/2018
Global IKFS-2 / METEOR-M N2 data coverage
Post-launch calibration (inter-calibration) products for basic instruments of METEOR-M and ELECTRO-L satellites.
LEO-GEO: MSU-MR vs SEVIRI
LEO-GEO: IKFS-2 vs SEVIRI
Validation results for the products derived from METEOR-M and ELECTRO-L data.
METEOR-M and ELECTRO-L basic instrument measurements data for pre-selected test sites.
HDF5 files of Level-1C IKFS-2. The data can be utilized for inter-calibration of IR-channels (imaging instruments).
5 July 2018, Bias = -0.5 K, RMSE = 0.9 K
SST Validation
  overlap area of SRC Planeta and NIC data
  area of NIC data over SRC Planeta data
  area of SRC Planeta over NIC data
10.8 mkm
12.0 mkm
LEO-LEO: IKFS-2 vs IASI
Bias Monitoring
LEO-LEO: MSU-MR vs AVHRR
GEO-LEO: MSU-GS vs IKFS-2
GEO-GEO: MSU-GS vs SEVIRI
Sea ice extent validation
Error statistics for temperature profile retrievals
Tzond – Tret, K
July 2018
RMSE
http://planet.rssi.ru/calval/
© SRC Planeta

## Slide 4
© SRC Planeta
Navigating through the website
Home | GSICS | Validation | Data | Info
 | Calibration |  | Archive | Satellites
 |  |  | IKFS-2 data | Calibration Landing Page
 |  |  |  | Data outages
 |  |  |  | Publications
 |  |  |  | Abbreviations
 |  |  |  | Contacts
 |  |  |  | Documents
http://planet.rssi.ru/calval/
For pages in red – only authorized access

## Slide 5
© SRC Planeta
Home page

## Slide 6
© SRC Planeta
GSICS page

## Slide 7
© SRC Planeta
GSICS/Calibration-inter-calibration
Post-launch calibration monitoring and correction (inter-calibration) |  | 
Baseline algorithms | Monitored instrument | Reference instrument
GEO-GEO | MSU-GS (IR)/Electro-L No.2 | SEVIRI/Meteosat-11
GEO-LEO | MSU-GS (VIS, NIR)/Electro-L No.2 | VIIRS/SNPP
GEO-LEO | MSU-GS (IR)/Electro-L No.2 | IKFS-2/Meteor-M No.2
LEO-LEO | MSU-MR (VIS)/Meteor-M No.2 | AVHRR/Metop, NOAA
LEO-GEO | MSU-MR (IR)/Meteor-M No.2 | SEVIRI/Meteosat-11
LEO-GEO | IKFS-2/Meteor-M No.2 | SEVIRI/Meteosat-11
LEO-simulator | MTVZA-GY/Meteor-M No.2 | Modeling (LBLRTM, FRTM-RTTOV,…)
GSICS Correction. Regression coefficients between reference and monitored observations enable to perform the GSICS Correction. Linear regression coefficients (C0 and C1) are estimated to derive relationship between radiances measured by monitored (Mon) and reference (Ref) instruments:
Radiance (Mon) = C0 + C1 × SBAF × Radiance (Ref), where SBAF - Spectral Band Adjustment Factor
Corrected satellite radiances are calculated using the relationship :
Corrected radiance (Mon) = {Radiance (Mon) − C0 }/ (C1 × SBAF )

## Slide 8
© SRC Planeta
GSICS/Calibration-inter-calibration page

## Slide 9
© SRC Planeta
GSICS/MSU-MR inter-calibration (VIS, NIR, IR)

## Slide 10
© SRC Planeta
Inter- calibration GEO-LEO
MSU-GS (Ch 1-3) vs VIIRS/Suomi NPP
Comparison above
deep convective clouds
over the Indian Ocean
± 20° North/South and East/West of Electro-L No. 2
sub-satellite point (76E)
Calculated SBAF between MSU-GS
and VIIRS ~1.0 for each pair of channels

## Slide 11
© SRC Planeta
Inter-Calibration GEO-GEO
MSU-GS (IR ch9- 10.7 µm) vs SEVIRI/Meteosat-11

## Slide 12
© SRC Planeta
Inter-calibration GEO-LEO
MSU-GS (ch6-8) vs IKFS-2/Meteor-M N2

## Slide 13
© SRC Planeta
GSICS Bias Monitoring and Correction
(Meteor-M №2/IKFS-2 vs Meteosat-10,-11/SEVIRI)

## Slide 14
© SRC Planeta
Validation page

## Slide 15
© SRC Planeta
SST Validation
SST (MSU-MR) vs ship’s measurements

## Slide 16
Temperature and Humidity profiles Validation
IKFS-2 based profiles vs radiosondes
Far-Eastern Region

## Slide 17
© SRC Planeta
Temperature profiles Validation
IKFS-2 based profiles vs radiosondes
Error statistics for 12.2018-02.2019. Sample size 255÷1353 for various levels
Global coverage
RMSE, N
BIAS

## Slide 18
© SRC Planeta
Wind vectors (Cloud motion winds)

## Slide 19
CO2 column amount validation
IKFS-2 vs CrIS, ZOTTO (OCO)
17.02.2019
July 2019

## Slide 20
© SRC Planeta
Data page
Archive
IKFS-2 data
Publicly available data
from March 2015 up to now (HDF-5 files)
Available Data MSU-MR, IKFS-2, MTVZA-GY
for 17 test sites from 2015 year (BIN files)

## Slide 21
© SRC Planeta
Info page/Satellites

## Slide 22
© SRC Planeta
Info page/Calibration Landing Page

## Slide 23
© SRC Planeta
Info page/Data outages

## Slide 24
© SRC Planeta
Info page/Publications

## Slide 25
© SRC Planeta
Info page/Documents
REST API functions:
Get list of test regions and their basic descriptive information;
Get list of remote sensing platforms. Remote sensing platform is a combination of satellite platform and sensing instrument on it;
Search instrument measurements archives by specified criteria;
Download files from instrument measurements archives.

## Slide 26
Frascati, Italy, 06 March 2019
2019 GSICS Data and Research Working Groups Annual Meeting
Thank you!