## Slide 1: GSICS Convention for Spectral Response Function files
Masaya Takahashi
Japan Meteorological Agency

## Slide 2: Spectral Response Function
    Information characterizing instrument from a radiometric viewpoint
Updating frequency
Once (derived at pre-launch ground test)
Periodic/aperiodic update to take into account instrument trending
In general, satellite operators provide their instruments’ SRFs online/offline
File format: depends on agency/mission
SRF
0.0 0.2 0.4 0.6 0.8 1.0
2400 2500 2600 2700 2800 2900
Wavenumber [cm-1]
SRFs for SWIR channel of
Himawari-8/AHI, GOES-16/ABI and Meteosat-10/SEVIRI
Purpose of this talk
  To introduce backgrounds on developing GSICS SRF Convention
  To show current status of GSICS SRF Convention and discuss future updates

## Slide 3
    SRF netCDFs for GSICS activities
    Python script to convert official SRFs to netCDFs: developed by GDWG in 2013
“This file was produced in support of GSICS activities and thus is not meant for public use although the data in the file is in the public domain.” (docs on NOAA GSICS Server)
The conversions have been manually done by GDWG chair
    Contents
    Metadata on satellite/instrument name, license, publisher info, and so on.
    Wavelength/wavenumber/SRF (normalized to max=1) + several ancillary info
Several files are available on GSICS Wiki
Background

## Slide 4: Use of netCDF SRF
    GIRO (GSICS Implementation of the ROLO model)
Reference model for lunar calibration, implemented in 2014
SRF data: one of inputs
NetCDF SRF Convention was adopted to support a variety of instruments in GIRO
    Users’ interests on the standardisation
    Good from the viewpoint of GSICS deliverables because GSICS Software/Tool like GIRO use the file
    GSCIS member agencies may refer the Convention for their official SRFs.
GIRO users (LCWS in Dec. 2014)

## Slide 5
GSICS SRF Convention
    Known issues in the SRF netCDF (as of Jul 2018)
File naming
NetCDF Convention

## Slide 6
    DataDesinator should be like SATCAL+SRF+VISIR
    Need interactions with WMO to add SRF in Data Category: SATCAL of Common Table C-13 of the W.M.O. Manual on Codes. (next slide)
    yyyyMMddhhmmss and versioning would be needed
SRF could be updated during the instrument lifetime (default: delivery date to customers)
Field demo/preop/op: not used because this is not a GSICS product
Updates of Filenaming Convention
Current Convention:
  W_XX-EUMETSAT-Darmstadt,VIS+IR+SRF,MSG1+SEVIRI_C_EUMG.nc
  Proposal for GSICS Standard SRF:
W_XX-EUMETSAT-Darmstadt,SATCAL+SRF+VISIR,MSG1+SEVIRI_C_EUMG_20060119------_01.nc
DataDesinator
yyyyMMddhhmmss
versioning

## Slide 7
Common Table C-13 Data Category |  |  | Common Table C-13 International Data Subcategory |  | 
Alphanum. Code | Name | Code Figure | Alphanum. Code | Name | Code Figure
SATCAL | Calibration dataset (satellite) | 30 | SUBSET | Subsetted data | 0
 |  |  | COLLOC | Collocated data | 1
 |  |  | OBC | On-board calibration data | 2
 |  |  | BIASM | Bias Monitoring | 3
 |  |  | NRTC | Near Real-Time Correction | 4
 |  |  | RAC | Re-analysis Correction | 5
Available DataCategory and InternationalDataSubcategory for GSICS (as of Mar 2019)
Common Table C-13 of the W.M.O. Manual on Codes
Adding SRF to InternationalDataSubcategory will be considered by interacting with WMO

## Slide 8
Proposal for Global Attributes / Dimensions / Variables
Updates of GSICS SRF netCDF Convention

## Slide 9
Option#1: keeping the current convention until we have real requirements to change
  Reasonable if there are no urgent or real requirements
Option#2: adopting the proposal which follows WMO GTS File Naming Convention and CF Convention
  No impacts on the current applications, but further discussions are needed to choose this option because quite a lot of parts would be changed
Option#3: defining a new convention which is not relevant to WMO Convention
  Option#3 (e.g. himawari8_ahi_srf_v01.nc): SRF file naming does not follow the WMO Convention any more
3 options for decision making

## Slide 10
Global Attribute Conventions=”CF-1.6” in the current netCDF SRF
  means the file follows CF-1.6, but
  the file is not CF-compliant because string and unsigned-byte data types are not supported in the past/latest CF-Conventions
Adding these data types is now discussed in the CF community
=> fully CF-compliant in future by updating Conventions attribute from CF-1.6 to 1.8.
The CF-compliant file by changing data types (i.e. string to char, unsigned byte to byte)
some existing applications (e.g. GIRO) may be affected by such a change
Discussion on gsics-dev
Option#1: keeping the current convention until we have real requirements to change
Option#2: adopting the proposal following CF and WMO GTS File Naming Convention
Option#3: SRF file naming does not follow the WMO Convention any more
Option#1 was chosen and option#2 could be considered in future

## Slide 11
Proposed recommendation in Plenary (3h):
  All agencies to provide SRF in NetCDF for link to GSICS and WMO OSCAR/Space – any thoughts?
Sharing the format conversion script (python)
  Original code was developed at NOAA in 2013
  Any license issue at NOAA for sharing the script on GitHub?
    JMA action: A.GDWG.2018.5a.2
Reminders:
Consideration of option#2
Updating the Convention to support MW instruments
  To be discussed in future
Discussions today

## Slide 13
Issues in the current netCDF SRF / proposal for GSICS Standard SRF – Global Attributes
NAME | CONTENT
Conventions | CF-1.6
Metadata_Conventions | Unidata Dataset Discovery v1.0
standard_name_vocabulary | CF Standard Name Table (Version 19, 22 March 2012)
project | Global Space-based Inter-Calibration System http://gsics.wmo.int
title | e.g. Meteosat-9 SEVIRI Normalized Spectral Response Data
summary | e.g. Normalized spectral response functions (SRF) for all channels of the Meteosat-9 SEVIRI instrument are stored in this file. The data came from the official files (see the source global attribute).
institution | e.g. EUMETSAT
licence | This file was produced in support of GSICS activities and thus is not meant for public use although the data is in the public domain. Any publication using this file should acknowledge both GSICS and the data's relevant organization. Neither the data creator, nor the data publisher, nor any of their employees or contractors, makes any warranty, express…
creator_name | e.g., EUMETSAT
creator_email | e.g. ops@eumetsat.int
creator_url | e.g. http://www.eumetsat.int
NAME | CONTENT
platform | e.g. Meteosat-9
instrument | e.g. SEVIRI
wmo_satellite_code | e.g. 56
wmo_satellite_instrument_code | e.g. 207
source | MSG_SEVIRI_Spectral_Response_Characterisation.XLS (MD5:...)
date_modified | YYYY-MM-DDTHH:MM:SSZ
history | e.g. 2016-11-07T01:43:51Z srf2nc.py v3.0.13
id | W_XX-EUMETSAT-Darmstadt,VIS+IR+SRF,MSG2+SEVIRI_C_EUMG.nc
naming_authority | jp.go.jma.msc.gsics
publisher_name | System Engineering Division, Meteorological Satellite Center, Japan Meteorological Agency
publisher_email | jma-msc-contact@ml.kishou.go.jp
publisher_url | http://www.data.jma.go.jp/mscweb/data/monitoring/calibration.html
    Several values of Global Attributes should be changed
    New Global Attributes may be added
Current Convention

## Slide 14
Issues in the current netCDF SRF / proposal for GSICS Standard SRF – Global Attributes
NAME | CONTENT
Conventions | CF-1.6
Metadata_Conventions | Unidata Dataset Discovery v1.0
standard_name_vocabulary | CF Standard Name Table (Version 19, 22 March 2012)
project | Global Space-based Inter-Calibration System http://gsics.wmo.int
title | e.g. Meteosat-9 SEVIRI Normalized Spectral Response Data
summary | e.g. Normalized spectral response functions (SRF) for all channels of the Meteosat-9 SEVIRI instrument are stored in this file. The data came from the official files (see the source global attribute).
institution | e.g. EUMETSAT
licence | Normalized spectral response functions (SRF) delivered as a GSICS deliverable is generated in accordance with the GSICS principles and practices. Normalized SRF files are public and may be used and redistributed freely. … (data disclaimer)
creator_name | e.g., EUMETSAT
creator_email | e.g. ops@eumetsat.int
creator_url | e.g. http://www.eumetsat.int
time_coverage_start | YYYY-MM-DDTHH:MM:SSZ
time_coverage_end | YYYY-MM-DDTHH:MM:SSZ (e.g. estimated instrument’s end-of-life date)
NAME | CONTENT
platform | e.g. Meteosat-9
instrument | e.g. SEVIRI
wmo_satellite_code | e.g. 56
wmo_satellite_instrument_code | e.g. 207
source | MSG_SEVIRI_Spectral_Response_Characterisation.XLS (MD5:...)
date_modified | YYYY-MM-DDTHH:MM:SSZ
history | e.g. 2016-11-07T01:43:51Z srf2nc.py v3.0.13
id | W_XX-EUMETSAT-Darmstadt,VIS+IR+SRF,MSG2+SEVIRI_C_EUMG.nc
naming_authority | Int.eumetsat
publisher_name | EUMETSAT - European Organisation for the Exploitation of Meteorological Satellites
publisher_email | ops@eumetsat.int
publisher_url | http://www.eumetsat.int
processing_level | e.g. v1.0.0
Proposal

## Slide 15
Issues in the current netCDF SRF / proposal for GSICS Standard SRF – Dimensions/Variables
NAME (Dimension) | LONG_NAME | STANDARD_NAME | UNITS | TYPE
channel (channel) | nominal channel central wavelength | N/A | um | double
channel_id (channel) | channel identifier | sensor_band_identifier | N/A | string
origin (channel) | original sample domain | N/A | km | ubyte
wavelength (sample, channel) | wavelength | N/A | um | double
wavenumber (sample, channel) | wavenumber | N/A | cm-1 | double
srf (sample, channel) | normalized spectral response | N/A | 1 | double
Current Convention
Variables
NAME | VALUE | DESCRIPTION
channel | e.g. 12 for MSG2/SEVIRI | # of channels included in the netCDF file
sample | e.g. 168 for MSG2/SEVIRI | Max # of SRF samples among channels in the netCDF file
Dimensions

## Slide 16
Issues in the current netCDF SRF / proposal for GSICS Standard SRF – Dimensions/Variables
NAME | VALUE | DESCRIPTION
channel | e.g. 12 for MSG2/SEVIRI | # of channels included in the netCDF file
sample | e.g. 168 for MSG2/SEVIRI | Max # of SRF samples among channels in the netCDF file
NAME (Dimension) | LONG_NAME | STANDARD_NAME | UNITS | TYPE
channel (channel) | nominal channel central wavelength | sensor_band_central_radiation_wavelength | m | double
channel_id (channel) | channel identifier | sensor_band_identifier | N/A | string
origin (channel) | original sample domain | N/A | km | ubyte
wavelength (sample, channel) | wavelength | radiation_wavelength | m | double
wavenumber (sample, channel) | wavenumber | N/A | cm-1 | double
srf (sample, channel) | normalized spectral response | N/A | 1 | double
wavelength_unc (sample, channel) | uncertainty of wavelength | N/A | m | double
wavenumber_unc (sample, channel) | uncertainty of wavenumber | N/A | cm-1 | double
srf_unc (sample, channel) | uncertainty of normalized spectral response | N/A | 1 | double
Variables
Dimensions
Proposal
    Any requirements for MW instruments?
    Variables on frequency may be needed
    If we use CF standard name, units must be changed
    Variables on SRF uncertainty are requested by S. Wagner