## Slide 1: The First Geostationary Infrared Hyper-spectral Measurements: In-orbit Validation Method for Radiometric Accuracy and its Preliminary Results
Qiang Guo, Xin Wang, and Rui Wen
guoqiang@cma.gov.cn
National Satellite Meteorological Center, CMA
2019 GSICS Data & Research Working Groups Annual Meeting
7 March 2019, Frascati, Italy

## Slide 2: Outline
Background
GEO-LEO/Sounder Intercalibration
In-orbit Radiometric Accuracy of GIIRS
Conclusion

## Slide 3
Spectral Parameters (Normal mode) | Range Resolution Channels LWIR: 700-1130 cm-1 0.625-1 689 S/MIR:1650-2250 cm-1 0.625-1 961 VIS : 0.55- 0.75 μm
Spatial Resolution | LWIR/MWIR : 16 Km SSP VIS : 2 Km SSP
Operational Mode | China area 5000  5000 Km2 Mesoscale area 1000  1000 Km2
Temporal Resolution | China area <1 hr Mesoscale area <½ hr
Sensitivity (mW/m2srcm2) | LWIR: 0.5-1.1 S/MIR: 0.1-0.14 VIS: S/N>200(ρ=100% )
Calibration accuracy | 1.5 K (3σ) radiation
Calibration accuracy | 10 ppm (3σ) spectrum
Quantization Bits | 13 bits
Main Specifications of GIIRS

## Slide 4
FY-4A: 32×4@16km
FY-4B: 16×8@12km

## Slide 5
Brightness Temperature Animation of FY-4A/GIIRS within MW Spectral Region

## Slide 6
GIIRS NWP Application in GRAPES

## Slide 7: Outline
Background
GEO-LEO/Sounder Intercalibration
In-orbit Radiometric Accuracy of GIIRS
Conclusion

## Slide 8
Spatial Collocation: quasi-full-overlap (QFO) criterion
GSICS: recommended overlap pattern (UW)
GeoCAVS: Overlap pattern far away from nadir (VW)
GEO-LEO/imager
GEO-LEO/sounder
Different overlap relationships of footprints between GEO and LEO sounders

## Slide 9
Clear Sky Detection: quasi-full-overlap (QFO) criterion
Atmospheric radiation characteristic of the stable weak ozone absorption peak (around 1043 cm-1) for the U.S. Standard Atmosphere profile. (a) Clear-sky spectral radiance (presented as BT); (b) weight function of channel 550 of GIIRS (its central wavelength: 1043.125 cm-1).
(a)
(b)
,

## Slide 10
Spectrum Transformation: between two Fourier Transform Spectrometers
IASI
GIIRS
Flowchart of spectra transformation between two FTSs

## Slide 11: Outline
Background
GEO-LEO/Sounder Intercalibration
In-orbit Radiometric Accuracy of GIIRS
Conclusion

## Slide 12
Examples of paired spectra between GIIRS and IASI at UTC 0230, 30 January, 2018
(Notes: red line for IASI, blue line for GIIRS)

## Slide 13
For a period between August 2017 and March 2018, the averaged absolute monthly biases of GIIRS are assessed to be 0.25K and 0.42K for the two uncontaminated spectral coverages (i.e. 760-1050 cm-1 and 1800-2188 cm-1) respectively
LW
MW

## Slide 14
Long-term RA results of all the uncontaminated channels for GIIRS against IASI from August 2017 to March 2018

## Slide 15: Outline
Background
GEO-LEO/Sounder Intercalibration
In-orbit Radiometric Accuracy of GIIRS
Conclusion

## Slide 16
For a period between August 2017 and March 2018, the averaged absolute monthly biases of GIIRS are assessed to be 0.25K and 0.42K for the two uncontaminated spectral coverages (i.e. 760-1050 cm-1 and 1800-2188 cm-1) respectively, while the annual variation feature of monthly biases appears clearly.
RA results for individual detectors of GIIRS indicate that the mean biases of column 3 is the best, columns 4 and 2 take the second place, and column 1 is the worst.
The preliminary RA outcomes also validate that the spectral calibration as well as the harmonization among different detectors of GIIRS still have more space for enhancement.
The proposed method is widely suitable for two FTSs intercalibration with not only GEO-LEO but also LEO-LEO modes, and is believed to be benefit to GSICS community for the future applications.
It has been submitted to TGRS (TGRS-2018-01812) and is undergoing review

## Slide 17
Thanks for your attention
Question?