## Slide 1: Multispectral IR inter-calibration update in CMA including GEO-LEO and LEO-LEO
Na XU, Hanlie XU, Xiuqing HU
National Satellite Meteorological Center(NSMC), CMA
2019 GSICS Annual Meeting, Frascati, Italy,
04-08, March, 2019

## Slide 2: OUTLINE
Overview of CMA IR products status
Baseline GSICS IR methodology update
Progresses on CMA GEO-LEO inter-calibration
Progresses on CMA LEO-LEO inter-calibration
Summary

## Slide 3: Overview of CMA IR products status
Type | Monitored Instrument | Reference Instrument | GSICS NRT/RAC Correction Products | GSICS Bias Monitoring
Operational Products for GEO Multispectral instruments | FY2C~G/VISSR | IASI-A+B(+ AIRS+CrIS) | Pre-Demo (planning to submit the GSICS Product Acceptance Form for official approvement) | CMA Web
 | FY2G/VISSR | HIRAS | Pre-Demo | Not released
 | FY2H/VISSR | IASI-A+B(+CrIS+HIRAS) | Developing | Developing
 | FY4A/AGRI | IASI-A+B(+CrIS+HIRAS) | Pre-Demo (planning to submit the GSICS Product Acceptance Form for official approvement) | Not released
Scientific Products (for LEO Multispectral instruments and LEO/GEO sounders) | FY3A~C VIRR/MERSI/IRAS | IASI-A+B(+CrIS) |  | CMA Web(only FY3C)
 | FY3D MERSI | IASI-A+B(+CrIS+HIRAS) |  | Not released
 | FY3D/HIRAS | IASI-A+B(+CrIS) |  | Developing
 | FY4A/GIIRS | IASI-A+B(+CrIS+HIRAS) |  | Developing
Achievements after 2018 Annual Meeting:
Developed new GSICS products for new multispectral instruments: FY-3D/MERSI, FY-4/AGRI
Supplemented HIRAS as reference for CMA scientific researches.
Notes: standard specification previous

## Slide 4: Baseline methodology update
Figure 1: Diagram of generic data flow for inter-calibration of monitored (MON) instrument with respect to reference (REF) instrument
Wang L K, et al., 2016
Xu H, et al., 2018
Accurate collocation(Wang L et al., 2013,2016) and spectral gap filling(Xu H, 2018) are applied in CMA IR inter-calibration.

## Slide 5
Spatial
Spectral
Point1：space deformation, different IFOV
Point2：Spatial Non-uniformity
Accurate collocation
(Wang L K, 2016)
Point1：Resolution and coverage mismatch
Point2：Low spectral resolution
Gapfilling(Xu H,2018)
Spatial Point Spread Functions
+
Spatial Accurate Collocation and Matching
Solution
Method and Consideration
Solution
16km
55km
29 km
16 km
Requirements:wide angle and spatial intercalibration (polarization,contamination,navigation...
Requirements:large spectral gap channels intercalibration
Notes: technique applicative

## Slide 6
Stripe Bias
(HIRAS)
Angle dependence Cloud Margin Bias
(MERSI?HIRAS?) (Geolocation&PSF)
A pretty good tool to reveal veiled biases due to unexpected instrument anomaly observation.
Application and assessment: Accurate collocation
NPP VIIRS&CrIS using CMA code
Satellite
P
wang et al.,2016
Notes: margin s

## Slide 7
Std/ave<0.005
Accurate
Traditional
Bias=0.2904K@287K
 |  | Std/ava<0.1 | Std/ava<0.05 | Std/ava<0.01 | Std/ava<0.005
bias | Accu. | 0.3998 | 0.4160 | 0.2995 | 0.2874
 | Trad. | 0.4417 | 0.4547 | 0.3258 | 0.2904
std | Accu. | 0.9960 | 0.7308 | 0.2168 | 0.1922
 | Trad. | 1.4860 | 0.7548 | 0.3267 | 0.1924
Sample number | Accu. | 22675 | 18372 | 5052 | 1631
 | Trad. | 23864 | 19039 | 3064 | 1370
Bias=0.2874K@287K
Application and assessment: Accurate collocation vs General option
Comparison of FY-3 MERSI&HIRAS intercalibration results based on accurate collocation and General option under the same filtering criteria.
Inter-calibration results based on different collocation methods are almost indentical using strict uniform filter.
Same Platform intercalibration
FY-3D MERSI&HIRAS
Notes: strict

## Slide 8
Different Platform intercalibration
FY-3 VIRR&S-NPP CrIS
Inter-calibration results among different platform based on different collocation methods almost the identical using quite uniform scene samples.
If the uniform scene filter is not considered, even under accurate collocation, the intercalibration results show great uncertainty.
0.2829K@250K
0.2867K@250K
0.1145K@250K
wang et al.,2016
Application and assessment: Accurate collocation vs General option
Comparison of FY-3 VIRR&S-NPP CrIS intercalibration results based on accurate collocation and General collocation
under the same filtering criteria.
Accurate
Traditional
under the same filtering criteria
Accurate results
without uniform filter

## Slide 9: Instruments Spectral Coverage
CH25
CH24
CH23
CH22
CH21
CH20
FY-3D/MERSI |  | FY-3D/HIRAS | NPP/CrIS | METOP/IASI
Band number | Wavelength Center | Spectral channel coverage (cm-1) |  | 
CH25 | 12μm (833cm-1) | 650-1135 | 650-1095 | 645-1210
CH24 | 10.8μm (926cm-1) |  |  | 
CH23 | 8.55μm (1169cm-1) | Gap | Gap | 
CH22 | 7.2μm (1389cm-1) | 1210-1750 | 1210-1750 | 1210-2000
CH21 | 4.05μm (2469cm-1) | 2155-2550 (A little bit gap) | 2155-2550 (A little bit gap) | 2000-2760 (A little bit gap)
CH20 | 3.8μm (2631cm-1) | Gap | Gap | 
MERSI SRF & IASI、HIRAS(CrIS) spectral coverage
Spectral Gap of HIRAS
Application and assessment: Spectral gapfilling

## Slide 10: CrIS and HIRAS Gap filling coefficients are applied in CMA multispectral instrument inter-calibration
Cold Scene
20180601-0820
Warm Scene
Blue：Original Spectra
Red ：Gapfilling Spectra
HIRAS BT Spectra after gapfilling
Application and assessment: Spectral gap filling

## Slide 11: SNO Intercalibration Regression based on IASI and CRIS for MERSI Band 8.55μm
Before filling
After filling
Bias@250K=-0.39K
Bias@250K=-0.54K
Spectral Gap
MERSI SRF
SNO track selection
60°N~80°N
Radiance Bias
TBB Bias
Time series of TB bias after gapfilling
MERSI-CrIS
Hanlie Xu, [7t]

## Slide 12: Progresses on GEO-LEO inter-calibration
New Activities
Implementation of GSICS inter-calibration methods to FY-2H VISSR and FY-4 AGRI;
Diurnal investigation using IASI and CrIS SNO samples
hyperspectral inter-calibration of FY-4 GIIRS w.r.t IASI ,CrIS and HIRAS;
New achievements
New IR GSICS Correction products are developed, i.e. FY4 AGRI w.r.t. IASI/CrIS/HIRAS, FY-2 w.r.t. HIRAS ;
FY-2H NRTC/RAC products are on-going;

## Slide 13
Updates of GEO-LEO intercalibration to multispectral instrument
Time sequence of FY-4 AGRI TB Biases at standard BT
B9(6.3μm)：~-0.3K
B10(7.1μm)：~0.8K
B11(8.5μm)：0.2K~0.5K
B12(10.8μm)：~-0.2K
B13(12μm)：~-0.2K
B14(13μm)：-0.2~-0.4K
FY4/AGRI VS METOP-B/IASI
AGRI IR Biases are less than 0.5K for B9/11~14, and about 0.8K for B10；
Bias time sequence of B11 and B14 are less stable than others.
SRF Update
SRF Update
Notes: 结果已经业务运行，结果可以共享

## Slide 14: Reference sounders comparison: double difference
METOP-B/IASI VS METOP-A/IASI
<<0.1K
S-NPP/CrIS VS METOP-A/IASI
<<0.1K(B9/10)
<0.1K(B12/13)
S-NPP/CrIS VS FY3D/HIRAS
<0.25K(after Decontamination )
Decontamination
Decontamination
6.3μm
7.1μm
10.8μm
12μm

## Slide 15: Diurnal Variation
6.3μm
7.1μm
10.8μm
12μm
There is no significant diurnal variation seen in FY-4A AGRI
  The biases of clear sky radiance (TB10.8>270k) are shown.
  Data period is July 2018.
  Reference sensors are:
Metop-A/IASI
Metop-B/IASI
S-NPP/CrIS
Midnight
Ref transfer
Notes: 如果是CRis与IASI间差异导致，IASI应该比Cris小， 实际两者的交叉比对结果也显示相同趋势

## Slide 16: Progresses on LEO-LEO inter-calibration
New Activities & Achievements
Implementation of GSICS inter-calibration methods to FY-3D MERSI II w.r.t. IASI/CrIS/HIRAS ;
Inter-platform and Intra-platform comparison between FY-3D MERSI II and CrIS, FY-3D MERSI II and HIRAS;
Hyperspectral inter-calibration of FY-3D HIRAS w.r.t IASI and CrIS;

## Slide 17
B25(12μm)
B22(7.2μm)
B23(8.5μm)
B24(10.8μm)
B20(3.8μm)
Updates of LEO-LEO intercalibration to multispectral instrument
FY3D/MERSI II VS METOP-B/IASI
MERSI II IR Biases are less than 0.5K for B20/22/23/25, and about 0.8K for B24；
The time sequence of TB biases is stable.
Time sequence of FY-3D MERSI II TB Biases at standard BT
Notes: focal plane

## Slide 18: FPA cooling down
FPA Temperature
3.8μm
4.05μm
7.2μm
8.55μm
10.8μm
12μm
The performances are improved especially for the photoconductive (PC) HgCdTe bands
Notes: reduced

## Slide 19
FY3D/MERSI II VS NPP/CrIS
Cross tracks are periodically occurring;
similar results with that of IASI
consecutive SNO tracks help to reveal the TB bias variation more timely
Valid Period Feb.2018 ~Aug.2018(within 15min)
BB WUCD
FPA cooling down (100K → 94K)
BB WUCD






Notes: Cross tracks sometimes appear continuously, sometimes not

## Slide 20: Coincident Orbit (SNOx) comparison with CrIS
Coincident observation orbit of FY-3D and S-NPP occurs periodically.

## Slide 21: global observation comparison beween MERSI II and CrIS on coincident orbit

## Slide 22: Summary
Under the GSICS framework, the baseline IR intercalibration methodology was updated by applying Likun Wang's accurate collocation and Hui Xu's spectral gapfilling methods .
GSICS IR inter-calibration method have been implemented to FENGYUN new multispectral instruments, e.g., MERSI II, FY-4, FY-2H(on-going), using IASI, CrIS, HIRAS as references.
Discussion:
The investigation results show that accurate collocation is a good tool for large spacial scale comparison, but not a necessary process for SNO inter-calibration focusing on uniform scenes.
Uniformity filter is the most important factor, helping us to reduce the uncertanty of navigation error, IFOV differences, geometric matching and other factors.
" With enough uniform scene samples, actually, even the collocation is not good enough, we still can achieve the similar accuracy and precision for radiometric assessment."
Notes: prettily

## Slide 23
Thank you for your attention!