## Slide 1
Polarisation – Specific Needs in Calibration & In-orbit Activities
Bertrand Fougnie, Margarita Vazquez-Navarro, Pepe Phillips,
Ali Mousivand, Bernd Husemann
for the Remote Sensing & Products division
11/03/2024

## Slide 2: Summary
Introduction
  Why polarisation ?
  Polarimeters
From radiometry to polarisation
Specific needs for the performance
Polarisation model
Measurement of the polarisation
In-flight calibration
  PICS, Rayleigh, Sunglint, Clouds, Moon, Statistics, Cross-comparison
Summary and Way forward

## Slide 3: Why instrument characterisation for polarisation?
Needed for:
Polarimeters: when the goal is to measure the polarisation from Earth-Atmosphere
  e.g. EPS-SG/3MI, CO2M/MAP, EPS/GOME-2
Many other instruments: to quantify and/or correct when it becomes a perturbing effect
  e.g. S3/SLSTR, MTG/FCI, EPS-SG/VII…
A proper on-ground characterisation remains critical
  Contribution and support industry for the definition and analysis of ground campaigns (e.g. 3MI)
  Derivation of a polarisation model for the instrument: support the understanding and monitoring
Implementation of in-flight methodology
  Need: In-orbit verification & assessment, and monitoring
  Implementation in operational systems: e.g. MICMICS (EUM), MUSCLE (CNES)…

## Slide 4: Polarisation – A different vision of the Earth-Atmosphere
Level 1 TOA reflectance (RGB)
3MI simulated observation
R=865nm
G=670nm
B=443nm
Polarized light
Natural light
Measure = Natural light + MM * Polarized Light
Qualitatively:
  where MM is the Mueller Matrix = the instrumental sensitivity to the polarisation
    MM to be maximised/optimised for a polarimeter
    MM to be minimised for a non-polarimeter instrument

## Slide 5: Polarimeters
Increasing suite of flying instruments
Long-term provision of polarimetric measurements coming
In this context, need for evaluation and monitoring of the performance
Maybe also harmonisation
Polarimetry = performance differs from more classical imagers
  Specific needs & methodologies
Non-exhaustive list (Dubovik et al, 2019; WMO-OSCAR database)

## Slide 6: From radiometry to polarisation…
General concept: from N measurements through polarisers  I/Q/U Stokes vector
From (Σ Xn) to I/Q/U: the Mueller matrix describes the instrumental response
Qualitatively (perfect system -60°/0°/60°):
  I = (X1 + X2 + X3)/3  average
  Ip ~ √( (X1-X2)² + (X1-X3)² + (X3-X2)² )  quadratic sum of differences
U
Q
I
X1
X2
X3
from [X1X2X3] to [IQU]
I
Ip =
√(Q²+U²)

## Slide 7: Performance – specific needs for polarisation
Qualitatively (perfect system -60°/0°/60°):
  I = (X1 + X2 + X3)/3  average
  Ip ~ √( (X1-X2)² + (X1-X3)² + (X3-X2)² )  quadratic sum of differences
The needs for polarisation are:
  1/ I requires the usual effort for characterisation, including absolute
  2/ Q, U, and Ip require additional efforts (but not that much absolute)  system performance
  Harmonisation of Xn components in term of radiometry:
    Impacted by the radiometric artefacts correction (Non-Linearity, Flat-Field, DarkCurrent, StrayLight…) +
    inter-calibration of Xn components + geometrical co-registration
    Note: when no incoming polarisation  no differences should be observed between Xn components
  Accurate knowledge of the polarimetric answer of the system
    = Mueller matrix or the components of the polarimetric model
    3/ Polarisation is useful when associated with multi-directionality
  High need of harmonisation of the “Views”
  Impacted by the radiometric artefacts correction (NL, FF, DC, SL…), inter-calibration of views + geometrical co-registration, LineOfSight (LoS)

## Slide 8: Polarisation Model
Example with 3MI – Why a model?
  Model based on the knowledge we have of the instrumental behaviour and its sub-systems
  Small deviation from the model MM and the measured MM
  Provide an understanding of the features observed in MM
4/ combination retardance, optics & polariser
3/ combination retardance
& polariser
1/ polariser
2/ optics
P1
P2
P3
P1
P2
P3

## Slide 9: Measure the polarisation sensitivity
On-ground or In-flight, the principle remains:
  Put a reference in front of instrument (pixel) – called “analyser”
  Analyse the behaviour of the signal
    Amplitude of polarisation sensitivity
    Angle of polarisation sensitivity
  On-ground: a polarised source serves as analyser
  In-flight: observed targets are polarised sources and can serve as analyser
1/ Amplitude of
polarisation
2/ Angle of
polarisation
2
1

## Slide 10: In-flight Calibration of Polarisation
A proper ground characterisation is always a pre-requisite
On-board (polarised) systems: useful when available
In-flight calibration based on natural targets
  Extension of the Vicarious Calibration methods which have already demonstrated their ability to provide a reliable performance, usually able to complement on-board systems (S3, MODIS…)
  The approach is statistical (minimum bias obtained only after collection of a large amount of data)
Useful Targets:
  Low polarisation (τ<5%): clouds/DCC + Neutral points (POLDER-2, PARASOL)
  Moderate polarisation (τ<15%): Moon
  Highly polarised (τ>60%): sunglint, Rayleigh (POLDER-1, MODIS)
  PICS (desert) in general, as long as there are characterised in polarisation
   Combination of methods provides a higher performance and confidence (+ assessment of the accuracy)
Strong heritage from POLDERs/PARASOL, GOME-2, SCIAMACHY, MODIS, VIIRS, S-GLI…
  Non-exhaustive list of methodologies and examples in the next slides

## Slide 11: Vicarious Technics - PICS
PICS-Desert: well known but PICS have their own polarisation properties
  Type: moderated (depending on bands)
  A TOA-BPDF model or reference is needed
    Mostly coming from atmosphere
  Don’t need a high spatial resolution – coarse is needed (would be needed for more heterogeneous sites)
  Don’t need a high angular resolution – smooth, avoiding specific features
  Spectral coverage – TBD but no obvious need for super-spectral
    Some bands are needed to anchor
    The interband approach can be used to extend to the whole spectrum
  3MI (and similar sensors) = good candidate to provide such references
    To be tested
    Early morning orbit, but the fitted model could allow extrapolation
    Could be combined with other polarimeters
Tilstra et al. 2003
Sciamachy

## Slide 12: Vicarious Technics – Rayleigh Scattering
Rayleigh Scattering
  Obvious potential – can be mostly fully polarised
  Type: strongly polarised (>60%)
  Accurate RTM calculation needed
    Effects of secondary terms are reduced (oceanic surface, aerosol)
  Examples :
    Adjustment of the MODIS correction
    GOME-2
Jafariserajehlou et al., 2020
see also Tilstra et al., 2014
Meister et al. 2014
MODIS
GOME-2

## Slide 13: Vicarious Technics - Sunglint
Sunglint
  Obvious potential – can be mostly fully polarised
  Type: strongly polarised (> 60%)
  Accurate RTM calculation needed
    Effects of secondary terms are reduced (oceanic surface, aerosol)
    Reduced sensitivity to the knowledge of the wind speed
  Interband in polarisation for the reflective domain
  Absolute polarisation also accessible
  Examples :
    POLDER-1
    PARASOL
Toubbé et al., 1999
Djellali et al., 2021
PARASOL
POLDER-1

## Slide 14: Vicarious Technics - Clouds
Ice Clouds
  Obvious potential – can be mostly fully polarised
  Type: very low (< 5%) in backscattering
  Selection of Ice clouds in backscattering domain
    Modelling can be used to extend the geometrical domain
  Checking the polarisation
  Examples :
    PARASOL
Fougnie et al., 2007
Riedi et al. 2010
PARASOL

## Slide 15: Vicarious Technics – Lunar calibration
Moon and Lunar surface
  Well known calibration target
  Type: Moderated (0-15%)
  Integrated disk or ROIs
    Historical measurements
    Potential for polarisation with the advantage of lunar
  Moon acquisitions are already a baseline
    Extension to polarisation would be a minimum cost
    The interband approach can be used to extend to the whole spectrum
  Example:
    S-GLI acquisitions
Dolphus, 1971

## Slide 16: Vicarious Technics – Simultaneous Observations
Simultaneous acquisitions (including SNO, but not only)
  Type: Various / All
  Example of polarisation sensitivity in-flight assessment:
    MODIS-Aqua (imager) using PARASOL (polarimeter) over marine stratocumulus clouds
      Limitation (and needed modelling) because of the difference in acquisition time and so geometry
    EPS-SG/VII (imager) using 3MI (polarimeter)
      Quasi-similar geometry with massive bins of matchups (same platform)
      multiple type of source, level of polarisation and orientation of polarisation (characterised by 3MI)
      Similar to a Lab measurements
    VIIRS/CLARREO
Phillips & Fougnie, 2024
McBride et al., 2023
VII
MODIS

## Slide 17: Vicarious Technics – Statistical
Behaviour of the polarisation: identify bias and quantify performance
  Type: Various / All
  Distribution of the polarisation angle
    Expected to be distributed around 90°
  Distribution of the polarisation around scattering plane
    Expected to be U distributed around 0
Schutgens et al., 2004
Goldin et al., 2023
Polarisation Angle
U component
POLDER-1
PARASOL

## Slide 18: Summary and way forward
Very High demand involving all GSICS agencies
EUMETSAT Workshop with targeted experts
  Exhaustive brainstorming on in-flight approaches & their performances
  3 needs:
    Evaluation of performance (commissioning)
    Monitoring
    Inter-calibration assessment
  Outcomes: recommendation for implementation and developments
GSICS: structure the interaction within a VISNIR sub-group?
  Discuss a set of common references or methodologies
  RTM, PICS reference BPDF, lunar polarisation model….
  Moving toward inter-calibration of the polarisation
    Special role for polariser equipped with on-board polarisation calibration systems
  Later: identify if some approaches can be implemented as GSICS references for operational missions

## Slide 19: References
Djellali, M. S., J. Riedi, S. Marcq, B. Fougnie, S. Hioki, and J.M. Nicolas, “Development of calibration methods using specular reflection over the ocean for the Multiviewing, Multichannel, Multipolarization Imager (3MI) of the EUMETSAT Polar System - Second Generation (EPS-SG),” SPIE Optical Engineering, January, 2019.
Toubbé, B., T. Bailleul, J. L. Deuzé, P. Goloub, O. Hagolle, and M. Herman, “In-flight calibration of the POLDER polarized channels using the sun’s glitter,” IEEE Trans. Geosci. Remote Sens. 37, 513–525, 1999.
Fougnie, B., G. Bracco, B. Lafrance, C. Ruffel, O. Hagolle, and C. Tinel, “PARASOL In-flight Calibration and Performance”, Applied Optics, vol. 46, n° 22, pp. 5435-5451, 2007.
Jafariserajehlou, S., B. Fougnie, “EPS/GOME-2 PMD Radiometric Adjustment over Rayleigh Scattering”, GSICS Annual Meeting, Virtual, 2021.
Tilstra, L. G., R. Lang, R. Munro, I. Aben, P. Stammes, “Contiguous polarisation spectra of the Earth from 300 to 850 nm measured by GOME-2 on-board MetOp-A”, Atmos. Meas. Tech., 7, 2047–2059, 2014.
Dolphus, A., E; Bowell, “Polarimetric Properties of the Lunar Surface and its Interpretation”, Astron. & Astrophys., 10, 29-53, 1971.
Phillips, P., and B. Fougnie, “In-orbit monitoring of the EUMETSAT Polar System - Second Generation (EPS-SG) Visible/Infrared Imager (METimage) Polarisation Sensitivity using the Multi-View, Multi-Channel, Multi-Polarisation Imager (3MI)”, SPIE Europe, Edinburg, 2024.
Schutgens, N. A. J., L. G. Tilstra, P. Stamnes, and F. M. Bréon, “On the relationship between Stokes parameters Q and U of atmospheric ultravioletvisiblenear-infrared radiation,” J. Geophys. Res. 109, 2004.
Meister, G., R. E. Eplee and B. A. Franz, "Corrections to MODIS Terra calibration and polarization trending derived from ocean color products", Proc. Earth Observing Syst. XIX, vol. 9218, Oct. 2014.
Goldin, D., B. Rajendra, S. Yolanda, “Evaluation of systematic errors on polarization parameters from POLDER instrument data for use in CLARREO Pathfinder-VIIRS intercalibration”, J. Applied Remote Sensing, Vol. 17, 2023.
Riedi, J., B. Marchant, S. Platnick, B. A. Baum, F. Thieuleux, C. Oudard, F. Parol, J.-M. Nicolas, and P. Dubuisson, “Cloud thermodynamic phase inferred from merged POLDER and MODIS data”, Atmos. Chem. Phys., vol. 10, 11851–11865, 2010
Tilstra, L., J. Acarreta, J.M. Krijger, P. Stammes, “Verification of SCIAMACHY‘s Polarisation Correction Over the Sahara Desert”, ENVISAT Validation Workshop (ESA SP-531). 9-13 December, Frascati, Italy, 2003
McBride, B. A., X. Xiong, A. Wu, “Assessment of polarization sensitivity of Aqua MODIS using co-incident POLDER-3 polarized measurements over marine stratocumulus clouds”, Earth Observing Systems XXVII, vol. 12232, 2022